## Slide 1: INTRODUCTION TO LOGIC DESIGN Chapter 2 Boolean Algebra and Logic Gates
gürtaçyemişçioğlu

## Slide 2: OUTLINE OF CHAPTER 1
Basic
Definition
Axiomatic Definition
of Boolean Algebra
Boolean
Functions
Canonical and
Standard Forms
Other Logic
Operations
Digital Logic
Gates
Integrated
Circuits
Basic Theorems
and Properties of
Boolean Algebra

## Slide 3: 2.1 Basic definitions

## Slide 4: BASIC DEFINITIONS
What is an algebra?
  Mathematical system consisting of
    Set of elements
    Set of operators
    Axioms or postulates
Why is it important?
  Defines rules of “calculations”

## Slide 5: BASIC DEFINITIONS
Example: arithmetic on natural numbers
  Set of elements: N = {1,2,3,4,…}
  Operator: +, –, *
  Axioms: associativity, distributivity, closure, identity elements, etc.
Note: operators with two inputs are called binary
  Does not mean they are restricted to binary numbers!
  Operator(s) with one input are called unary

## Slide 6: BASIC DEFINITION
A set is collection of having the same property.
  S : set, x and y : element or event
  For example: S = {1, 2, 3, 4}
    If x = 2, then xÎS.
    If y = 5, then y S.

## Slide 7: BASIC DEFINITIONS
A binary operator defines on a set S of elements is a rule that assigns, to each pair of elements from S, a unique element from S.
  For example: given a set S, consider x*y = z.
    * is a binary operator.
  If (x, y) through * get z and x, y, zÎS, then
    * is a binary operator of S.
  if * is not a binary operator of S and x, yÎS, then
    z  S.

## Slide 8: BASIC DEFINITION
Closure. A set S is closed with respect to a binary operator if,
  For every pair of elements of S, the binary operator specifies a rule for obtaining a unique element of S.
  For example, natural numbers N={1,2,3,...} is closed with respect to the binary operator + by the rule of arithmetic addition, since, for any x, yÎN, there is a unique zÎN such that
    x + y = z
  But operator – is not closed for N, because 2-3 = -1 and 2, 3ÎN, but
    (-1)N.
The most common postulates used to formulate various algebraic structures are as follows:

## Slide 9: BASIC DEFINITIONS
Associative law. A binary operator * on a set S is said to be associative whenever
  (x * y) * z = x * (y * z) for all x, y, zÎS
    (x+y)+z = x+(y+z)
Commutative law. A binary operator * on a set S is said to be commutative whenever
  x * y = y * x for all x, yÎS
    x+y = y+x

## Slide 10: BASIC DEFINITIONS
Identity element. A set S is said to have an identity element with respect to a binary operation * on S if there exists an element eÎS with the property that
  e * x = x * e = x for every xÎS
    0 + x = x + 0 = x for every xÎI. I = {…, -3, -2, -1, 0, 1, 2, 3, …}.
    1 * x = x * 1 = x for every xÎI. I = {…, -3, -2, -1, 0, 1, 2, 3, …}.

## Slide 11: BASIC DEFINITION
Inverse. A set S is having the identity element e with respect to the binary operator to have an inverse whenever, for every xÎS, there exists an element yÎS such that
  x * y = e
    In the set of integers, I, the operator + over I with e = 0, the inverse of an element x is (-x) since x+(-x) = 0.

## Slide 12: BASIC DEFINITION
Distributive law. If * and ．are two binary operators on a set S, * is said to be distributive over ． whenever
  x * (y．z) = (x * y)．(x * z)

## Slide 13: BASIC DEFINITION
The field of real numbers is the basis for arithmetic and ordinary algebra. The operators and postulates have the following meanings:
  The binary operator + defines addition.
  The additive identity is 0.
  The additive inverse defines subtraction.
  The binary operator ．defines multiplication.
  The multiplicative identity is 1.
  The multiplicative inverse of x = 1/x defines division, i.e., x ．1/x = 1.
  The only distributive law applicable is that of ． over +:
    x ．(y+z) = (x ． y) + (x ． z)

## Slide 14: 2.2 Axiomatic definition of boolean algebra

## Slide 15: AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA
We need to define algebra for binary values
  Developed by George Boole in 1854
Huntington postulates for Boolean algebra (1904):
B = {0, 1} and two binary operations, + and．
  Closure with respect to operator + and operator ·
  Identity element 0 for operator + and 1 for operator ·
  Commutativity with respect to + and ·
    x+y = y+x, x·y = y·x

## Slide 16: AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA
  Distributivity of · over +, and + over ·
    x·(y+z) = (x·y)+(x·z) and x+(y·z) = (x+y)·(x+z)
  Complement for every element x is x’ with x+x’=1, x·x’=0
  There are at least two elements x,yB such that xy
Terminology:
  Literal: A variable or its complement
  Product term: literals connected by •
  Sum term: literals connected by +

## Slide 17: AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA
A two- valued Boolean algebra is defined:
  on a set of two elements, B = {0,1},
  with rules for the two binary operators + and •
  The rules of operations: AND、OR and NOT
AND
OR
NOT
X
Y
X Y
0
0
0
0
1
0
1
0
0
1
1
1
X
Y
X + Y
0
0
0
0
1
1
1
0
1
1
1
1
X
1
0
0
1

## Slide 18: AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA
Huntington postulates for the set B = {0,1} and the two binary operators defined before.
Closure law
  1,0B
Identity laws
  0 for + and 1 for ·
Commutative laws
  x+y = y+x, x·y = y·x
Distributive laws
  x· (y+z) = (x·y) + (x · z)

## Slide 19: AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA
x | y | z | y + z | x · (y + z) | x · y | x · z | (x · y) + (x · z)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Distributive laws

## Slide 20: AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA
Complement
  x+x‘ = 1 → 0+0‘ = 0+1 = 1; 1+1‘ = 1+0 = 1
Has two distinct elements
  1 and 0, with 0 ≠ 1
Note
  A set of two elements
  + : OR operation; ．: AND operation
  A complement operator: NOT operation
  Binary logic is a two-valued Boolean algebra

## Slide 21: 2.3 Basic theorems and properties of boolean algebra

## Slide 22: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Duality Principle says that:
  if an expression is valid in Boolean algebra, then
  the dual of that expression is also valid.
To form the dual of an expression:
  replace all + operators with · operators,
  all · operators with + operators,
  all 1’s with 0’s, and all 0’s with 1’s.

## Slide 23: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Form the dual of the expression
  x + (yz) = (x + y)(x + z)
Following the replacement rules…
  x(y + z) = xy + xz
Take care not to alter the location of the parentheses if they are present.

## Slide 24: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Postulates and Theorems of Boolean Algebra |  | 
Postulate 2, identity | (a) x + 0 = x | (b) x · 1 = x
Postulate 5, complementarity | (a) x + x’ = 1 | (b) x · x’ = 0
Theorem 1, idempotent | (a) x + x = x | (b) x · x = x
Theorem 2, involution | (a) x + 1 = 1 | (b) x · 0 = 0
Theorem 3, involution | (x’)’ = x | 
Postulate 3, commutative | (a) x + y = y + x | (b) xy = yx
Theorem 4, associative | (a) x + (y + z) = (x + y) + z | (b) x(yz) = (xy)z
Postulate 4, distributive | (a) x (y + z) = xy + xz | (b) x + yz = (x + y) (x + z)
Theorem 5, DeMorgan | (a) (x + y)’ = x’ y’ | (b) (xy)’ = x’ + y’
Theorem 6, absorption | (a) x + xy = x | (b) x(x+y) = x

## Slide 25: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Need more rules to modify algebraic expressions
  Theorems that are derived from postulates
What is a theorem?
  A formula or statement that is derived from postulates (or other proven theorems)
Basic theorems of Boolean algebra
  Theorem 1 (a): x + x = x (b): x · x = x
  Looks straightforward, but needs to be proven!

## Slide 26: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Theorem 1 (a) show that x+x = x.
x+x = (x+x) ·1 by 2(b)
  = (x+x)(x+x’) by 5(a)
  = x+xx’ by 4(b)
  = x+0 by 5(b)
  = x by 2(a)
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
We can now use Theorem 1(a) in future proofs

## Slide 27: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Theorem 1 (b) show that x·x = x.
x·x = xx+0 by 2(a)
  = xx+xx’ by 5(b)
  = x(x+x’) by 4(a)
  = x·1 by 5(a)
  = x by 2(b)
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 1: (a) x+x=x,

## Slide 28: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Theorem 2 (a) show that x+1 = 1.
x + 1 = 1．(x + 1) by 2(b)
  =(x + x')(x + 1) by 5(a)
  = x + x' 1 by 4(b)
  = x + x' by 2(b)
  = 1 by 5(a)
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 1: (a) x+x=x, (b) x.x=x

## Slide 29: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Theorem 2(b): x．0 = 0 by duality
Theorem 3: (x')' = x
  Postulate 5 defines the complement of x,
    x + x' = 1
    x ． x' = 0
  The complement of x' is x is also (x')'
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 1: (a) x+x=x, (b) x.x=x
Th. 2: (a) x+1=1

## Slide 30: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Absorption Property (Covering) Theorem 6(a): x + xy = x
x + xy = x．1 + xy by 2(b)
  = x (1 + y) by 4(a)
  = x (y + 1) by 3(a)
  = x．1 by Th. 2(a)
  = x by 2(b)
Theorem 6(b): x (x + y) = x by duality
By means of truth table (another way to proof )
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 1: (a) x+x=x, (b) x·x=x
Th. 2: (a) x+1=1, (b) x·0=0
x | y | xy | x+xy
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 1

## Slide 31: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
x | y | x’ | y’ | x+y | (x+y)’ | x’y’ | xy | x’+y’ | (xy)’
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
DeMorgan’s Theorem
Theorem 5(a): (x + y)’ = x’y’
Theorem 5(b): (xy)’ = x’ + y’
By means of truth table

## Slide 32: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
Consensus Theorem
xy + x’z + yz = xy + x’z
(x + y) • (x’ + z) • (y + z) = (x + y) • (x’ + z) -- (dual)
Proof: xy + x’z + yz = xy + x’z + (x + x’) yz = xy + x’z + xyz + x’yz = (xy + xyz) + (x’z + x’zy) = xy + x’z

## Slide 33: BASIC THEOREMS AND PROPERTIES OF BOOLEAN ALGEBRA
The operator precedence for evaluating Boolean Expression is
  Parentheses
  NOT
  AND
  OR
Examples
  x y' + z
  (x y + z)'

## Slide 34: 2.4 Boolean functions

## Slide 35: BOOLEAN FUNCTIONS
A Boolean function consists of:
  Binary variables
  Binary operators OR and AND
  Unary operator NOT
  Parentheses
  The constants 0 and 1
Examples
  F1= x y z'
  F2 = x + y'z
  F3 = x' y' z + x' y z + x y'
  F4 = x y' + x' z

## Slide 36: BOOLEAN FUNCTIONS
For a given value of the binary variables, the function can be equal to either 1 or 0.
Consider as an example the following Boolean function:
  F1 = x + y’ z
  The function F1 = 1, if x = 1 OR if y’ = 1 and z = 1.
  F1 = 0 otherwise.
The complement operation dictates that when y’ = 1 then y = 0.
Therefore, we can say that
  F1 = 1 if x = 1 OR if y = 0 and z = 1.

## Slide 37: BOOLEAN FUNCTIONS
A Boolean function expresses the logical relationship between binary variables.
It is evaluated by determining the binary value of the expression for all possible values of the variables.
A Boolean function can be represented in a truth table.

## Slide 38: BOOLEAN FUNCTIONS
The truth table of 2n entries
F1= x y z‘, F2 = x + y'z, F3 = x' y' z + x' y z + x y‘, F4 = x y' + x' z
  Two Boolean expressions may specify the same function F3 = F4
x | y | z | x’ | y’ | z’ | y’z | x’y’z | x’yz | xy’ | x’z | F1 | F2 | F3 | F4
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 39: BOOLEAN FUNCTION
Implementation with logic gates
F4 is more economical

## Slide 40: BOOLEAN FUNCTION
Algebraic Manipulation
When a Boolean expression is implemented with logic gates,
  Each term requires a gate
  Each variable within the term designates an input to the gate
  Literal is a single variable within a term that may be complemented or not.

## Slide 41: BOOLEAN FUNCTION
Example:
  F1= x y z‘ 1 term and 3 literals
  F2 = x + y'z 2 terms and 3 literals
  F3 = x' y' z + x' y z + x y‘ 3 terms and 8 literals
  F4 = x y' + x' z 2 terms and 4 literals
Manipulation of Boolean algebra consists mostly of reducing an expression by reducing the number of terms, the number of literals, or both in a Boolean expression, it is often possible to obtain a simpler, less area, cheaper circuit.

## Slide 42: BOOLEAN FUNCTION
x(x’+y)
  = (x x’) + (x y) by post (4a)
  = 0 + x y by post (5b)
  = x y by post (2a)
x+x’y
  = (x + x’) (x + y) by post (4b)
  = 1 (x + y) by post (5a)
  = x + y by post (2b)
(x + y) (x + y’)
  = x + y y’ post (4b)
  = x + 0 post (5b)
  = x post (2a)
(x + y) (x’ + z) (y + z) = (x + y) (x’ + z)
  consesus theorem with duality.
Simplify the following functions to a minimum number of literals.

## Slide 43: BOOLEAN FUNCTION
x y + x’ z + y z
  = x y + x’ z + 1 y z
  = x y + x’ z + (x + x’) y z post (5a)
  = x y + x’ z + x y z + x’ y z post (4a)
  = x y + x y z + x’ z + x’ y z post (3a)
  = x y (1 + z) + x’z (1 + y) post (4a)
  = x y 1 + x’ z 1 Theo(2a)
  = x y + x’ z post (2b)
Simplify the following functions to a minimum number of literals.

## Slide 44: BOOLEAN FUNCTION
The complement of a function F is F’ and is obtained from
  An interchange of 0’s for 1’s and 1’s for 0’s in the value of F.
The complement of a function may be derived algebraically through De Morgan’s theorem.
  De Morgan’s theorem can be extended to three or more variables.

## Slide 45: BOOLEAN FUNCTION
(A + B + C)’ = (A + x)’ let B + C = x
  = A’ x’ by theorem (5a) De Morgan
  = A’ (B + C)’ substitute B+C = x
  = A’ (B’ C’) by theorem (5a) De Morgan
  = A’ B’ C’ by theorem (4b) (associative)

## Slide 46: BOOLEAN FUNCTION
Generalizations:
  Function is obtained by interchanging AND and OR operators and complementing each literal.
    (A+B+C+D+ ... +F)' = A'B'C'D'... F'
    (ABCD ... F)' = A'+ B'+C'+D' ... +F'

## Slide 47: BOOLEAN FUNCTION
F1’ = (x‘ y z' + x‘ y‘ z)' .
= (x’ y z’)’ (x’ y’ z)’
= ( x + y’ + z) (x + y + z’)
F2’ = x (y’ z' + y z).
= [x(y’ z’ + y z)]’
= x’ + (y’ z’ + y z)’
= x + (y’ z’)’ (y z)’
= x’ (y+ z) (y’ + z’)
Find the complement of the function F1 by applying De Morgan’s theorem as many times as necessary

## Slide 48: BOOLEAN FUNCTION
Simpler procedure:
  Take the dual of the function and complement each literal
Find the complement of the function F1
  F1 = (x‘ y z' + x‘ y‘ z)' .
  = (x’ y z’)’ (x’ y’ z)’
  The dual of F1 = (x’ + y + z’) (x’ + y’ z).
  Complement each literal = (x + y’ + z) (x + y + z’) = F1'

## Slide 49: BOOLEAN FUNCTION
Find the complement of the function F2
  F2 = x (y’ z' + y z).
  = x (y’ z’) + (y z)
  The dual of F2 = x + (y’ + z’) (y + z)
  Complement each literal = x’ + (y + z) (y’ + z’) = F2'

## Slide 50: 2.5 Canonical and standard forms

## Slide 51: CANONICAL AND STANDARD FORMS
A binary variable may appear either in its normal for (x) or in its complement form (x’).
Consider :
  x AND y.
Each variable may appear in either form, there are four possible combinations:
  x’ y’
  x’ y
  x y’
  x y
Each of these four AND term is called a minterm or a standard product.
n variables can be combined to form 2n minterms.

## Slide 52: CANONICAL AND STANDARD FORMS
In a similar fashion,
  n variables forming and OR term,
  with each variable being primed or unprimed,
  provide 2n possible combinations,
  called maxterms or standard sums.
  Each maxterm is the complement of its corresponding minterm, and vice versa.

## Slide 53: CANONICAL AND STANDARD FORMS
 |  |  | Minterms |  | Maxterms | 
x | y | z | Term | Designation | Term | Designation
0 | 0 | 0 | x’ y’ z’ | m0 | x + y + z | M0
0 | 0 | 1 | x’ y’ z | m1 | x + y + z’ | M1
0 | 1 | 0 | x’ y z’ | m2 | x + y’ + z | M2
0 | 1 | 1 | x’ y z | m3 | x + y’ + z’ | M3
1 | 0 | 0 | x y’ z’ | m4 | x’ + y + z | M4
1 | 0 | 1 | x y’ z | m5 | x’ + y + z’ | M5
1 | 1 | 0 | x y z’ | m6 | x’ + y’ + z | M6
1 | 1 | 1 | x y z | m7 | x’ + y’ + z’ | M7

## Slide 54: CANONICAL AND STANDARD FORMS
A Boolean function can be expressed algebraically by
  A truth table
  Sum of minterms
  Each of these minterms results in f1 = 1.

## Slide 55: CANONICAL AND STANDARD FORMS
x | y | z | f1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
x’y’z
xy’z’
xyz
  f1 =
x'y'z
+ xyz
+ xy'z'
  = m1 + m4 +m7 (Minterms)

## Slide 56: CANONICAL AND STANDARD FORMS
x | y | z | f2
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
x’yz
xy’z
xyz
  f2 =
x'yz
+ xyz
+ xy'z
  = m3 + m5 +m6 + m7 (Minterms)
xyz’
+ xyz'

## Slide 57: CANONICAL AND STANDARD FORMS
These examples demonstrate an important property of Boolean algebra:
  Any Boolean function can be expressed as a sum (ORing) of minterms.
Consider the complement of a Boolean function.
  From the truth table
    A minterm for each combination that produces a 0
    Then ORing those terms.

## Slide 58: CANONICAL AND STANDARD FORMS
The complement of f1:
  f1' = m0 + m2 +m3 + m5 + m6
  = x‘ y‘ z‘ + x‘ y z‘ + x‘ y z + x y‘ z + x y z‘
  If we take the complement of f1‘ , then we obtain f1
  (f1‘)’ = (x‘ y‘ z‘ + x‘ y z‘ + x‘ y z + x y‘ z + x y z‘)’
  f1= (x + y + z) (x + y’ + z) (x + y’ + z’) (x’ + y’ + z)
  = M0 M2 M3 M5 M6
x | y | z | f1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 59: CANONICAL AND STANDARD FORMS
The complement of f2:
  f2' = m0 + m1 +m2 + m4
  = x‘ y‘ z‘ + x‘ y’ z + x‘ y z’ + x y‘ z’
  If we take the complement of f2‘ , then we obtain f2
  (f2‘)’ = (x‘ y‘ z‘ + x‘ y’ z + x‘ y z’ + x y‘ z’)’
  f2= (x + y + z) (x + y + z’) (x + y’ + z) (x’ + y+ z)
  = M0 M1 M2 M4
x | y | z | f2
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 60: CANONICAL AND STANDARD FORMS
These examples demonstrate a second property of Boolean algebra:
  Any Boolean function can be expressed as a product of (ANDing) of maxterms.
Consider the complement of a Boolean function.
  From the truth table
    A maxterm for each combination that produces a 0
    Then ANDing those terms.
Boolean functions expressed as a sum of minterms or product of maxterms are said to be in canonical form.

## Slide 61: CANONICAL AND STANDARD FORMS
Sum of minterms:
  There are 2n minterms and
  22n combinations of function with n Boolean variables.
  It is sometimes convenient to express the Boolean function in its sum of minterms form.
  If not in this form, it can be made so by first expanding the expression into a sum of AND terms.
  Each term is then inspected to see if it contains all the variables.
  If it misses one or more variables, it is ANDed with an expression such as x + x’, where x is one of the missing variables.

## Slide 62: CANONICAL AND STANDARD FORMS
Example: express F = A+B’C in a sum of minterms.
  Step1: A is missing two variable B and C!
  1st include B
  A = A (B + B’)
  = AB + AB’
  2nd include C
  A = AB (C + C’) + AB’ (C+C’)
  = ABC + ABC’ + AB’C + AB’C’

## Slide 63: CANONICAL AND STANDARD FORMS
  Step2: B’C is missing one variable A!
  Include A
  B’C = B’C (A + A’)
  = AB’C + A’B’C
  Step3: Combine all terms
  F = ABC + ABC’ + AB’C + AB’C’ + AB’C + A’B’C
    according to Theorem 1 (x + x = x),
    it is possible to remove one of them
  F = ABC + ABC’ + AB’C’ + AB’C + A’B’C = m1 + m4 + m5 + m6 + m7

## Slide 64: CANONICAL AND STANDARD FORMS
  F =
  = m1 + m4 + m5 + m6 + m7
When in its sum of minterms the Boolean function can be expressed as:
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
ABC
+ ABC’
+ AB’C’
+ AB’C
+ A’B’C

## Slide 65: CANONICAL AND STANDARD FORMS
Product of maxterms:
  22n functions of n binary variables can be also expressed as product of maxterms.
  To express the Boolean functions as a product of maxterms
    It must first be brought into a form of OR terms.
  This may be done by using the distributive law, x + yz = (x +y) (x + z).
  Then any missing variable x in each OR term is ORed with x x’.

## Slide 66: CANONICAL AND STANDARD FORMS
Example: express F = x y + x’ z in a product of maxterm.
Step1: using distributive law
  = (xy + x’) (xy + z)
Step2: using distributive law
  = (x + x’) (y + x’) (x + z) (y + z)
  = 1 (x’ + y) (x + z) (y + z)
  = (x’ + y) (x + z) (y + z)

## Slide 67: CANONICAL AND STANDARD FORMS
  = (x’ + y) (x + z) (y + z)
Function has three variables x, y and z. Each OR term is missing one variable.
  (x’ + y) = x’ + y + z z’ = (x’ + y + z) (x’ + y + z’)
  (x + z) = x + z + y y’ = (x + y + z) (x + y’ +z)
  (y + z) = y + z + x x’ = (x + y + z) (x’ + y + z)
Combine all the terms and remove the ones that appear twice
  F = (x + y + z) (x + y’ + z) (x’ + y + z) (x’ + y + z’)

## Slide 68: CANONICAL AND STANDARD FORMS
  F =
  = M0 M2 M4 M5
Convenient way to express this function is:
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
x’yz’
+ x’yz
+ xy’z
+ xyz

## Slide 69: CANONICAL AND STANDARD FORMS
The complement of a function expressed as:
  The sum of minterms = the sum of minterms missing from the original function
  Because the original function is expressed by those minterms that make the function equal to 1, where its complement is 0.
  Example:
    = m0 + m2 + m3

## Slide 70: CANONICAL AND STANDARD FORMS
Example:
  Thus = m0 + m2 + m3
  Complement of F’ by DeMorgan’s theorem
    F = (m0 + m2 + m3)’ = m0’ m2’ m3’ = M0 M2 M3 =
  m0’ = Mj

## Slide 71: CANONICAL AND STANDARD FORMS
Sum of minterms = product of maxterms
Interchange the symbols S and P and list those numbers missing from the original form
    S of 1's
    P of 0's

## Slide 72: CANONICAL AND STANDARD FORMS
Example: F = x y + x’ z
  x y = x y (z + z’) = x y z + x y z’
  x’z = x’z (y + y’) = x’ y z + x’ y’ z
  F = x y z + x y z’ + x’ y z + x’ y’ z
    with 1’s
    with 0’s
x | y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 73: CANONICAL AND STANDARD FORMS
The two canonical forms of Boolean algebra are basic forms that one obtains from reading a function from the truth table.
These forms are very seldom the ones with the least number of literals, because each minterm or maxterm must contain, by definition, all the variables either complemented or uncomplemented.
Standard form, the terms that form the function may contain one, two, or any number of literals.
  Sum of products and products of sum

## Slide 74: CANONICAL AND STANDARD FORMS
Sum of products
  Contains AND terms (product terms) of one or more literals each.
  The sum denotes the ORing of these terms.
  Example:
    F1 = y’ + x y + x’ y z’
      3 product terms of one, two and three literals.
      Their sum is in effect an OR operation.

## Slide 75: CANONICAL AND STANDARD FORMS
F1 = y’ + x y + x’ y z’
Logic diagram of sum-of-products
  Each product term requires and AND gate except for a term with a single literal.
  The logic sum is formed with an OR gate.

## Slide 76: CANONICAL AND STANDARD FORMS
Product of sums
  Contains OR terms (sum terms) of one or more literals each.
  The product denotes the ANDing of these terms.
  Example:
    F2 = x (y’ + z) (x’ + y + z’)
      3 sum terms of one, two and three literals.
      Their product is in effect an AND operation.

## Slide 77: CANONICAL AND STANDARD FORMS
F2 = x (y’ + z) (x’ + y + z’)
Logic diagram of product of sums
  Each product term requires and AND gate except for a term with a single literal.
  The logic sum is formed with an OR gate.

## Slide 78: CANONICAL AND STANDARD FORMS
Multi-level implementation
  F3 = AB + C (D + E)
  Neither in sum of products nor in products of sums.

## Slide 79: CANONICAL AND STANDARD FORMS
Change it to a standard form by using the distributive law
  F3 = AB + C (D + E) = AB + CD + CE

## Slide 80: 2.6 other logic operations

## Slide 81: OTHER LOGIC OPERATIONS
2n rows in the truth table of n binary variables.
22n functions for n binary variables.
n = 2, and the number of possible Boolean functions is 16.
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1

## Slide 82: OTHER LOGIC OPERATIONS
Boolean Functions | Operator Symbol | Name | Comments
F0 = 0 |  | Null | Binary Constant 0
F1 = x y |  | AND | x and y
F2 = x y’ | x / y | Inhibition | x, but not y
F3 = x |  | Transfer | x’
F4 = x’ y | y / x | Inhibition | y, but not x
F5 = y |  | Transfer | y
F6 = x y’ + x’ y | x ⊕ y | Exclusive-OR | x or y, but not both
F7 = x + y | x + y | OR | x or y
F8 = (x + y)’ | x  y | NOR | NOT- OR
F9 = (x y + x’ y’) | (x ⊕ y) ‘ | Equivalence | x equals y
F10 = y’ | y’ | Complement | NOT y
F11 = x + y’ | x ⊂ y | Implication | If y, then x
F12 = x’ | x’ | Complement | NOT x
F13 = x’ + y | x ⊃ y | Implication | If x, then y
F14 = (xy)’ | x  y | NAND | NOT- AND
F15 = 1 |  | Identity | Binary constant 1
Boolean Functions | Operator Symbol | Name | Comments
F0 = 0 |  | Null | Binary Constant 0
F1 = x y |  | AND | x and y
F2 = x y’ | x / y | Inhibition | x, but not y
F3 = x |  | Transfer | x’
F4 = x’ y | y / x | Inhibition | y, but not x
F5 = y |  | Transfer | y
F6 = x y’ + x’ y | x ⊕ y | Exclusive-OR | x or y, but not both
F7 = x + y | x + y | OR | x or y
F8 = (x + y)’ | x  y | NOR | NOT- OR
F9 = (x y + x’ y’) | (x ⊕ y) ‘ | Equivalence | x equals y
F10 = y’ | y’ | Complement | NOT y
F11 = x + y’ | x ⊂ y | Implication | If y, then x
F12 = x’ | x’ | Complement | NOT x
F13 = x’ + y | x ⊃ y | Implication | If x, then y
F14 = (xy)’ | x  y | NAND | NOT- AND
F15 = 1 |  | Identity | Binary constant 1

## Slide 83: OTHER LOGIC OPERATIONS
The functions are determined from the 16 binary combinations that can be assigned to F.
The 16 functions can be expressed algebraically by means of Boolean functions.
The Boolean expressions listed are simplified to their minimum number of literals.
All the new symbols shown, except for the exclusive-OR symbol ⊕ are not in common use by digital designers.

## Slide 84: 2.7 digital logic gates

## Slide 85: DIGITAL LOGIC GATES
Boolean expression: AND, OR and NOT operations
Constructing gates of other logic operations
  The feasibility and economy;
  The possibility of extending gate's inputs;
  The basic properties of the binary operations (commutative and associative);
  The ability of the gate to implement Boolean functions.

## Slide 86: DIGITAL LOGIC GATES
Consider the 16 functions in Table (slide 82)
  Two are equal to a constant (F0 and F15).
  Four are repeated twice (F4, F5, F10 and F11).
  Inhibition (F2) and implication (F13) are not commutative or associative.
  The other eight: complement (F12), transfer (F3), AND (F1), OR (F7), NAND (F14), NOR (F8), XOR (F6), and equivalence (XNOR) (F9) are used as standard gates.
  Complement: inverter.
  Transfer: buffer (increasing drive strength).
  Equivalence: XNOR.

## Slide 87: DIGITAL LOGIC GATES
Name | Graphic Symbol | Algebraic Function | Truth Table |  |  | 
AND |  | F = x y | x | y |  | F
 |  |  | 0 | 0 |  | 0
 |  |  | 0 | 1 |  | 0
 |  |  | 1 | 0 |  | 0
 |  |  | 1 | 1 |  | 1
OR |  | F = x + y | x | y |  | F
 |  |  | 0 | 0 |  | 0
 |  |  | 0 | 1 |  | 1
 |  |  | 1 | 0 |  | 1
 |  |  | 1 | 1 |  | 1
INVERTER |  | F = x ’ | x |  | y | 
 |  |  | 0 |  | 1 | 
 |  |  | 1 |  | 0 | 

## Slide 88: DIGITAL LOGIC GATES
Name | Graphic Symbol | Algebraic Function | Truth Table |  |  | 
BUFFER |  | F = x | x |  | y | 
 |  |  | 0 |  | 0 | 
 |  |  | 1 |  | 1 | 
NAND |  | F = (x y) ’ | x | y |  | F
 |  |  | 0 | 0 |  | 1
 |  |  | 0 | 1 |  | 1
 |  |  | 1 | 0 |  | 1
 |  |  | 1 | 1 |  | 0
NOR |  | F = ( x + y) ‘ | x | y |  | F
 |  |  | 0 | 0 |  | 1
 |  |  | 0 | 1 |  | 0
 |  |  | 1 | 0 |  | 0
 |  |  | 1 | 1 |  | 0

## Slide 89: DIGITAL LOGIC GATES
Name | Graphic Symbol | Algebraic Function | Truth Table |  | 
XOR |  | F = x ⊕ y | x | y | F
 |  |  | 0 | 0 | 0
 |  |  | 0 | 1 | 1
 |  |  | 1 | 0 | 1
 |  |  | 1 | 1 | 0
XNOR |  | F = ( x ⊕ y ) ‘ | x | y | F
 |  |  | 0 | 0 | 1
 |  |  | 0 | 1 | 0
 |  |  | 1 | 0 | 0
 |  |  | 1 | 1 | 1

## Slide 90: DIGITAL LOGIC GATES
Extension to multiple inputs
  A gate can be extended to multiple inputs.
    If its binary operation is commutative and associative.
  AND and OR are commutative and associative.
    OR
      x + y = y + x
      (x + y) + z = x + (y + z) = x + y + z
    AND
      x y = y x
      (x y) z = x (y z) = x y z

## Slide 91: DIGITAL LOGIC GATES
The NAND and NOR functions are commutative, but they are not associative
  (x  y) z ≠ x (y  z)
    (x  y)  z = [ (x + y)’ + z]’
    = (x + y) z’ = x z’ + y z’
    x (y  z) = [ x + (y + z)‘ ]’
    = x‘ (y + z) = x’ y + x’ z

## Slide 92: DIGITAL LOGIC GATES
The NAND and NOR functions are commutative, and their gates can be extended to have more than two inputs, provided that the definition of the operation is slightly modified.
The difficulty is that the NAND and NOR operators are not associative
  (x  y) z ≠ x (y  z)
    (x  y)  z = [ (x + y) ’ + z] ’ = (x + y) z ’ = x z ’ + y z ’
    x (y  z) = [ x + (y + z) ‘ ]’ = x ‘ (y + z) = x ’ y + x ’ z
To overcome this;
  Define the multiple NOR (or NAND) gate as complemented OR (or AND) gate.
    x  y  z = (x + y + z) ’
    x  y  z = (x y z) ’

## Slide 93: DIGITAL LOGIC GATES
Multiple NOR = a complement of OR gate,
Multiple NAND = a complement of AND.
The cascaded NAND operations = sum of products.
The cascaded NOR operations = product of sums.

## Slide 94: DIGITAL LOGIC GATES
The XOR and XNOR gates are commutative and associative.
Multiple-input XOR gates are uncommon?
XOR is an odd function: it is equal to 1 if the inputs variables have an odd number of 1's.
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 95: DIGITAL LOGIC GATES
The binary signals at the inputs and outputs of any gate has one of two values, except during transition.
  One signal value represents logic-1
  The other logic-0.
Two signal values are assigned to two logic values
There exist two different assignments of signal level to logic value.

## Slide 96: DIGITAL LOGIC GATES
The higher signal level is designated by H and the lower signal level by L.
Choosing the high-level H to represent logic-1 defines a positive logic system.
Choosing the low-level L to represent logic-0 defines a negative logic system.

## Slide 97: DIGITAL LOGIC GATES
The physical behaviour of the gate when H is 3 volts and L is 0 volts.
Truth table of (c) assumes positive logic assignment, with H = 1 and L = 0.
x | y | F | 
L | L | L | 
L | H | L | 
H | L | L | 
H | H | H | 
(a) Truth table with H and L |  |  | (b) Gate block diagram
x | y | x | 
0 | 0 | 0 | 
0 | 1 | 0 | 
1 | 0 | 0 | 
1 | 1 | 1 | 
(c) Truth table for positive logic |  |  | (d) Positive logic AND gate

## Slide 98: DIGITAL LOGIC GATES
Truth table of (e) assumes positive logic assignment, with H = 0 and L = 1.
x | y | z | 
0 | 0 | 1 | 
0 | 1 | 1 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
(e) Truth table for negative logic |  |  | (f) Negative logic OR gate

## Slide 99: 2.8 integrated Circuits

## Slide 100: INTEGRATED CIRCUITS
Level of Integration
An IC (a chip)
Examples:
  Small-scale Integration (SSI): < 10 gates
  Medium-scale Integration (MSI): 10 ~ 100 gates
  Large-scale Integration (LSI): 100 ~ xk gates
  Very Large-scale Integration (VLSI): > xk gates

## Slide 101: INTEGRATED CIRCUITS
VLSI
  Small size (compact size)
  Low cost
  Low power consumption
  High reliability
  High speed

## Slide 102: INTEGRATED CIRCUITS
Digital logic families: circuit technology
  TTL: transistor-transistor logic (dying?)
  ECL: emitter-coupled logic (high speed, high power consumption)
  MOS: metal-oxide semiconductor (NMOS, high density)
  CMOS: complementary MOS (low power)
  BiCMOS: high speed, high density

## Slide 103: INTEGRATED CIRCUITS
The characteristics of digital logic families
  Fan-out: the number of standard loads that the output of a typical gate can drive.
  Power dissipation.
  Propagation delay: the average transition delay time for the signal to propagate from input to output.
  Noise margin: the minimum of external noise voltage that caused an undesirable change in the circuit output.

## Slide 104: INTEGRATED CIRCUITS
CAD – Computer-Aided Design
  Millions of transistors
  Computer-based representation and aid
  Automatic the design process
  Design entry
    Schematic capture
    HDL – Hardware Description Language
      Verilog, VHDL
  Simulation
  Physical realization
    ASIC, FPGA, PLD

## Slide 105: INTEGRATED CIRCUITS
Why is it better to have more gates on a single chip?
  Easier to build systems
  Lower power consumption
  Higher clock frequencies
What are the drawbacks of large circuits?
  Complex to design
  Chips have design constraints
  Hard to test

## Slide 106: INTEGRATED CIRCUITS
Need tools to help develop integrated circuits
  Computer Aided Design (CAD) tools
  Automate tedious steps of design process
  Hardware description language (HDL) describe circuits
  VHDL (see the lab) is one such system