## Slide 1: INTRODUCTION TO LOGIC DESIGN Chapter 5 Synchronous Sequential Logic
gürtaçyemişçioğlu

## Slide 2: OUTLINE OF CHAPTER 5
Sequential
Circuits
Latches
Analysis of
Clocked
Sequential Circuits
State Reduction
and Assignment
Design Procedure
Flip-flop

## Slide 3: 5.1 SEQUENTIAL circuits

## Slide 4: SEQUENTIAL CIRCUITS
Every digital system is likely to have combinational circuits.
Most systems encountered in practice also include storage elements, which require that the system be described in terms of sequential logic.
Combinational
Circuit
Memory Elements
Inputs
Outputs

## Slide 5: SEQUENTIAL CIRCUITS
The storage elements are devices capable of storing binary information.
The binary information stored in these elements at any given time defines the state of the sequential circuit at that time.
The sequential circuit receives binary information from external inputs.
These inputs, together with the present state of the storage elements, determine the binary value of the outputs.

## Slide 6: SEQUENTIAL CIRCUITS
They also determine the condition for changing the state in the storage elements.
A sequential circuit is specified by a time sequence of inputs, output, and internal states.

## Slide 7: SEQUENTIAL CIRCUITS
There are two main types of sequential circuits.
Their classification depends on the timing of their signals.
Sequential Circuit
Synchronous
Asynchronous

## Slide 8: SEQUENTIAL CIRCUITS
Asynchronous Sequential Circuit
  The behaviour of the circuit depends upon the input signals at any instant of time and the order in which the inputs change.
Combinational
Circuit
Memory Elements
Inputs
Outputs

## Slide 9: SEQUENTIAL CIRCUITS
Asynchronous Sequential Circuit
  In gate – type asynchronous systems, the storage elements consist of logic gates whose propagation delay provides the required storage.
  Thus, an asynchronous sequential circuit may be regarded as a combinational circuit with feedback.
  Because of the feedback among logic gates, an asynchronous sequential circuit may become unstable at times.

## Slide 10: SEQUENTIAL CIRCUITS
Synchronous Sequential Circuit
  The behaviour can be defined from the knowledge of its signals at discrete instants of time.
Combinational
Circuit
Flip-flops
Inputs
Outputs
Clock

## Slide 11: SEQUENTIAL CIRCUITS
Synchronous Sequential Circuit
  Employs signals that affect the storage elements only at discrete instants of time.
  Synchronisation is achieved by a timing device called a clock generator.
    Provides a periodic train of clock pulses.
    Clock pulses are distributed throughout the system in such a way that storage elements are affected only with the arrival of each pulse.

## Slide 12: SEQUENTIAL CIRCUITS
Synchronous Sequential Circuit
    In practice, the clock pulses are applied with other signals that specify the required change in the storage elements.
  Circuits that use clock pulses in the inputs of storage elements are called clocked sequential circuits.
  The storage elements used in clocked sequential circuits are called flip – flops.
  A flip – flop is a binary storage device capable of storing one bit of information.

## Slide 13: 5.2 latches

## Slide 14: LATCHES
Latches are the basic circuits from which all flip – flops are constructed.
Although latches are useful for storing binary information and for the design of asynchronous sequential circuits.
They are not practical for use in synchronous sequential circuits.

## Slide 15: LATCHES
S | R | Q | Q’
1 | 0 |  | 
0 | 0 |  | 
0 | 1 |  | 
0 | 0 |  | 
1 | 1 |  | 
SR Latch
1
0
0
1
Hold
State
Set State
Reset State
Hold
State
Invalid
State
0
1
0
1
0
0
1
0
1
0
0
1
0
0

## Slide 16: LATCHES
SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
S R | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid
Set
Reset
No change

## Slide 17: LATCHES
SR Latch with Control Input
C | S | R | Q
0 | X | X | HOLD
1 | 0 | 0 | HOLD
1 | 0 | 1 | Q = 0
1 | 1 | 0 | Q = 1
1 | 1 | 1 | Q = Q’
No change
No change
Reset
Set
Invalid

## Slide 18: LATCHES
D Latch (D = Data)
  One way to eliminate the undesirable condition of the indeterminate state in the SR latch is to ensure that inputs S and R are never equal to 1 at the same time.
  D latch has two inputs
    D (data) - directly goes to the S input and its complement is applied to the R input.
    C (control)

## Slide 19: LATCHES
D Latch (D = Data)
C | D | Q
0 | X | HOLD
1 | 0 | Q = 0
1 | 1 | Q = 1
No change
Reset
Set
C
Timing Diagram
D
Q
t
Output may change

## Slide 20: LATCHES
D Latch (D = Data)
C | D | Q
0 | X | HOLD
1 | 0 | Q = 0
1 | 1 | Q = 1
No change
Reset
Set
C
Timing Diagram
D
Q
Output may change

## Slide 21: LATCHES
D Latch (D = Data)
  The D latch has an ability to hold data in its internal storage.
  It is suited for use as a temporary storage for binary information.
  This circuit is often called transparent latch.
    The output follow changes in the data input as long as the control input is enabled.

## Slide 22: 5.3 FLIP – FLOPS

## Slide 23: FLIP – FLOPS
Flip – flops are constructed in such a way to make D latches operate properly when they are part of a sequential circuit that employs a common clock.
The problem with the latch is that
  It responds to a change in the level of a clock pulse.
    Positive level response in the control input allows changes, in the output when the D input changes while the control pulse stays at logic 1.
The key to the proper operation of a flip – flop is
  to trigger it only during a signal transition.

## Slide 24: FLIP – FLOPS
Controlled latches are level – triggered
Flip-Flops are edge – triggered
C
CLK
Positive Edge
CLK
Negative Edge

## Slide 25: FLIP – FLOPS
There are two ways that a latch can be modified to form a flip – flop.
  Employ two latches in a special configuration that
    isolates the output of the flip – flop from being affected while its input is changing.
  Produce a flip – flop that triggers only during a signal transition.
    From 0 to 1 or from 1 to 0 only.
    Disabled during the rest of the clock pulse duration.

## Slide 26: FLIP – FLOPS
Master – Slave D flip – flops
D Latch
(Master)
D
C
Q
D Latch
(Slave)
D
C
Q
Q
D
CLK
CLK
D
QMaster
QSlave
Looks like it is negative edge-triggered
Master
Slave

## Slide 27: FLIP – FLOPS
Edge-Triggered D Flip – Flop
Two latches respond to the external D (data) and CLK (clock inputs).
Third latch provides the outputs for the flip – flop.

## Slide 28: FLIP – FLOPS
Edge-Triggered D Flip – Flop
When CLK = 0, S = 1 and R = 1.Output = present state.
If D = 0, when CLK  1
  R changes to 0
  Flip – flop goes to the RESET state.
  Q = 0.

## Slide 29: FLIP – FLOPS
Edge-Triggered D Flip – Flop
If D changes when CLK = 1 then
  R remains at 0.
  Flip – flop is locked out
  Unresponsive to further changes in the input.
When CLK  0,
  R  1
  Placing the output latch in the quiescent condition.
  No change in the output.

## Slide 30: FLIP – FLOPS
Edge-Triggered D Flip – Flop
If D = 1 when CLK = 0  1,
  S changes to 0.
  Circuit goes to SET state
  Q = 1.
  Any change in D while CLK = 1 does not affect the output.

## Slide 31: FLIP – FLOPS
Edge-Triggered D Flip – Flop
When CLK in the positive-edge-triggered flip – flop
  Makes positive transition
    The value of D is transferred to Q.
  Makes negative transition
    Does not affect the output.
  Steady CLK 1 or 0
    Does not affect the output.

## Slide 32: FLIP – FLOPS
Edge-Triggered D Flip – Flop
  The timing of the response of a flip – flop to input data and clock must be taken into consideration when using edge – triggered flip - flops.
    There is a minimum time, called setup time, for which the D input must be maintained at a constant value prior to the occurrence of the clock transition.
    There is a minimum time, called hold time, for which the D input must not change after the application of the positive transition of the clock.

## Slide 33: FLIP – FLOPS
Edge-Triggered D Flip – Flop
Positive Edge
Negative Edge
D
Q
Q
D
Q
Q
Dynamic input

## Slide 34: FLIP – FLOPS
The most economical and efficient flip – flop constructed is the edge – triggered D flip – flop.
  It requires smallest number of gates.
Other types of flip – flops can be constructed by using the D flip – flop and external logic.
  JK flip – flops
  T flip - flops

## Slide 35: FLIP – FLOPS
There are three operations that can be performed with a flip – flop:
  Set it to 1
  Reset it to 0
  Complement its output

## Slide 36: FLIP – FLOPS
JK Flip – Flop
  Performs all three operations.
When J = 1, sets the flip – flop to 1.
When K = 1, resets the flip – flop to 0.
D = JQ’ + K’Q

## Slide 37: FLIP – FLOPS
JK Flip – Flop
Operation 1
When J = 1 and K = 0,
  D = 1.Q’ + 1.Q (Post2b)
  D = Q’ + Q (Post5a)
  D = 1
  Next clock edge sets the output to 1.
D = JQ’ + K’Q

## Slide 38: FLIP – FLOPS
JK Flip – Flop
Operation 2
When J = 0 and K = 1,
  D = 0.Q’ + 0.Q (Theo2b)
  D = 0 + 0
  D = 0
  Next clock edge sets the output to 0.
D = JQ’ + K’Q

## Slide 39: FLIP – FLOPS
JK Flip – Flop
Operation 3
When J = 1 and K = 1,
  D = 1.Q’ + 0.Q (Post2b)
  D = Q’ + 0 .Q (Theo2b)
  D = Q’ + 0 (Post2a)
  D = Q’
  Next clock edge complements the output.
D = JQ’ + K’Q

## Slide 40: FLIP – FLOPS
JK Flip – Flop
When J = 0 and K = 0,
  D = 0.Q’ + 1.Q (Theo2b)
  D = 0 + 1 .Q (Post2b)
  D = 0 + Q (Post2a)
  D = Q
  Next clock edge the output is unchanged.
D = JQ’ + K’Q

## Slide 41: FLIP – FLOPS
JK Flip – Flop
D = JQ’ + K’Q
J
Q
Q
K

## Slide 42: FLIP – FLOPS
T (toggle) Flip – Flop
  Complementing flip – flop.
  Can be obtained from a JK flip – flop.
  When inputs J and K are tied together.
  Useful for designing binary counters.
J
Q
Q
K
T
C
D = JQ’ + K’Q
D = TQ’ + T’Q = T  Q

## Slide 43: FLIP – FLOPS
T (toggle) Flip – Flop
  When T = 0 (J = K = 0)
  A clock edge does not change the output.
  When T = 1 (J = K = 1)
  A clock edge complements the output.
J
Q
Q
K
T
C
D = JQ’ + K’Q
D = TQ’ + T’Q = T  Q

## Slide 44: FLIP – FLOPS
T (toggle) Flip – Flop
  Can be constructed with a D flip – flop and an XOR gate.
  When T = 0 then D = Q
    No change in the output.
  When T = 1 then D = Q’
    Output complements
D
Q
Q
T
C
D = TQ’ + T’Q = T  Q

## Slide 45: FLIP – FLOPS
T (toggle) Flip – Flop
J
Q
Q
K
T
C
D
Q
Q
T
C
T
Q
Q
C
(a) From JK Flip – Flop
(b) From D Flip – Flop
(c) Graphic Symbol

## Slide 46: FLIP – FLOPS
Flip – Flop Characteristics Table
Reset
Set
D | Q (t+1)
0 | 0
1 | 1
D
Q
Q
Q(t+1) = D
Q(t+1) = T  Q

## Slide 47: FLIP – FLOPS
Flip – Flop Characteristics Table
No change
Reset
Set
Toggle
J
Q
Q
K
J | K | Q (t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q

## Slide 48: FLIP – FLOPS
Flip – Flop Characteristics Table
T
Q
Q
No change
Toggle
T | Q (t+1)
0 | Q(t)
1 | Q’(t)
Q(t+1) = T ⊕ Q

## Slide 49: FLIP – FLOPS
Some flip – flops have asynchronous inputs that are used to force the flip – flop to a particular state independent of the clock.
The input that sets the flip – flop to 1 is called preset.
The input that clears the flip – flop to 0 is called clear or direct reset.
When power is on in a digital system, the state of the flip flop is unknown.

## Slide 50: FLIP – FLOPS
When power is on in a digital system, the state of the flip flop is unknown.
The direct inputs are useful for bringing all flip – flops in the system to a known starting state prior to the clocked operation.

## Slide 51: FLIP – FLOPS
Asynchronous Reset
R’ | D | CLK | Q(t+1)
0 | x | x | 0
D
Q
Q
R
Reset

## Slide 52: FLIP – FLOPS
Asynchronous Reset
D
Q
Q
R
Reset
R’ | D | CLK | Q(t+1)
0 | x | x | 0
1 | 0 | ↑ | 0
1 | 1 | ↑ | 1

## Slide 53: FLIP – FLOPS
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
D
Q
Q
CLR
Reset
PR
Preset

## Slide 54: FLIP – FLOPS
Asynchronous Preset and Clear
D
Q
Q
CLR
Reset
PR
Preset
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
0 | 1 | x | x | 1

## Slide 55: FLIP – FLOPS
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
0 | 1 | x | x | 1
1 | 1 | 0 | ↑ | 0
1 | 1 | 1 | ↑ | 1
Asynchronous Preset and Clear
D
Q
Q
CLR
Reset
PR
Preset

## Slide 56: 5.4 Analysis of clocked Sequential circuits

## Slide 57: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
The behaviour of a clocked sequential circuit is determined from:
  The inputs
  The outputs
  The state of its flip – flops
The outputs and the next state are both a function of
  The inputs
  The present state

## Slide 58: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
The analysis of sequential circuit consists of:
  Obtaining a table or a diagram for the time sequence of
    Inputs
    Outputs
    Internal states
  It is also possible to write Boolean expression that describe the behaviour of the sequential circuit.

## Slide 59: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
State Equations
The behaviour of a clocked sequential circuit can be described algebraically by means of state equations (transition equations).
A state equation specifies the next state as a function of
  The present state
  Inputs

## Slide 60: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Consider:
Circuit consists of:
  Two D flip – flops A and B.
  An input x.
  An output y.
  It is possible to write a set of equations for the circuit.

## Slide 61: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Consider:
A(t+1) = A(t) . x(t) + B(t) . x(t)
B(t+1) = A’(t) . x(t)
  (t+1)  next state of the flip flop
  Right side of the equation is a Boolean expression
    Specifies the present state
    Input conditions that make the next state = 1.

## Slide 62: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Consider:
A(t+1) = A(t) . x(t) + B(t) . x(t)
B(t+1) = A’(t) . x(t)
  Since all the variables in the Boolean expression are a function of the present state
  We can omit the designation (t)
A(t+1) = A . x + B . x
B(t+1) = A’ . x

## Slide 63: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Consider:
Similarly,
y(t) = [A(t) + B(t)] x’(t)
y = (A + B) x’

## Slide 64: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Consider:
A(t+1) = A . x + B . x
B(t+1) = A’ . x
y = (A + B) x’

## Slide 65: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
State Table
The time sequence of inputs, outputs and flip – flop can be enumerated in state table (transition table).
In general, a sequential circuit with m flip – flops and n inputs needs 2m+n rows in the state table.

## Slide 66: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
State Table
A(t+1) = A . x + B . x
B(t+1) = A’ . x
y = (A + B) x’
Present State (t) |  | Input (t) | Next State (t+1) |  | Output
A | B | x | A | B | y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
0
0
0
0
1
0
0
0
1
0
1
0
0
0
1
1
0
0
0
0
1
1
0
0

## Slide 67: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
State Table 2
A(t+1) = A . x + B . x
B(t+1) = A’ . x
y = (A + B) x’
Present State (t) | Next State (t+1) |  | Output |  | 
 | x=0 | x=1 | x=0 | x=1 | 
AB | AB | AB | y |  | y
00 |  |  |  |  | 
01 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
00
01
0
00
11
1
00
10
1
00
10
1
0
0
0
0

## Slide 68: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
State Diagram
The information available in a state table can be represented graphically in the form of a state diagram.
State is represented by a circle
Transition between states are indicated by directed lines connecting the circles.

## Slide 69: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
State Diagram
Present State (t) | Next State (t+1) |  | Output |  | 
 | x=0 | x=1 | x=0 | x=1 | 
AB | AB | AB | y |  | y
00 |  |  |  |  | 
01 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
00
01
0
00
11
1
00
10
1
00
10
1
0
0
0
0
0 0
1 0
0 1
1 1
0/0
0/1
1/0
1/0
1/0
1/0
0/1
0/1
AB
input/output

## Slide 70: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Analysis with D Flip – Flops
A(t+1) = DA = A  x  y
D
Q
Q
x
CLK
y
A
Present state | Inputs |  | Next state
A | x | y | A
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0
1
00,11
00,11
01,10
01,10

## Slide 71: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Analysis with JK Flip – Flops
JA = B KA = B . x’
JB = x’ KB = A  x
A(t+1) = JA Q’A + K’A QA
= A’B + AB’ + Ax
B(t+1) = JB Q’B + K’B QB
= B’x’ + ABx + A’Bx’

## Slide 72: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Analysis with JK Flip – Flops
JA = B KA = B x’
JB = x’ KB = A  x
A(t+1) = JA Q’A + K’A QA
= A’B + AB’ + Ax
B(t+1) = JB Q’B + K’B QB
= B’x’ + ABx + A’Bx’
Present State |  | I/P | Next State |  | Flip – Flop Inputs | 
A | B | x | A | B | JA KA | JB KB
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 0 1 0
0 0 0 1
1 1 1 0
1 0 0 1
0 0 1 1
0 0 0 0
1 1 1 1
1 0 0 0
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1

## Slide 73: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Analysis with JK Flip – Flops
0 0
1 1
0 1
1 0
x=1
x = 0
x=1
x = 0
x = 1
x =0
x = 0
x = 1
Present State |  | I/P | Next State |  | Flip – Flop Inputs | 
A | B | x | A | B | JA KA | JB KB
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 0 1 0
0 0 0 1
1 1 1 0
1 0 0 1
0 0 1 1
0 0 0 0
1 1 1 1
1 0 0 0
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1

## Slide 74: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Analysis with T Flip – Flops
TA = B.x TB = x
y = A . B
Q(t+1) = T ⊕ Q = T’Q + TQ’
A(t+1) = TA ⊕ A = TA’ A + TA A’
= (Bx)’ A + BxA’
= (B’ + x’)A + A’Bx
= AB’ + Ax’ + A’Bx
B(t+1) = TB ⊕ B = TB’ B + TB B’
= x’B + xB’
= x ⊕ B

## Slide 75: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Analysis with T Flip – Flops
TA = B.x TB = x
y = A . B
Q(t+1) = T ⊕ Q = T’Q + TQ’
A(t+1) = TA ⊕ A = TA’ A + TA A’
= (Bx)’ A + BxA’
= (B’ + x’)A + A’Bx
= AB’ + Ax’ + A’Bx
B(t+1) = TB ⊕ B = TB’ B + TB B’
= x’B + xB’
= x ⊕ B
Present State |  | I/P | Next State |  | FF Inputs | Output
A | B | x | A | B | TA TB | y
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 0
0 1
0 1
1 0
1 0
1 1
1 1
0 0
0 0
0 1
0 0
1 1
0 0
0 1
0 0
1 1
0
0
0
0
0
0
1
1

## Slide 76: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Analysis with T Flip – Flops
Present State |  | I/P | Next State |  | FF Inputs | Output
A | B | x | A | B | TA TB | y
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 0
0 1
0 1
1 0
1 0
1 1
1 1
0 0
0 0
0 1
0 0
1 1
0 0
0 1
0 0
1 1
0
0
0
0
0
0
1
1
00/0
01/0
11/1
10/0
x = 0
x = 1
x = 0
x = 1
x = 1
x = 1
x = 0
x = 0

## Slide 77: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Mealy and Moore Models
The most general model of a sequential circuit has:
  Inputs
  Outputs
  Internal states.
Sequential circuits are divided into two (they differ in the way output is generated:
  Mealy model
  Moore model

## Slide 78: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Mealy and Moore Models
Mealy model:
  The output is a function of both the present state and input.
  The outputs may change if the inputs change during the clock pulse period.
    The outputs may have momentary false values unless the inputs are synchronized with the clocks.
  Example of Sequential Circuit

## Slide 79: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Mealy and Moore Models
Moore model:
  The output is function of the present state only.
  The outputs are synchronous with the clocks.
  Example of Sequential Circuit

## Slide 80: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Mealy and Moore Models
Next State Combinational Logic
State Register
Output Combinational Logic
Outputs
(Mealy – type)
clock
Inputs
Mealy Machine
Next State Combinational Logic
State Register
Output Combinational Logic
Outputs
(Moore – type)
clock
Inputs
Moore Machine

## Slide 81: ANALYSIS OF CLOCKED SEQUENTIAL CIRCUITS
Present State |  | I/P | Next State |  | O/P
A | B | x | A | B | y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0
Mealy
For the same state, the output changes with the input
Present State |  | I/P | Next State |  | O/P
A | B | x | A | B | y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1
Moore
For the same state, the output does not change with the input

## Slide 82: 5.5 state reduction And assignment

## Slide 83: STATE REDUCTION AND ASSIGNMENT
The analysis of sequential circuits
  starts from a circuit diagram and
  culminates in a state table or diagram.
The design of a sequential circuits
  starts from a set of specifications and
  culminates in a logic diagram.

## Slide 84: STATE REDUCTION AND ASSIGNMENT
State – reduction algorithms are concerned with procedures for reducing the number of states in a state table, while keeping the external input – output requirements unchanged.
Since m flip – flops produce 2m states,
  a reduction in the number of states may (or may not) result in a reduction in the number of flip – flops.
An unpredictable effect in reducing the number of flip – flops is that sometimes the equivalent circuit (with fewer flip – flops) may require more combinational gates.

## Slide 85: STATE REDUCTION AND ASSIGNMENT
Consider a sequential circuit whose specification is given in the state diagram.
There are infinite number of input sequence that may be applied to the circuit;
  Each results in a unique output sequence.
0/0
g
a
b
c
d
e
f
0/0
0/0
0/0
0/0
1/0
1/0
0/0
1/1
1/1
1/1
0/0
1/1
1/0

## Slide 86: STATE REDUCTION AND ASSIGNMENT
Consider input sequence
  01010110100
  Starting from the initial state a.
  Each input of 0/1 produces an output of 0/1 and causes circuit to go to the next state.
0/0
g
a
b
c
d
e
f
0/0
0/0
0/0
0/0
1/0
1/0
0/0
1/1
1/1
1/1
0/0
1/1
1/0

## Slide 87: STATE REDUCTION AND ASSIGNMENT
Consider input sequence
  01010110100
0/0
g
a
b
c
d
e
f
0/0
0/0
0/0
0/0
1/0
1/0
0/0
1/1
1/1
1/1
0/0
1/1
1/0
state |  |  |  |  |  |  |  |  |  |  |  | 
input |  |  |  |  |  |  |  |  |  |  |  | 
output |  |  |  |  |  |  |  |  |  |  |  | 
a
0
0
a
1
0
b
0
0
c
1
0
d
0
0
e
1
1
f
1
1
f
0
0
g
1
1
f
0
0
g
0
0
a

## Slide 88: STATE REDUCTION AND ASSIGNMENT
Two circuits are equivalent
  Have identical outputs for all input sequences;
  The number of states is not important.
The problem of state reduction is
  To find ways of reducing the number of states in a sequential circuit without altering the input – output relationships.

## Slide 89: STATE REDUCTION AND ASSIGNMENT
Equivalent States
  Two states are said to be equivalent if,
    For each member of the set of inputs,
    they give exactly the same output and
    send the circuit to the same state or to an equivalent state.
  When two states are equivalent, one of them can be removed without altering the input – output relationships.

## Slide 90: STATE REDUCTION AND ASSIGNMENT
Reduce the number of states
  Draw a state table
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
a |  |  |  | 
b |  |  |  | 
c |  |  |  | 
d |  |  |  | 
e |  |  |  | 
f |  |  |  | 
g |  |  |  | 
0/0
g
a
b
c
d
e
f
0/0
0/0
0/0
0/0
1/0
1/0
0/0
1/1
1/1
1/1
0/0
1/1
1/0
a b
c d
a d
e f
a f
g f
a f
0 0
0 0
0 0
0 1
0 1
0 1
0 1

## Slide 91: STATE REDUCTION AND ASSIGNMENT
Reduce the number of states
  e = g (remove g)
  The row g is removed.
  State g is replaced by state e each time it occurs in the next – state columns.
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
a |  |  |  | 
b |  |  |  | 
c |  |  |  | 
d |  |  |  | 
e |  |  |  | 
f |  |  |  | 
g |  |  |  | 
a b
c d
a d
e f
a f
g f
a f
0 0
0 0
0 0
0 1
0 1
0 1
0 1

## Slide 92: STATE REDUCTION AND ASSIGNMENT
Reduce the number of states
  Present state f has now next states e and f and outputs 0 and 1 for x = 0 and x = 1.
  Then, d = f (remove f)
  The row f is removed.
  The state f is replaced by state d.
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
a |  |  |  | 
b |  |  |  | 
c |  |  |  | 
d |  |  |  | 
e |  |  |  | 
f |  |  |  | 
a b
c d
a d
e f
a f
e f
0 0
0 0
0 0
0 1
0 1
0 1

## Slide 93: STATE REDUCTION AND ASSIGNMENT
Reduce the number of states
  Final table
  This table satisfies the original input – output specifications and will produce the required output sequence for any given input sequence.
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
a |  |  |  | 
b |  |  |  | 
c |  |  |  | 
d |  |  |  | 
e |  |  |  | 
a b
c d
a d
e d
a d
0 0
0 0
0 0
0 1
0 1

## Slide 94: STATE REDUCTION AND ASSIGNMENT
Reduce the number of states
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
a |  |  |  | 
b |  |  |  | 
c |  |  |  | 
d |  |  |  | 
e |  |  |  | 
a b
c d
a d
e d
a d
0 0
0 0
0 0
0 1
0 1
0/0
g
a
b
c
d
0/0
0/0
0/0
1/0
1/0
1/1
1/1
0/0
1/0

## Slide 95: STATE REDUCTION AND ASSIGNMENT
Reduce the number of states
  The checking of each pair of states for possible equivalence can be done systematically using Implication Table.
  The unused states are treated as don't-care condition Þ fewer combinational gates.

## Slide 96: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  The state-reduction procedure for completely specified state tables is based on the algorithm that two states in a state table can be combined into one if they can be shown to be equivalent. There are occasions when a pair of states do not have the same next states, but, nonetheless, go to equivalent next states. Consider the following state table:

## Slide 97: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  Consider the following state table:
  (a, b) imply (c, d) and (c, d) imply (a, b). Both pairs of states are equivalent; i.e., a and b are equivalent as well as c and d.
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
a | c | b | 0 | 1
b | d | a | 0 | 1
c | a | d | 1 | 0
d | b | d | 1 | 0

## Slide 98: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  The checking of each pair of states for possible equivalence in a table with a large number of states can be done systematically by means of an implication table. This a chart that consists of squares, one for every possible pair of states, that provide spaces for listing any possible implied states. Consider the following state table:

## Slide 99: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  Consider the following state table:
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
a | d | b | 0 | 0
b | e | a | 0 | 0
c | g | f | 0 | 1
d | a | d | 1 | 0
e | a | d | 1 | 0
f | c | b | 0 | 0
g | a | e | 1 | 0
  Implication table:

## Slide 100: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  On the left side along the vertical are listed all the states defined in the state table except the last, and across the bottom horizontally are listed all the states except the last.
  The states that are not equivalent are marked with a ‘x’ in the corresponding square, whereas their equivalence is recorded with a ‘√’.

## Slide 101: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  Some of the squares have entries of implied states that must be further investigated to determine whether they are equivalent or not.
  The step-by-step procedure of filling in the squares is as follows:
  Place a cross in any square corresponding to a pair of states whose outputs are not equal for every input.
  Enter in the remaining squares the pairs of states that are implied by the pair of states representing the squares. We do that by starting from the top square in the left column and going down and then proceeding with the next column to the right.

## Slide 102: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  3. Make successive passes through the table to determine whether any additional squares should be marked with a ‘x’. A square in the table is crossed out if it contains at least one implied pair that is not equivalent.
  4. Finally, all the squares that have no crosses are recorded with check marks. The equivalent states are: (a, b), (d, e), (d, g), (e, g).

## Slide 103: STATE REDUCTION AND ASSIGNMENT
Implication Table (extra reading)
  We now combine pairs of states into larger groups of equivalent states. The last three pairs can be combined into a set of three equivalent states (d, e,g) because each one of the states in the group is equivalent to the other two. The final partition of these states consists of the equivalent states found from the implication table, together with all the remaining states in the state table that are not equivalent to any other state:
  (a, b) (c) (d, e, g) (f)

## Slide 104: STATE REDUCTION AND ASSIGNMENT
State Assignment
  In order to design a sequential circuit with physical components, it is necessary to assign coded binary values to the states.
  To minimize the cost of the combinational circuits.
  For a circuit with m states, the codes must contain n bits where 2n = ≥ m.
  Ex: with 3 bits it is possible to assign codes to 8 states denoted by binary numbers 000 trough 111.

## Slide 105: STATE REDUCTION AND ASSIGNMENT
State Assignment
  If the state table1 is used, we must assign binary values to 7 states.
    Remaining state is unused.
  If the state table2 is used, only five states need binary assignment.
    Remaining 3 state is unused.
    Unused states treated as don’t care conditions.
    Since don’t care conditions usually help in obtaining a simpler circuit, it is more likely that the circuit with five states will require fewer combinational gates than the one with seven states.

## Slide 106: STATE REDUCTION AND ASSIGNMENT
State Assignment
Present state | Assignment 1 Binary | Assignment 2 Gray Code | Assignment 3 One-hot
a | 000 | 000 | 00001
b | 001 | 001 | 00010
c | 010 | 011 | 00100
d | 011 | 010 | 01000
e | 100 | 110 | 10000

## Slide 107: STATE REDUCTION AND ASSIGNMENT
State Assignment
  Any binary number assignment is satisfactory as long as each state is assigned a unique number.
  Use binary assignment 1.
Present state | Next state |  | Output | 
 | x = 0 | x = 1 | x = 0 | x = 1
000 | 000 | 001 | 0 | 0
001 | 010 | 011 | 0 | 0
010 | 000 | 011 | 0 | 0
011 | 100 | 011 | 0 | 1
100 | 000 | 011 | 0 | 1

## Slide 108: 5.6 design procedure

## Slide 109: DESIGN PROCEDURE
The design of a clocked sequential circuit starts from
  a set of specifications and
  culminates in a logic diagram or
  a list of Boolean functions from which the logic diagram can be obtained.

## Slide 110: DESIGN PROCEDURE
Derive a state diagram for the circuit from the word description.
Reduce the number of states if necessary.
Assign binary values to the states.
Obtain the binary-coded state table.
Choose the type of flip-flops.
Derive the simplified flip-flop input equations and output equations.
Draw the logic diagram.

## Slide 111: DESIGN PROCEDURE
Example: We wish to design a circuit that detects three or more consecutive 1’s in a string of bits coming through an input line.
State diagram:
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1

## Slide 112: DESIGN PROCEDURE
This is a Moore model sequential circuit since the output is 1 when the circuit is in State3 and 0 otherwise.
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1
State | A B
S0 | 0 0
S1 | 0 1
S2 | 1 0
S3 | 1 1

## Slide 113: DESIGN PROCEDURE
Present State |  | I/P | Next State |  |  | O/P
A | B | x | A | B | y | 
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1
0 0 0
0 1 0
0 0 0
1 0 0
0 0 0
1 1 0
0 0 1
1 1 1

## Slide 114: DESIGN PROCEDURE
To implement the circuit,
  Two D flip-flops are chosen to represent the four states and label their outputs A and B.
  There is one input x.
  There is one output y.
  The characteristic equation of the D flip – flop is
    Q(t+1) = DQ.

## Slide 115: DESIGN PROCEDURE
To implement the circuit,
  The flip – flop input equations can be obtained directly from the next – state columns of A and B and expressed in sum of minterms.
  A(t+1) = DA(A,B,x) = ∑ (3, 5, 7)
  B(t+1) = DB(A,B,x) = ∑ (1, 5, 7)
  y(A,B,x) = ∑ (6, 7)
Present State |  | I/P | Next State |  |  | O/P
A | B | x | A | B | y | 
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0 0 0
0 1 0
0 0 0
1 0 0
0 0 0
1 1 0
0 0 1
1 1 1

## Slide 116: DESIGN PROCEDURE
Synthesis using D Flip - flops
  A(t+1) = DA(A,B,x) = ∑ (3, 5, 7)
  B(t+1) = DB(A,B,x) = ∑ (1, 5, 7)
  y(A,B,x) = ∑ (6, 7)
DA’s K - Map
Bx A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | M2
 |  |  |  | 1 | 
A | 1 | m4 | m5 | m7 | M6
 |  |  | 1 | 1 | 
 |  |  | x |  | 
DA = Ax
+ Bx

## Slide 117: DESIGN PROCEDURE
Synthesis using D Flip – flops
  A(t+1) = DA(A,B,x) = ∑ (3, 5, 7)
  B(t+1) = DB(A,B,x) = ∑ (1, 5, 7)
  y(A,B,x) = ∑ (6, 7)
DB’s K - Map
Bx A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | M2
 |  |  | 1 |  | 
A | 1 | m4 | m5 | m7 | M6
 |  |  | 1 | 1 | 
 |  |  | x |  | 
DA = Ax
+ B’x

## Slide 118: DESIGN PROCEDURE
Synthesis using D Flip – flops
  A(t+1) = DA(A,B,x) = ∑ (3, 5, 7)
  B(t+1) = DB(A,B,x) = ∑ (1, 5, 7)
  y(A,B,x) = ∑ (6, 7)
y’s K - Map
Bx A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | M2
A | 1 | m4 | m5 | m7 | M6
 |  |  |  | 1 | 1
 |  |  | x |  | 
y = AB

## Slide 119: DESIGN PROCEDURE
Synthesis using D Flip – flops
  DA = Ax + Bx
  DB = Ax + B’x
  y = AB
Logic Diagram of Sequence Detector

## Slide 120: DESIGN PROCEDURE
When – D type flip-flops are employed, the input equations are obtained directly from the next state.
This is not the case for the JK and T types of flip-flops. In order to determine the input equations for these flip flops, it is necessary to derive a functional relationship between the state table and the input equations.

## Slide 121: DESIGN PROCEDURE
During the design process we usually know the transition from present state to the next state and wish to find the flip – flop input conditions that will cause the required transition.
For this reason, we need a table that lists the required inputs for a given change of state. Such table is called an excitation table.

## Slide 122: DESIGN PROCEDURE
D Flip – Flop Excitation table
Present State | Next State | F.F. Input
Q(t) | Q(t+1) | D
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
0
1
D | Q (t+1)
0 | 0
1 | 1
D Flip – Flop Characteristic Table
Q(t+1) = D

## Slide 123: DESIGN PROCEDURE
JK Flip – Flop Excitation table
Present State | Next State | F.F. Input | 
Q(t) | Q(t+1) | J | K
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0 0 (No change)
0 1 (Reset)
0 X
1 X
X 1
X 0
1 0 (Set)
1 1 (Toggle)
0 1 (Reset)
1 1 (Toggle)
0 0 (No change)
1 0 (Set)
JK Flip – Flop Characteristic Table
J | K | Q (t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q

## Slide 124: DESIGN PROCEDURE
T Flip – Flop Excitation table
Present State | Next State | F.F. Input
Q(t) | Q(t+1) | T
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0
T Flip – Flop Characteristic Table
T | Q (t+1)
0 | Q(t)
1 | Q’(t)
Q(t+1) = T ⊕ Q

## Slide 125: DESIGN PROCEDURE
0
1
1
0
0
1
0
1
Synthesis Using JK Flip – Flops: Detect 3 or more consecutive 1’s
S0 / 0
S1 / 0
S3 / 1
S2 / 0

## Slide 126: DESIGN PROCEDURE
Synthesis Using JK Flip – Flops: Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 1 | 1 | 0 |  |  |  | 
1 | 0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 1 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 | 0 |  |  |  | 
1 | 1 | 1 | 1 | 1 |  |  |  | 
0 X
0 X
0 X
1 X
X 1
X 0
X 1
X 0
0 X
1 X
X 1
X 1
0 X
1 X
X 1
X 0
JA (A, B, x) = ∑ (3, 4, 5, 6, 7)
KA (A, B, x) = ∑ (0, 1, 2, 3, 4, 6)
JB (A, B, x) = ∑ (1, 2, 3, 5, 6, 7)
KB (A, B, x) = ∑ (0, 1, 2, 3, 4, 5, 6)

## Slide 127: DESIGN PROCEDURE
Synthesis Using JK Flip – Flops: Detect 3 or more consecutive 1’s
  JA (A, B, x) = ∑ (3, 4, 5, 6, 7)
  KA (A, B, x) = ∑ (0, 1, 2, 3, 4, 6)
  JB (A, B, x) = ∑ (1, 2, 3, 5, 6, 7)
  KB (A, B, x) = ∑ (0, 1, 2, 3, 4, 5, 6)
JA’s K-Map
Bx A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  |  | 1 | 
A | 1 | m4 | m5 | m7 | m6
 |  | X | X | X | X
 |  |  | x |  | 
JA = Bx

## Slide 128: DESIGN PROCEDURE
Synthesis Using JK Flip – Flops: Detect 3 or more consecutive 1’s
  JA (A, B, x) = ∑ (3, 4, 5, 6, 7)
  KA (A, B, x) = ∑ (0, 1, 2, 3, 4, 6)
  JB (A, B, x) = ∑ (1, 2, 3, 5, 6, 7)
  KB (A, B, x) = ∑ (0, 1, 2, 3, 4, 5, 6)
KA’s K-Map
Bx A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | X | X | X | X
A | 1 | m4 | m5 | m7 | M6
 |  | 1 |  |  | 1
 |  |  | x |  | 
KA = x’

## Slide 129: DESIGN PROCEDURE
Synthesis Using JK Flip – Flops: Detect 3 or more consecutive 1’s
  JA (A, B, x) = ∑ (3, 4, 5, 6, 7)
  KA (A, B, x) = ∑ (0, 1, 2, 3, 4, 6)
  JB (A, B, x) = ∑ (1, 2, 3, 5, 6, 7)
  KB (A, B, x) = ∑ (0, 1, 2, 3, 4, 5, 6)
JB’s K-Map
Bx A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  | 1 | X | X
A | 1 | m4 | m5 | m7 | M6
 |  |  | 1 | X | X
 |  |  | x |  | 
JB = x

## Slide 130: DESIGN PROCEDURE
Synthesis Using JK Flip – Flops: Detect 3 or more consecutive 1’s
  JA (A, B, x) = ∑ (3, 4, 5, 6, 7)
  KA (A, B, x) = ∑ (0, 1, 2, 3, 4, 6)
  JB (A, B, x) = ∑ (1, 2, 3, 5, 6, 7)
  KB (A, B, x) = ∑ (0, 1, 2, 3, 4, 5, 6)
KB’s K-Map
Bx A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | X | X | 1 | 1
A | 1 | m4 | m5 | m7 | m6
 |  | X | X |  | 1
 |  |  | x |  | 
KB = A’
+ x’

## Slide 131: DESIGN PROCEDURE
Synthesis Using JK Flip – Flops: Detect 3 or more consecutive 1’s
  JA = Bx
  KA = x’
  JB = x
  KB = A’ + x’
Logic Diagram of Sequence Detector

## Slide 132: DESIGN PROCEDURE
Synthesis Using T Flip – Flops: 3-bit Counter. An n-bit binary counter consists of n flip – flops that can count in binary from 0 to 2n – 1.
000
100
101
110
111
001
010
011

## Slide 133: DESIGN PROCEDURE
Synthesis Using T Flip – Flops: 3-bit Counter.
Present State |  |  |  | Next State |  |  |  | Flip-Flop Inputs |  | 
A2 | A1 | A0 |  | A2 | A1 | A0 |  | TA2 | TA1 | TA0
0 | 0 | 0 |  | 0 | 0 | 1 |  |  |  | 
0 | 0 | 1 |  | 0 | 1 | 0 |  |  |  | 
0 | 1 | 0 |  | 0 | 1 | 1 |  |  |  | 
0 | 1 | 1 |  | 1 | 0 | 0 |  |  |  | 
1 | 0 | 0 |  | 1 | 0 | 1 |  |  |  | 
1 | 0 | 1 |  | 1 | 1 | 0 |  |  |  | 
1 | 1 | 0 |  | 1 | 1 | 1 |  |  |  | 
1 | 1 | 1 |  | 0 | 0 | 0 |  |  |  | 
0
0
0
1
0
0
0
1
0
1
0
1
0
1
0
1
1
1
1
1
1
1
1
1
TA2 (A2, A1, A0) = ∑ (3, 7)
TA1 (A2, A1, A0) = ∑ (1, 3, 5, 7)
TA0 (A2, A1, A0) = ∑ (0, 1, 2, 3, 4, 5, 6, 7)

## Slide 134: DESIGN PROCEDURE
Synthesis Using T Flip – Flops: 3-bit Counter.
  TA2 (A2, A1, A0) = ∑ (3, 7)
  TA1 (A2, A1, A0) = ∑ (1, 3, 5, 7)
  TA0 (A2, A1, A0) = ∑ (0, 1, 2, 3, 4, 5, 6, 7)
TA2’s K-Map
A1A0 A2 |  |  |  | A1 | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  |  | 1 | 
A | 1 | m4 | m5 | m7 | m6
 |  |  |  | 1 | 
 |  |  | A0 |  | 
TA2 = A1A0

## Slide 135: DESIGN PROCEDURE
Synthesis Using T Flip – Flops: 3-bit Counter.
  TA2 (A2, A1, A0) = ∑ (3, 7)
  TA1 (A2, A1, A0) = ∑ (1, 3, 5, 7)
  TA0 (A2, A1, A0) = ∑ (0, 1, 2, 3, 4, 5, 6, 7)
TA1’s K-Map
A1A0 A2 |  |  |  | A1 | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  | 1 | 1 | 
A | 1 | m4 | m5 | m7 | m6
 |  |  | 1 | 1 | 
 |  |  | A0 |  | 
TA1 = A0

## Slide 136: DESIGN PROCEDURE
Synthesis Using T Flip – Flops: 3-bit Counter.
  TA2 (A2, A1, A0) = ∑ (3, 7)
  TA1 (A2, A1, A0) = ∑ (1, 3, 5, 7)
  TA0 (A2, A1, A0) = ∑ (0, 1, 2, 3, 4, 5, 6, 7)
TA0’s K-Map
A1A0 A2 |  |  |  | A1 | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 1 | 1 | 1 | 1
A | 1 | m4 | m5 | m7 | m6
 |  | 1 | 1 | 1 | 1
 |  |  | A0 |  | 
TA0 = 1

## Slide 137: DESIGN PROCEDURE
Synthesis Using T Flip – Flops: 3-bit Counter.
  TA2 = A1A0
  TA1 = A0
  TA0 = 1
Logic Diagram of 3-bit Binary Counter

## Slide 138: THANK YOU!
GOOD LUCK!