## Slide 1: INTRODUCTION TO LOGIC DESIGN Chapter 1 Digital Systems and Binary Numbers
gürtaçyemişçioğlu

## Slide 2: OUTLINE OF CHAPTER 1
Digital
Systems
Binary
Numbers
Number-base
Conversions
Octal &
Hexadecimal
Numbers
Complements
Signed Binary
Numbers
Binary
Codes
Binary Storage
& Registers
Binary Logic
Binary
Arithmetic

## Slide 3: 1.1 DIGITAL systems

## Slide 4: DIGITAL SYSTEMS
Digital age and information age
Digital computers
  General purposes
  Many scientific, industrial and commercial applications
Digital systems
  Telephone switching exchanges
  Digital camera
  Electronic calculators, PDA's
  Digital TV
Discrete information-processing systems
  Manipulate discrete elements of information
  For example, {1, 2, 3, …} and {A, B, C, …}…

## Slide 5: DIGITAL SYSTEMS
DIGITAL SIGNAL
The physical quantities or signals can assume only discrete values.
Greater accuracy
ANALOG SIGNAL
  The physical quantities or signals may vary continuously over a specified range.
t
X(t)
t
X(t)

## Slide 6: DIGITAL SYSTEMS
Binary digital signal
  An information variable represented by physical quantity.
  For digital systems, the variable takes on discrete values.
    Two level, or binary values are the most prevalent values.
  Binary values are represented abstractly by:
    Digits 0 and 1
    Words (symbols) False (F) and True (T)
    Words (symbols) Low (L) and High (H)
    And words On and Off

## Slide 7: DIGITAL SYSTEMS
Binary values are represented by values or ranges of values of physical quantities.
t
V(t)
Logic 1
Logic 0
undefine

## Slide 8: 1.2 Binary Numbers

## Slide 9: BINARY NUMBERS
Decimal Number System
Base (also called radix) = 10
  10 digits
  { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Digit Position
  Integer & fraction
Digit Weight
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
5
1
2
7
4
102
101
100
10-1
10-2
500
10
2
0.7
0.04
100
10
1
0.1
0.01
5x100
1x10
2x1
7x0.1
4x0.01
d2 x B2 + d1 x B1 + d0 x B0+d-1 x B-1+d-2x B-2
(512.74)10
+
+
+

## Slide 10: BINARY NUMBERS
Octal Number System
Base = 8
  8 digits
  { 0, 1, 2, 3, 4, 5, 6, 7}
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation
5
1
2
7
4
82
81
80
8-1
8-2
320
8
2
0.875
0.0625
64
8
1
1/8
1/64
5x64
1x8
2x1
7x1/8
4x1/64
o2 x B2 + o1 x B1 + o0 x B0 + o-1 x B-1+o-2 x B-2
(512.74)8
(330.9375)10
+
+
+

## Slide 11: BINARY NUMBERS
Hexadecimal Number System
Base = 16
  16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F}
Weights
  Weight = (Base) Position
Magnitude
  Sum of “bit x Weight”
Formal Notation
1
E
5
7
A
162
161
160
16-1
16-2
256
224
5
0.4375
0.039
256
16
1
1/16
1/256
1x256
14x16
5x1
7x1/16
10x1/256
H2 x B2 + H1 x B1 + H0 x B0+H-1 x B-1+H-2x B-2
(458.4765625)10
(1E5.7A)16
+
+
+

## Slide 12: BINARY NUMBERS
Binary Number System
Base = 2
  2 digits { 0, 1 }, called binary digits or “bits”
Weights
  Weight = (Base) Position
Magnitude
  Sum of “bit x Weight”
Formal Notation
Groups of bits
  4 bits = Nibble, 8 bits = Byte
1
0
1
0
1
22
21
20
2-1
2-2
4
0
1
0
0.25
4
2
1
0.5
0.25
1x4
0x2
1x1
0x0.5
1x0.25
b2 x B2 + b1 x B1 + b0 x B0+b-1 x B-1+b-2x B-2
(5.25)10
(101.01)2
+
+
+

## Slide 13: BINARY NUMBERS
n | 2n
0 | 20=1
1 | 21=2
2 | 22=4
3 | 23=8
4 | 24=16
5 | 25=32
6 | 26=64
7 | 27=128
n | 2n
8 | 28=256
9 | 29=512
10 | 210=1024
11 | 211=2048
12 | 212=4096
20 | 220=1M
30 | 230=1G
40 | 240=1T
The power of 2

## Slide 14: 1.3 Binary Arithmetic

## Slide 15: BINARY ARITHMETIC
5
5
5
5
+
0
1
1
= Ten ≥ Base
 Subtract a Base
1
1
Carry
ADDITION
Decimal Addition

## Slide 16: BINARY ARITHMETIC
ADDITION
Binary Addition - Column Addition
1
0
1
1
1
1
1
1
1
1
0
+
0
0
0
0
1
1
1
≥ (2)10
1
1
1
1
1
1
= 61
= 23
= 84

## Slide 17: BINARY ARITHMETIC
SUBTRACTION
Binary Subtraction - Borrow a “Base” when needed
0
0
1
1
1
0
1
1
1
1
0
−
0
1
0
1
1
1
0
= (10)2
2
2
2
2
1
0
0
0
1
= 77
= 23
= 54

## Slide 18: BINARY ARITHMETIC
MULTIPLICATION
Binary Multiplication – Bit by bit
0
1
1
1
1
0
1
1
0
0
0
0
0
0
0
1
1
1
1
0
1
1
1
1
0
0
0
0
0
0
1
1
0
1
1
1
0
x

## Slide 19: 1.4 Number-base conversion

## Slide 20: NUMBER BASE CONVERSION
Decimal
(Base 10)
Octal
(Base 8)
Binary
(Base 2)
Hexadecimal
(Base 16)
Evaluate Magnitude
Evaluate Magnitude
Evaluate Magnitude

## Slide 21: NUMBER BASE CONVERSION
Decimal to binary conversion
Divide the number by the ‘Base’ (=2)
Take the remainder (either 0 or 1) as a coefficient
Take the quotient and repeat the division

## Slide 22: NUMBER BASE CONVERSION
Decimal (integer) to binary conversion
Example: (13)10
Quotient
Remainder
Coefficient
Answer: (13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB LSB
13
/ 2 = 6
1 a0 = 1
6
/ 2 = 3
0 a1 = 0
3
/ 2 = 1
1 a2 = 1
1
/ 2 = 0
1 a3 = 1

## Slide 23: NUMBER BASE CONVERSION
Decimal (fraction) to binary conversion
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division

## Slide 24: NUMBER BASE CONVERSION
Decimal (fraction) to binary conversion
Example: (0.625)10
Integer
Fraction
Coefficient
Answer: (0.625)10 = (0.a-1 a-2 a-3)2 = (0.101)2
MSB LSB
0.625
* 2 = 1 . 25
0.25
* 2 = 0 . 5
0.5
* 2 = 1 . 0
a-1 = 1
a-2 = 0
a-3 = 1

## Slide 25: NUMBER BASE CONVERSION
Decimal (integer) to octal conversion
Example: (175)10
Quotient
Remainder
Coefficient
Answer: (175)10 = (a3 a2 a1 a0)2 = (257)8
MSB LSB
175
/ 8 = 21
7 a0 = 7
21
/ 8 = 2
5 a1 = 5
2
/ 8 = 0
2 a2 = 2

## Slide 26: NUMBER BASE CONVERSION
Decimal (fraction) to octal conversion
Example: (0.3125)10
Integer
Fraction
Coefficient
Answer: (0.3125)10 = (0.a-1 a-2 a-3)2 = (0.24)8
MSB LSB
0.3125
* 8 = 2 . 5
0.5
* 8 = 4 . 0
a-1 = 2
a-2 = 4

## Slide 27: 1.5 Octal & hexadecimal Numbers

## Slide 28: OCTAL & HEXADECIMAL NUMBERS
Binary to octal conversion
8 = 23
Each group of 3 bits represents an octal digit
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111
Example:
( 1 0 1 1 0 . 0 1 )2
( 2 6 . 2 )8
Assume Zeros
Works both ways (Binary to Octal & Octal to Binary)
0
0

## Slide 29: OCTAL & HEXADECIMAL NUMBERS
Binary to hexadecimal conversion
16 = 24
Each group of 4 bits represents a hexadecimal digit
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111
Example:
( 1 0 1 1 0 . 0 1 )2
( 1 6 . 4 )16
Assume Zeros
Works both ways (Binary to Hex & Hex to Binary)
000
00

## Slide 30: OCTAL & HEXADECIMAL NUMBERS
Octal to hexadecimal conversion
Convert to binary as an intermediate step
Example:
( 0 1 0 1 1 0 . 0 1 0 )2
( 1 6 . 4 )16
Works both ways (Octal to Hex & Hex to Octal)
( 2 6 . 2 )8
Assume Zeros
0 0
0

## Slide 31: OCTAL & HEXADECIMAL NUMBERS
Decimal | Octal | Hex | Binary
00 | 00 | 0 | 0000
01 | 01 | 1 | 0001
02 | 02 | 2 | 0010
03 | 03 | 3 | 0011
04 | 04 | 4 | 0100
05 | 05 | 5 | 0101
06 | 06 | 6 | 0110
07 | 07 | 7 | 0111
08 | 10 | 8 | 1000
09 | 11 | 9 | 1001
10 | 12 | A | 1010
11 | 13 | B | 1011
12 | 14 | C | 1100
13 | 15 | D | 1101
14 | 16 | E | 1110
15 | 17 | F | 1111

## Slide 32: 1.6 complements

## Slide 33: COMPLEMENTS
Complements are used in digital computers to simplify the subtraction operation and for logical manipulation. Simplifying operations leads to simpler, less expensive circuits to implement the operations.
There are two types of complements for each base-r system:
  diminished radix complement.
  the radix complement

## Slide 34: COMPLEMENTS
Diminished Radix Complement (r-1)’s Complement
  Given a Number = N, base = r, digits = n,
  The (r–1)’s complement of N is defined as:
  (rn –1) – N
Example for 6-digit decimal numbers:
  9’s complement is (rn – 1)–N = (106–1)–N = 999999–N
  9’s complement of 546700 is 999999–546700 = 453299

## Slide 35: COMPLEMENTS
For decimal numbers r = 10 and
  (r-1) = 9, this is called 9’s complement of N.
  (10n-1)-N.
  10n represents a number that consist of a single 1 followed by n 0’s.
  10n-1 is a number represented by n 9’s.
For binary numbers r = 2 and
  r-1 = 1, this is called 1’s complement of N.
  (2n-1)-N.
  2n represents a binary number that consist of a 1 followed by n 0’s.

## Slide 36: COMPLEMENTS
For Example: 0011
When subtracting binary digit from 1 we can have either 1-0 =1 or 1-1 =0 which causes bit to change from 0 to 1 or from 1 to 0.
1’s complement of a binary is formed by changing 1’s to 0’s and 0’s to 1’s.
Example: 00110111100100
  (24-1) – 0011
24 = 10000
- 1
01111
  1111
  - 0011
  1100

## Slide 37: COMPLEMENTS
Example for 7-digit binary numbers:
  1’s complement is (rn – 1) – N = (27–1)–N = 1111111–N
  1’s complement of 1011000 is 1111111–1011000 = 0100111
Observation:
  Subtraction from (rn – 1) will never require a borrow
  Diminished radix complement can be computed digit-by-digit

## Slide 38: COMPLEMENTS
1’s Complement (Diminished Radix Complement)
All ‘0’s become ‘1’s
All ‘1’s become ‘0’s
If you add a number and its 1’s complement …
+
0
1
0
0
1
1
1
1
1
0
1
1
0
0
0
0
1
1
1
1
1
1
1
1

## Slide 39: COMPLEMENTS
Radix Complement, the r's Complement
  Given a Number = N, base = r, digits = n,
  The r’s complement of N is defined as:
  rn - N, for N ≠ 0 and 0 for N = 0.
The r's complement is obtained by adding 1 to the (r  1) 's complement, since
  = [(rn  1) – N] + 1.
  = rn-N

## Slide 40: COMPLEMENTS
10’s complement of N can be formed:
  By leaving all least significant 0’s unchanged.
  By subtracting first non-zero least significant digit by 10
  By subtracting all higher significant digits from 9.
2’s complement of N can be formed:
  By leaving all least significant 0’s and the first 1 unchanged and replacing 1’s with 0’s and 0’s with 1’s in all other higher significant digits.

## Slide 41: COMPLEMENTS
Example: Base-10
  The 10's complement of 012398:
  The 10’s complement of 246700:
9
9
9
9
9
10
0
1
2
3
9
8
-
9
8
7
6
0
2
9
9
9
10
0
0
2
4
6
7
0
0
-
7
5
3
3
0
0

## Slide 42: COMPLEMENTS
2’s Complement (Radix Complement)
  Take 1’s complement then add 1
  Toggle all bits to the left of the first ‘1’ from the right
  Example:
  Number:
  1’s Comp.:
1 0 1 1 0 0 0 0
0
0
0
0
1
0
1
0
+
0
1
0
0
1
1
1
1
1
0
1
1
0
0
0
0
0
1
0
1
0
0
0
0
1
1
1
1
1
or

## Slide 43: COMPLEMENTS
Example: Base-2
  The 2's complement of 1101100 is 0010100
1 1 0 1 1 0 0
0
0
1
0
1
0
0
+
0
0
1
0
0
1
1
1
1
0
1
1
0
0
0
0
1
0
1
0
0
1
1
1
or

## Slide 44: COMPLEMENTS
Example: Base-2
  The 2's complement of 0110111 is 1001001
0 1 1 0 1 1 1
1
0
0
1
0
0
1
+
1
0
0
1
0
0
0
0
1
1
0
1
1
1
1
0
0
1
0
0
1
1
or

## Slide 45: COMPLEMENTS
Complement of the complement restores the number to its original value
  r’s complement of N is rn-N
  The complement of the complement is
  rn-(rn-N) = N  original number

## Slide 46: COMPLEMENTS
The subtraction of two n-digit unsigned numbers M – N in base r can be done as follows:
  Add the minuend M to the r’s complement of the subtrahend N.
    N r’s complement = rn-N
    = M + rn-N
    = M – N+rn
  If M ≥ N, the sum will produce an end carry rn, which can be discarded; what is left is the result M – N.
  If M < N, the sum does not produce an end carry and is equal to rn-(N-M), which is the r’s complement of (N-M). To obtain the answer in a familiar form, take the r’s complement of the sum and place negative sign in front.

## Slide 47: COMPLEMENT
Example 1.5
  Using 10's complement, subtract 72532 – 3250.
M = 72532
N = 3250
Step1: Take 10’s complement of N
9
9
10
0
3
2
5
0
-
6
7
5
0
9
9

## Slide 48: COMPLEMENT
Step2: To find the SUM, Add 10’s complement of N to M
72532
+
96750
169282
Step3: To find the ANSWER discard end carry 105, Subtract rn from SUM
169282
100000
-
69282
SUM=
ANSWER=

## Slide 49: COMPLEMENT
Example 1.6
  Using 10's complement, subtract 3250 - 72532.
M = 3250
N = 72532
Step1: Take 10’s complement of N
9
9
9
10
2
5
3
2
-
7
4
6
8
2
9
7

## Slide 50: COMPLEMENT
Step2: To find the SUM, Add 10’s complement of N to M
03250
+
27468
30718
Step3: To find the ANSWER take the –(10’s complement of SUM)
-69282
SUM=
ANSWER=
There is no end carry!
9
9
9
10
9
0
7
1
8
-
9
2
8
2
6
3

## Slide 51: COMPLEMENT
1
0
1
1
1
1
0
0
0
0
1
0
Example 1.7: Given the two binary numbers X = 1010100 and Y = 1000011, perform the subtraction (a) X – Y and (b) Y – X using 2’s complements.
(a) Step1: Take the 2’s complement of Y
1
1
  Step2: Add 2’s complement of Y to X
0
1
0
0
1
1
0
1
1
1
1
1
0
0
+
0
1
0
1
0
0
0
1
There is an end carry!

## Slide 52: COMPLEMENT
  Step3: Discard the end carry.
(b) Y – X: Step1: Take the 2’s complement of X
+
0
1
0
1
0
0
0
1
0
0
0
0
0
0
0
1
0
1
0
1
0
0
0
0
0
0
1
1
0
1
0
0
1
0
0
1
1
0
ANSWER=

## Slide 53: COMPLEMENT
  Step2: Add 2’s complement of X to Y
0
0
0
1
0
1
1
1
0
1
0
1
0
0
+
1
0
1
1
1
1
1
There is no end carry!
  Step3: To find the answer Y – X = - (2’s complement of SUM)
1
0
0
0
1
0
0
1
0
1
1
1
1
1
-
SUM=

## Slide 54: COMPLEMENTS
Subtraction of unsigned numbers can also be done by means of the (r  1)'s complement. Remember that the (r  1) 's complement is one less then the r's complement.
Example 1.8 :Repeat Example 1.7, but this time using 1's complement.
X – Y = 1010100 – 1000011(84 – 67 = 17)
Step1: Take the 1’s complement of Y
0
0
1
1
1
1
0
0
0
0
1
0
1
1

## Slide 55: COMPLEMENTS
Step2: Add1’s complement of Y to the X
Step3: Remove the end carry and add 1 (End-around carry)
0
1
0
0
1
1
0
1
1
1
0
1
0
0
+
0
1
0
0
0
0
0
1
There is an end carry!
Sum is 1 less than the correct difference when an end carry occurs!
+
0
1
0
0
0
0
0
1
0
1
0
1
0
0
0
ANSWER=
= 16
= 17
SUM=

## Slide 56: COMPLEMENTS
Example 1.8 :Repeat Example 1.7, but this time using 1's complement.
Y – X = 1000011 – 1010100 (67 – 84 = -17)
Step1: Take the 1’s complement of X
1
1
0
1
0
1
0
0
1
0
0
1
1
0

## Slide 57: COMPLEMENTS
Step2: Add1’s complement of X to the Y
Step3: To find the answer Y – X = - (1’s complement of SUM)
0
0
0
1
0
1
1
1
0
1
1
0
0
1
+
1
0
1
0
1
1
1
There is NO end carry!
ANSWER=
= -17
SUM=
-
1
0
0
0
1
0
0
1
0
1
0
1
1
1

## Slide 58: 1.7 Signed binary numbers

## Slide 59: SIGNED BINARY NUMBERS
To represent negative integers, we need a notation for negative values.
It is customary to represent the sign with a bit placed in the left most position of the number since binary digits.
The convention is to make the sign bit
  0 for positive and 1 for negative.
Example
  Signed-magnitude representation: 10001001
  Signed-1’s complement representation: 11110110
  Signed-2’s complement representation: 11110111
Table 1.3 lists all possible four-bit signed binary numbers in the three representations.

## Slide 60: SIGNED BINARY NUMBERS
Decimal | Signed-2’s Complement | Signed-1’s Complement | Signed Magnitude
+7 | 0111 | 0111 | 0111
+6 | 0110 | 0110 | 0110
+5 | 0101 | 0101 | 0101
+4 | 0100 | 0100 | 0100
+3 | 0011 | 0011 | 0011
+2 | 0010 | 0010 | 0010
+1 | 0001 | 0001 | 0001
+0 | 0000 | 0000 | 0000
-0 | - | 1111 | 1000
-1 | 1111 | 1110 | 1001
-2 | 1110 | 1101 | 1010
-3 | 1101 | 1100 | 1011
-4 | 1100 | 1011 | 1100
-5 | 1011 | 1010 | 1101
-6 | 1010 | 1001 | 1110
-7 | 1001 | 1000 | 1111
-8 | 1000 | - | -

## Slide 61: SIGNED BINARY NUMBERS
Arithmetic addition
  The addition of two numbers in the signed-magnitude system follows the rules of ordinary arithmetic.
    If the signs are the same;
      we add the two magnitudes and give the sum the common sign.
    If the signs are different;
      we subtract the smaller magnitude from the larger and give the difference the sign of the larger magnitude.

## Slide 62: SIGNED BINARY NUMBERS
  The addition of two signed binary numbers with negative numbers represented in signed-2's-complement form is obtained from the addition of the two numbers, including their sign bits.
  A carry out of the sign-bit position is discarded.
Example:
0
0
0
0
1
0
1
0
0
1
1
1
0
0
+
0
1
0
1
0
0
1
0
0
0
19
6
13
+
+
+
1
1
1
0
0
1
1
0
0
1
1
1
0
0
+
0
0
0
1
1
0
1
0
1
0
7
6
13
-
+
+

## Slide 63: SIGNED BINARY NUMBERS
Example:
0
0
0
0
1
0
1
1
1
0
1
0
1
1
+
1
1
1
1
0
1
0
1
0
1
7
6
13
+
-
-
1
1
1
0
0
1
1
1
1
0
1
0
1
1
+
1
0
1
1
1
1
0
1
1
1
19
6
13
-
-
-

## Slide 64: SIGNED BINARY NUMBERS
Arithmetic Subtraction
  In 2’s-complement form:
    Take the 2’s complement of the subtrahend (including the sign bit) and add it to the minuend (including sign bit).
    A carry out of sign-bit position is discarded.
  – (+B) = (
  – (-B) = (

## Slide 65: SIGNED BINARY NUMBERS
Example:
  (-6) – (-13)  (11111010 – 11110011)
1
1
1
0
0
1
1
0
0
1
1
1
0
0
-
0
0
0
1
1
0
1
0
1
0
7
6
13
-
+
+

## Slide 66: 1.8 Binary codes

## Slide 67: BINARY CODES
BCD Code
  A number with k decimal digits will require 4k bits in BCD.
  Decimal 396 is represented in BCD with 12bits as:
  Each group of 4 bits representing one decimal digit.
396
0011
1001
0110

## Slide 68: BINARY CODES
  A decimal number in BCD is the same as its equivalent binary number only when the number is between 0 and 9.
  The binary combinations 1010 through 1111 are not used and have no meaning in BCD.
Decimal Symbol | BCD Digit
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001

## Slide 69: BINARY CODES
Example:
  Consider decimal 185 and its corresponding value in BCD and binary:
(185)10
(0001
1000
0101)BCD
=
(10111001)2

## Slide 70: BINARY CODES
BCD Addition
  Consider the addition of two decimal digits in BCD
  Since each digit does not exceed 9
  The sum cannot be greater than 9 + 9 + 1 = 19
    the 1 in the sum being a previous carry
  Suppose we add the BCD digits as if they were binary numbers
  The binary sum will produce a result in the range from 0 to 19
  In binary this will be from 0000 to 10011, but in BCD it is from 0000 to 1 1001
    The first 1 being a carry and the next four bits being the BCD digit sum

## Slide 71: BINARY CODES
BCD Addition
  When binary sum is equal to or less than 1001 (without a carry)
    The corresponding BCD digit is correct
  When the binary sum is greater than or equal to 1010
    The result is an invalid BCD digit
  The addition of 6 = (0110)2 to the binary sum converts it to the correct digit and also produces a carry as required
  This is because the difference between a carry in the most significant bit position of the binary sum and a decimal carry.
    16 – 10 = 6

## Slide 72: BINARY CODES
BCD Addition
  Consider the following three addition of two decimal digits in BCD
0
0
1
0
0
1
1
0
+
1
1
0
0
9
4
5
+
0
0
1
0
1
1
0
0
+
1
0
1
0
12
4
8
+
1
0
0
0
1
1
0
0
+
0
1
0
0
17
8
9
+
1

0
0
1
1
+
0
0
0
1
1
0
0
1
1
+
0
1
1
1
1
Correct BCD digit sum (2)
Carry
Correct BCD digit sum (7)
Carry

## Slide 73: BINARY CODES
The addition of two n-digit unsigned BCD numbers follows the same procedure.
  Consider the addition of 184 + 576 = 760 in BCD
0
1
0
0
1
0
0
0
0
0
1
0
4
1
8
0
1
1
0
0
1
1
1
0
0
1
1
6
5
7
+
+
+
0
1
1
1
0
0
0
0
1
0
0
1
1
1
1
Binary Sum
Add 6
BCD Sum
0
0
1
1
+
0
0
1
1
+
0
0
1
1
0
0
0
0
0
1
1
1
0
7
6
+

## Slide 74: BINARY CODES
The representation of signed decimal numbers in BCD is similar to the representation of signed numbers in binary.
We can use either the familiar sign and magnitude system or the signed-complement system.
The sign of a decimal number is usually represented with four bits to conform to the 4-bit code of the decimal digits.
  “+” with 0 0 0 0 and “-” with 1001 (BCD equivalent of 9)

## Slide 75: BINARY CODES
The signed-complement system can be either the 9’s or the 10’s complement.
  But the 10’s complement is the one most often used.
To obtain the 10’s complement of a BCD number:
  First take the 9’s complement
    9’s complement is calculated from the subtraction of each digit from 9.
  Then add one to the least significant digit

## Slide 76: BINARY CODES
The procedures developed for the signed-2’s complement system in the previous section apply also to the signed-10’s complement system for decimal numbers.
Addition is done by:
  adding all digits,
  including the sign digit and
  discarding the end carry.
This assumes that all negative numbers are in 10’s complement form.

## Slide 77: BINARY CODES
Consider the addition (+375) + (-240) = +135
Step1: Find the 10’s complement of (-240)
Step 2: Add 10’s complement of (-240) to 375 and discard the end carry.
9
10
0
2
4
0
-
7
6
0
135
375
760
+
0
9
0

## Slide 78: BINARY CODES

## Slide 79: BINARY CODES
Gray code:
  The output data of many physical systems produce quantities that are continuous.
  These data must be converted into digital form before they are applied to a digital system.
  Continuous or analog information is converted into digital form by means of an analog-to-digital converter.
t
X(t)

## Slide 80: BINARY CODES
Gray code:
  It is convenient to use gray code to represent the digital data when it is converted from analog data.
  The advantage is that only bit in the code group changes in going from one number to the next.
    Error detection.
    Representation of analog data.
    Low power design.
Gray Code | Decimal Equivalent
0000 | 0
0001 | 1
0011 | 2
0010 | 3
0110 | 4
0111 | 5
0101 | 6
0100 | 7
1100 | 8
1101 | 9
1111 | 10
1110 | 11
1010 | 12
1011 | 13
1001 | 14
1000 | 15

## Slide 81: BINARY CODES
American Standard Code for Information Interchange (ASCII) Character Code (Refer to Table 1.7)
A popular code used to represent information sent as character-based data.
It uses 7-bits to represent 128 characters:
  94 Graphic printing characters.
  34 Non-printing characters.
Some non-printing characters are used for text format (e.g. BS = Backspace, CR = carriage return).
Other non-printing characters are used for record marking and flow control (e.g. STX and ETX start and end text areas).

## Slide 82: BINARY CODES

## Slide 83: BINARY CODES

## Slide 84: BINARY CODES
ASCII has some interesting properties:
  Digits 0 to 9 span Hexadecimal values 3016 to 3916
  Upper case A-Z span 4116 to 5A16
  Lower case a-z span 6116 to 7A16
    Lower to upper case translation (and vice versa) occurs by flipping bit 6.

## Slide 85: BINARY CODES
Error-Detecting Code
  To detect errors in data communication and processing, an eighth bit is sometimes added to the ASCII character to indicate its parity.
  A parity bit is an extra bit included with a message to make the total number of 1's either even or odd.
Example:
  Consider the following two characters and their even and odd parity:
 | With even parity | With odd parity
ASCII A = 1000001 | 01000001 | 11000001
ASCII T = 1010100 | 11010100 | 01010100

## Slide 86: BINARY CODES
Error-Detecting Code
  Redundancy (e.g. extra information), in the form of extra bits, can be incorporated into binary code words to detect and correct errors.
  A simple form of redundancy is parity, an extra bit appended onto the code word to make the number of 1’s odd or even. Parity can detect all single-bit errors and some multiple-bit errors.
  A code word has even parity if the number of 1’s in the code word is even.
  A code word has odd parity if the number of 1’s in the code word is odd.
  Example:
    Message A: 10001001 1 (even parity)
    Message B: 10001001 0 (odd parity)

## Slide 87: 1.9 Binary storage & registers

## Slide 88: BINARY STORAGE & REGISTERS
Registers
  A binary cell is a device that possesses two stable states and is capable of storing one of the two states.
  A register is a group of binary cells. A register with n cells can store any discrete quantity of information that contains n bits.
1/0
1
1
0
1
0
1
0
1
n cells
2n possible states

## Slide 89: BINARY STORAGE & REGISTERS
A binary cell
  Two stable state
  Store one bit of information
  Examples: flip-flop circuits, ferrite cores, capacitor
A register
  A group of binary cells
  AX in x86 CPU
Register Transfer
  A transfer of the information stored in one register to another.
  One of the major operations in digital system.
  An example in next slides.

## Slide 90: BINARY STORAGE & REGISTERS
Memory
Control Unit
Datapath
Input / Output
CPU
Inputs: Keyboard, mouse, modem, microphone
Outputs: CRT, LCD, modem, speakers
Synchronous or Asynchronous?

## Slide 91: BINARY STORAGE & REGISTER
Keyboard
Control
J
O
H
N
8 cells
Input Register
8 cells
8 cells
8 cells
8 cells
Processor Register
01001010 01001111 11001000 11001110
Memory Register
J
O
H
N
INPUT UNIT
PROCESSOR UNIT
MEMORY UNIT
Figure 1.1 Transfer of information among register

## Slide 92: BINARY STORAGE & REGISTERS
The other major component of a digital system
  Circuit elements to manipulate individual bits of information
  Load-store machine
    LD R1;
    LD R2;
    ADD R3, R2, R1;
    SD R3;
PROCESSOR UNIT
0011100001
0001000010
Digital logic circuits for binary addition
0100100011
0100100011
0011100001
0001000010
MEMORY UNIT
R1
R2
R3
SUM
Operand1
Operand2
Figure 1.2 Example of binary information processing

## Slide 93: 1.10 Binary logic

## Slide 94: BINARY LOGIC
Definition of Binary Logic
  Binary logic consists of binary variables and a set of logical operations.
  The variables are designated by letters of the alphabet, such as A, B, C, x, y, z, etc., with each variable having two and only two distinct possible values: 1 and 0,
  Three basic logical operations: AND, OR, and NOT.

## Slide 95: BINARY LOGIC
AND operation is represented by a dot () or by the absence of an operator.
  Example: or
    “X AND Y is equal to Z”.
    Z =1 if only X = 1 and Y = 1; otherwise Z = 0.
      X, Y and Z are binary variables and can be equal either to 1 or 0, nothing else.

## Slide 96: BINARY LOGIC
OR operation is represented by a plus (+).
  Example:
    “X OR Y is equal to Z”.
    Z =1 if X = 1 OR Y = 1 or if both X = 1 OR Y = 1.
    If both X = 0 OR Y = 0, then Z =0.

## Slide 97: BINARY LOGIC
NOT operation is represented by a prim (’) sometimes by an overbar ()
  Example: or = Z
    “NOT X is equal to Z”.
    If X = 1, then Z =0, but if X = 0, then Z = 1.
    The NOT operation is also referred to as the complement operation, since it changes a 1 to 0 and a 0 to 1.

## Slide 98: BINARY LOGIC
Truth tables, Boolean expressions and Logic Gates
AND
OR
NOT
X
Y
Z
0
0
0
0
1
0
1
0
0
1
1
1
X
Y
Z
0
0
0
0
1
1
1
0
1
1
1
1
X
Z
1
0
0
1
=
=
= Z

## Slide 99: BINARY LOGIC
AND
OR

## Slide 100: BINARY LOGIC
Example of binary signals
Logic 1
Logic 0
undefined
Volts
0
1
2
3
Transition occurs between these limits
Signal range for logic 1
Signal range for logic 0
0
1
2
3

## Slide 101: BINARY LOGIC
  Graphic Symbols and Input-Output Signals for Logic gates:
(a) two input AND gate
(b) two input OR gate
(c) NOT gate or Inverter

## Slide 102: BINARY LOGIC
  Graphic Symbols and Input-Output Signals for many input logic gates:
A
B
C
F = A B C
A
B
C
D
F = A + B + C + D
(a) three input AND gate
(b) four input OR gate