# TOP500 List - June 2011 (1-100) http://www.top500.org/list/2011/06/100

Rmax and Rpeak values are in TFlops. For more details about other fields, check the TOP500 description.

Power data in KW for entire system

next

| Rank | Site | Computer/Year Vendor | Cores | Rmax | Rpeak | Power |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | RIKEN Advanced Institute for Computational Science (AICS) Japan | K computer, SPARC64 VIIIfx 2.0GHz, Tofu interconnect / 2011 Fujitsu | 548352 | 8162.00 | 8773.63 | 9898.56 |
| 2 | National Supercomputing Center in Tianjin China | Tianhe-1A - NUDT TH MPP, X5670 2.93Ghz 6C, NVIDIA GPU, FT-1000 8C / 2010 NUDT | 186368 | 2566.00 | 4701.00 | 4040.00 |
| 3 | DOE/SC/Oak Ridge National Laboratory United States | Jaguar - Cray XT5-HE Opteron 6-core 2.6 GHz / 2009 Cray Inc. | 224162 | 1759.00 | 2331.00 | 6950.60 |
| 4 | National Supercomputing Centre in Shenzhen (NSCS) China | Nebulae - Dawning TC3600 Blade, Intel X5650, NVidia Tesla C2050 GPU / 2010 Dawning | 120640 | 1271.00 | 2984.30 | 2580.00 |
| 5 | GSIC Center, Tokyo Institute of Technology Japan | TSUBAME 2.0 - HP ProLiant SL390s G7 Xeon 6C X5670, Nvidia GPU, Linux/Windows / 2010 NEC/HP | 73278 | 1192.00 | 2287.63 | 1398.61 |
| 6 | DOE/NNSA/LANL/SNL United States | Cielo - Cray XE6 8-core 2.4 GHz / 2011 Cray Inc. | 142272 | 1110.00 | 1365.81 | 3980.00 |
| 7 | NASA/Ames Research Center/NAS United States | Pleiades - SGI Altix ICE 8200EX/8400EX, Xeon HT QC 3.0/Xeon 5570/5670 2.93 Ghz, Infiniband / 2011 SGI | 111104 | 1088.00 | 1315.33 | 4102.00 |
| 8 | DOE/SC/LBNL/NERSC United States | Hopper - Cray XE6 12-core 2.1 GHz / 2010 Cray Inc. | 153408 | 1054.00 | 1288.63 | 2910.00 |
| 9 | Commissariat a l'Energie Atomique (CEA) France | Tera-100 - Bull bullx super-node S6010/S6030 / 2010 Bull SA | 138368 | 1050.00 | 1254.55 | 4590.00 |

### TOP 10 Sites for November 2019

For more information about the sites and systems in the list, click on the links or view the complete list.

| Rank | System | Cores | Rmax (TFlop/s) | Rpeak (TFlop/s) | Power (kW) |
| --- | --- | --- | --- | --- | --- |
| 1 | Summit - IBM Power System AC922, IBM POWER9 22C 3.07GHz, NVIDIA Volta GV100, Dual-rail Mellanox EDR Infiniband , IBM DOE/SC/Oak Ridge National Laboratory United States | 2,414,592 | 148,600.0 | 200,794.9 | 10,096 |
| 2 | Sierra - IBM Power System AC922, IBM POWER9 22C 3.1GHz, NVIDIA Volta GV100, Dual-rail Mellanox EDR Infiniband , IBM / NVIDIA / Mellanox DOE/NNSA/LLNL United States | 1,572,480 | 94,640.0 | 125,712.0 | 7,438 |
| 3 | Sunway TaihuLight - Sunway MPP, Sunway SW26010 260C 1.45GHz, Sunway , NRCPC National Supercomputing Center in Wuxi China | 10,649,600 | 93,014.6 | 125,435.9 | 15,371 |
| 4 | Tianhe-2A - TH-IVB-FEP Cluster, Intel Xeon E5-2692v2 12C 2.2GHz, TH Express-2, Matrix-2000 , NUDT National Super Computer Center in Guangzhou China | 4,981,760 | 61,444.5 | 100,678.7 | 18,482 |

PARALLEL MACHINES AND COMPUTATIONS

Instruction’s layout:

Opcode | operand1 | operand 2 | operand 3

Instructions may have different number of operands, different length.

Opcode defines instruction’s format, defining instruction’s length

Parallelism in sequential computers

I/O processor (IOP) can share access to memory with CPU. While CPU runs code not requiring access to external devices, IOP can perform previously issued query. So, several programs can live simultaneously – basis for multiprogramming mode of working of conventional computers.

Pipelining approach

PIPELINING APPROACH (CONT 1)

USING MULTIPLE ARITHMETIC UNITS

In the case of multiple arithmetic units able to execute their own operation as in VLIW (Very Long Instruction Word) machines, independent operations may be executed in parallel.

This requires look-ahead analysis to find operations not in the conflict. If two operations don’t use common data items or if they only read them – then they are not conflicting.

USING MULTIPLE ARITHMETIC UNITS (CONT 1)

In the best case evaluation of such an expression will require 5 steps (height of the computation tree is 5)

USING MULTIPLE ARITHMETIC UNITS (CONT 2)

Intelligent compiler using commutativity and associativity laws

a*b = b*a, a+b = b+a

a*(b*c) = (a*b)*c, a+(b+c) = (a+b)+c

can restructure computation tree to less height:

Flynn’s classification of systems

In conventional von Neumann machine we have a single stream of instructions (represented by PC, through which flows this stream) and a single stream of data processed by these instructions. This may be viewed as SISD machine. In Flynn’s classification, systems are distinguished on the base of numbers of existing streams of instructions and data (single or multiple):

| Instruction \ Data Streams | Single Data | Multiple |
| --- | --- | --- |
| Single instruction | sisd | simd |
| Multiple | misd | mimd |

SISD computers are the conventional von Neumann’s machines.

In SIMD computers same operations are to be performed on disjoint data items, which may be viewed as vectors. For example, a single vector add operation is used to produce a new vector

C = A + B,

whose elements are component wise addition of the two vectors.

Single operation can be issued by one CU, and is to be executed by multiple arithmetic units

In MISD computers a stream of data is processed by multiple instructions simultaneously using pipelining.

SIMD and MISD (conveyor, pipelined) computers are intended for vectors processing, they have similar representation in instruction sets and programming languages, therefore MISD computers are also called as pipelined SIMD computers

In MIMD computers, we have multiple CPUs processing their own data under streams of their own instructions

SIMD AND PIPELINED SIMD COMPUTERS

SIMD AND PIPELINED SIMD COMPUTERS (CONT 1)

Arithmetic pipeline is similar to fetch-execute pipeline previously considered (Figures 1-4, 1-5).

MIMD COMPUTERS OR MULTIPROCESSORS

There are 2 prototypical forms of MIMD computers, distinguished by the way the data are shared between processors.

The shared memory form has a general interconnection network between multiple processors and multiple memories so that any processor can access any memory location.

The distributed memory form associates a distinct memory with each processor with data being transmitted directly between processors.

MIMD COMPUTERS OR MULTIPROCESSORS (CONT 1)

Pipelined MIMD computers are also called multithreaded machines (instruction stream – thread).

INTERCONNECTION NETWORKS