## Slide 1
1
MOS Field-EffectTransistors (MOSFETs)
Lecture-5

## Slide 2
5.1 Device Structure
Figure 5.1 shows the physical structure of the n-channel enhancement-type MOSFET. The meaning of the names “enhancement” and “n-channel” will become apparent shortly. The transistor is fabricated on a p-type substrate, which is a single-crystal silicon wafer that provides physical support for the device
Thus four terminals are brought out: the gate terminal (G), the source terminal (S), the drain terminal (D), and the substrate or body terminal (B)
Figure 5.1

## Slide 3
At this point it should be clear that the name of the device (metal-oxide-semiconductor FET) is derived from its physical structure.
The gate electrode is electrically insulated from the device body (by the oxide layer).
It will be shown that a voltage applied to the gate controls current flow between source and drain. This current will flow in the longitudinal direction from drain to source in the region labeled “channel region.” Note that this region has a length L and a width W, two important parameters of the MOSFET. Typically, L is in the range of 0.03 μm to 1 μm, and W is in the range of 0.05 μm to 100 μm.
Notes: sedr42021_0401a.jpg

## Slide 4
Operation with Zero Gate Voltage
With zero voltage applied to the gate, two back-to-back diodes exist in series between drain and source.
One diode is formed by the pn junction between the n+ drain region and the p-type substrate, and the other diode is formed by the pn junction between the p-type substrate and the n+ source region
These back-to-back diodes prevent current conduction from drain to source when a voltage vDS is applied. In fact, the path between drain and source has a very high resistance

## Slide 5
Creating a Channel for Current Flow
Consider next the situation depicted in Fig. 5.2
With source and drain grounded, free holes under the gate region are repelled by the positive voltage, creating a depletion region of bound negative charge.
Electrons in the source and drain regions are forced into the channel, creating an n region under the gate terminal which connects the source and drain regions.
The value of vGS at which a sufficient number of mobile electrons accumulate in the channel region to form a conducting channel is called the threshold voltage Vt.
Correspondingly, the MOSFET of Fig. 5.2 is called an n-channel MOSFET or, alternatively, an NMOS transistor. Note that an n-channel MOSFET is formed in a p-type substrate:The channel is created by inverting the substrate surface from p type to n type.

## Slide 6
Figure 5.2 The enhancement-type NMOS transistor with a positive voltage applied to the gate. An n channel is induced at the top of the substrate beneath the gate.
Notes: sedr42021_0402.jpg

## Slide 7
Applying a Small vDS
A small positive voltage vDS is applied between drain and source. This causes a small current to flow in the induced channel. Current is carried by free electrons traveling from source to drain.
The magnitude of iD depends on the density of electrons in the channel, which in turn depends on the magnitude of vGS.
For vGS = Vt channel is just induced; the current conducted is still negligibly small. (vGS  Vt): excess gate voltage, overdrive voltage.

## Slide 8
Figure 5.3
An NMOS transistor with vGS > Vt and with a small vDS applied. The device acts as a resistance whose value is determined by vGS. Specifically, the channel conductance is proportional to vGS – Vt’ and thus iD is proportional to (vGS – Vt) vDS.
Notes: sedr42021_0403.jpg

## Slide 9
Figure 5.4
The iD–vDS characteristics of the MOSFET in Fig. 5.3 when the voltage applied between drain and source, vDS, is kept small. The device operates as a linear resistor whose value is controlled by vGS.
Notes: sedr42021_0404.jpg

## Slide 10
The operation of the MOSFET as a voltage-controlled resistance is further illustrated in Fig. 5.4, which is a sketch of iD versus vDS for various values of vGS.
Observe that the resistance is infinite for VGS ≤ Vt and decreases as VGS is increased above Vt.
It is interesting to note that although VGS is used as the parameter for the set of graphs in Fig. 5.4, the graphs in fact depend only on (VGS – Vt)
The description above indicates that for the MOSFET to conduct, a channel has to be induced. Then, increasing VGS above the threshold voltage Vt enhances the channel, hence the names enhancement-mode operation and enhancement-type MOSFET. Finally, we note that the current that leaves the source terminal (iS) is equal to the current that enters the drain terminal (iD), and the gate current iG = 0.

## Slide 11
Operation as VDS is increased
We next consider the situation as VDS is increased. For this purpose, let VGS be held constant at a value greater than Vt; that is, let the MOSFET be operated at a constant overdrive voltage VOV .
Figure 5.5
Operation of the enhancement NMOS transistor as vDS is increased. The induced channel acquires a tapered shape, and its resistance increases as vDS is increased. Here, vGS is kept constant at a value > Vt.

## Slide 12
Figure 5.6
Increasing vDS causes the channel to acquire a tapered shape. Eventually, as vDS reaches vGS – Vt’ the channel is pinched off at the drain end. Increasing vDS above vGS – Vt has little effect (theoretically, no effect) on the channel’s shape.
Notes: sedr42021_0407.jpg

## Slide 13
As VDS is increased, the channel becomes more tapered and its resistance increases correspondingly. Thus, the iD−VDS curve does not continue as a straight line but bends as shown in Fig. 5.7.
Figure 5.7 The drain current iD versus the drain-to-source voltage vDS for an enhancement-type NMOS transistor operated with vGS > Vt.

## Slide 14
Circuit Symbol
Figure 5.8
Circuit symbol for the n-channel enhancement-type MOSFET.
Modified circuit symbol with an arrowhead on the source terminal to distinguish it from the drain and to indicate device polarity (i.e., n channel).
Simplified circuit symbol to be used when the source is connected to the body or when the effect of the body on device operation is unimportant.
Notes: sedr42021_0406.jpg

## Slide 15
Current–Voltage Characteristics
Notes: sedr42021_0405.jpg

## Slide 16
Notes: sedr42021_0410a.jpg

## Slide 17
Figure 5.9 (a) An n-channel enhancement-type MOSFET with vGS and vDS applied and with the normal directions of current flow indicated. (b) The iD–vDS characteristics for a device with k’n (W/L) = 1.0 mA/V2.
Notes: sedr42021_0411a.jpg

## Slide 18
Figure 5.10 The iD–vGS characteristic for an enhancement-type NMOS transistor in saturation (Vt = 1 V, k’n W/L = 1.0 mA/V2).
Notes: sedr42021_0412.jpg

## Slide 19
Figure 5.11 Large-signal equivalent-circuit model of an n-channel MOSFET operating in the saturation region.
Notes: sedr42021_0413.jpg

## Slide 20
Figure 5.12
Effect of vDS on iD in the saturation region. The MOSFET parameter VA depends on the process technology and, for a given process, is proportional to the channel length L.
Notes: sedr42021_0416.jpg

## Slide 21
Figure 5.13
Large-signal equivalent circuit model of the n-channel MOSFET in saturation, incorporating the output resistance ro. The output resistance models the linear dependence of iD on vDS.
Notes: sedr42021_0417.jpg

## Slide 22
Example 5.1:
MOSFET Circuits at DC
Determine the values of RD and RS so that the transistor operates at
Solution 5.1:
To establish a dc voltage of +0.5 V at the drain, we must select RD as follows:
Notes: sedr42021_0420.jpg

## Slide 23
Since VD = 0.5 V is greater than VG, the NMOS transistor is operating in the saturation region, and we can use the saturation-region expression of iD to determine the required value of VOV.
Proof:
we can use the saturation-region expression of iD to determine the required value of VOV ,
= µn Cox process transconductance
parameter.

## Slide 25
Example 5.2:
Solution 5.2:
Find R in the circuit to obtain a current of 80 A. Find also the drain voltage VD.
Notes: sedr42021_0421.jpg

## Slide 26
Practice Problem 5.1
In the MOSFET circuit shown, the transistor has
, Vt = 1 V.
(a) Find R so that the drain current is ID = 1.6 mA.
(b) Find the drain voltage VD and the drain current ID for R = 5 kΩ.
(a) R=

## Slide 27
Example 5.3:
Solution 5.3:

## Slide 28
Practice Problem 5.2
In the MOSFET circuit shown, the transistor has the following parameters
0.5 , , Vt = 0.8 V
Find the drain current ID, and the gate-source voltage VGS.
State in which region of its characteristics the transistor operates.

## Slide 29
Example 5.4:
Determine the voltages at all nodes and currents in all branches.

## Slide 30
Solution 5.4:

## Slide 32
Practice Problem 5.3
In the MOSFET circuit shown, the transistor has the following parameters
, , Vt = 2 V
Find the drain current ID, and the gate-source voltage VGS. State in which region of its characteristics the transistor operates.

## Slide 33
Practice Problem 5.4
In the MOSFET circuit shown below, the transistors have widths W1 = 10 μm, W2 = 40 μm, and their lengths are equal, i.e. L1 = L2 = 2 μm. Both transistors have kn = 0.2mA/V2 , and Vt = 1 V. Find the voltage Vo and the current ID.

## Slide 34
Practice Problem 5.5

## Slide 37
To turn a PMOS transistor on, the gate voltage has to be made lower than that of the source by at least |Vtp| .
To operate in the triode region, the drain voltage has to exceed that of the gate by at least |Vtp| ; otherwise, the PMOS operates in saturation.

## Slide 38
Exercises

## Slide 42
b)

## Slide 43
|VOV |= 1 V
|VOV |= VSG - |VtP |
So VSG =1V+1V= 2V
Apply KVL, VDG –VSG + VSD = 0 V
VSD = 2V -1V= 1V

## Slide 44
Recall that
VDG –VSG + VSD = 0 V. Put VSD=
VDG = = 1V= 0.1mA xR
R= 10kΩ
Recall that
VDG –VSG + VSD = 0 V. To have
VSG = VSD , VDG = 0 V.
Since VDG = IxR and I0A then R= 0 Ω

## Slide 45
Design the circuit shown below so that the transistor operates in saturation with ID = 0.5 mA and VD = +3 V. Let the PMOS transistor have Vtp = −1 V and kp(W/L) = 1 mA/V2 . Assume λ = 0. What is the largest value that RD can have while maintaining saturation-region operation?
Example 5.5:

## Slide 46
Solution 5.5:
Since the MOSFET is to be in saturation, we can write
Saturation-mode operation will be maintained up to the point that VD exceeds VG by |Vt|; that is, until
This value of drain voltage is obtained with RD given by

## Slide 47
Example 5.6:
The NMOS and PMOS transistors in the circuit below are matched., Assuming λ=0 for both devices, find the drain currents iDN and iDP, as well as the voltage vO, for vI = 0 V, +2.5 V, and −2.5 V.

## Slide 48
Solution 5.6:
We note that since QN and QP are perfectly matched and are operating at equal values of |VGS| = 2.5 V, the circuit is symmetrical, which dictates that vO = 0 V. Thus both QN and QP are operating with |VDG| = 0 and, hence, in saturation. The drain currents can now be found from

## Slide 49
Next, we consider the circuit with vI = +2.5 V. Transistor QP will have a VSG of zero and thus will be cut off, reducing the circuit to that shown below. We note that vO will be negative, and thus vGD will be greater than Vtn, causing QN to operate in the triode region. For simplicity we shall assume that vDS is small and thus use
From the circuit diagram shown

## Slide 51
The situation for the case vI = −2.5 V
It will be the exact complement of the case vI = +2.5 V: Transistor QN will be off. Thus IDN = 0, QP will be operating in the triode region with IDP = 0.244 mA and vO = +2.44 V.

## Slide 52
Notes: sedr42021_e0412.jpg

## Slide 53
Notes: sedr42021_0422.jpg

## Slide 54
Notes: sedr42021_0423a.jpg

## Slide 55
Notes: sedr42021_0424.jpg

## Slide 57
Since VOV = 0.2 V and VDS = 0.4 V, we see that the maximum allowable negative signal swing at the drain is 0.2 V. Thus the maximum symmetrical signal swing allowable at the drain is ± 0.2 V

## Slide 58
Notes: sedr42021_0425a.jpg

## Slide 59
Figure (a) Basic structure of the common-source amplifier. (b) Graphical construction to determine the transfer characteristic of the amplifier in (a).
Notes: sedr42021_0426a.jpg

## Slide 60
Figure (Continued) (c) Transfer characteristic showing operation as an amplifier biased at point Q.
Notes: sedr42021_0426c.jpg

## Slide 61
(a) Find the quiescent operating point Q-point (ID, VDS) for the MOSFET in the fixed gate bias circuit below. Neglect channel-length modulation.
Example 5.5:

## Slide 62
Solution 5.5:
Unknowns:
ID , VDS , and VGS

## Slide 63
Thus, the Q-point is (50.0 uA, 5.00 V) with VGS = 3V
We have VDS = 5 V and VGS − VT = 2 V. Since VDS exceeds VGS − VT , the transistor is indeed pinched-off and in the saturation region

## Slide 64
Find the Q-point = (ID, VDS) for the MOSFET in the four resistor bias circuit shown below.
Example 5.6:
Solution 5.6:
The first step in our Q-point analysis of the equivalent circuit above is to assume that the MOSFET transistor is saturated

## Slide 66
4= VGS +
8.2=2VGS +(VGS-1)2
VGS = 2.68V
VEQ = VGS + ID RS
ID = =34 uA
VDS = 10V − [34uA x(75 k+ 39 k)] = 6.12 V
The saturation region assumption is consistent with the resulting Q-point: (34uA, 6.12 V) with VGS = 2.68 V.

## Slide 69
Notes: sedr42021_0435.jpg

## Slide 71
Notes: sedr42021_0438a.jpg

## Slide 74
Notes: sedr42021_0434.jpg

## Slide 75
Example 5.7:
Notes: sedr42021_0436.jpg

## Slide 76
Solution 5.7:
=
It works in saturation mode. The drain current is
= 2.5 MΩ

## Slide 77
For the CS amplifier of Example 5.7 determine Rin, Ro, and the overall voltage gain Gv where Rsig = 100 kΩ and RL = 20 kΩ.
Example 5.8:
Solution 5.8:
Notes: sedr42021_0437a.jpg

## Slide 78
Ro=(RD || ro) = (18k || 200k) = 16.5 kΩ
Rin = (RG1 || RG2)= 5M||2.5M= 1.67MΩ
Notes: sedr42021_0439.jpg

## Slide 79
Figure (a) Capacitively coupled common-source amplifier. (b) A sketch of the frequency response of the amplifier in (a) delineating the three frequency bands of interest.
Notes: sedr42021_0449a.jpg

## Slide 80
The MOSFET in the common-source amplifier shown has the small-signal parameters
gm = 2 mA/V, ro = 50 kΩ.
Assume that the transistor is properly biased at a point in its saturation region.
(a) Draw the small-signal equivalent circuit of the amplifier.
(b) Find the voltage gain , and the overall voltage gain .
Practice Problem 5.6