Eastern Mediterranean University

Department of Computer Engineering

CMPE-223 Worksheet # 4

- Consider the following combinational circuit:

  - Analyze the circuit by deriving the corresponding truth table.

  - Obtain the simplified expressions for F1 and F2.

- Consider the following combinational circuit:

  - Analyze the circuit by deriving the corresponding truth table.

  - Obtain the simplified expressions for F1 and F2.

- Find the minimal cost realization of the following combinational circuit. (i.e re-implement F with minimum number of gates).

- Design a combinational circuit with three inputs and one output. The output is 1 when the binary value of the input is greater than 3. The output is 0 otherwise.