## Slide 1: INTRODUCTION TO LOGIC DESIGN Chapter 3 Gate-Level Minimazation
gürtaçyemişçioğlu

## Slide 2: OUTLINE OF CHAPTER 1
The Map
Method
Product of
Sums
Simplification
Don’t Care
Conditions
NAND and NOR
Implementations
Other Two
Level
Implementations
Exclusive-OR
Function
Hardware
Description
Language
Four – Variable
K-Map

## Slide 3: 3.1 The Map Method

## Slide 4: THE MAP METHOD
Gate-level minimization refers to the design task of finding an optimal gate-level implementation of Boolean functions describing a digital circuit.

## Slide 5: THE MAP METHOD
The complexity of the digital logic gates
  The complexity of the algebraic expression
Logic minimization
  Algebraic approaches: lack of specific rules
  The Karnaugh map
    A simple straight forward procedure
    A pictorial form of a truth table
    Applicable if the # of variables < 7

## Slide 6: THE MAP METHOD
A diagram made up of squares
  Each square represents one minterm
The simplified expression produced by the map are always in one of the two standard forms:
  Sum of products
  Product of sums

## Slide 7: THE MAP METHOD
Boolean function
  Sum of minterms
  Sum of products (or product of sum) in the simplest form
  A minimum number of terms
  A minimum number of literals
  The simplified expression may not be unique

## Slide 8: THE MAP METHOD
A two-variable map
  Four minterms
  x' = row 0; x = row 1
  y' = column 0; y = column 1
  A truth table in square diagram
  xy
Figure 3.1 Two-variable Map
y x | 0 | 1
0 | m0 | m1
1 | m2 | m3
y x |  |  | y
 |  | 0 | 1
 | 0 | x’y’ | x’y
x | 1 | xy’ | xy

## Slide 9: THE MAP METHOD
Fig. 3.2(a):
  xy = m3
Fig. 3.2(b):
  x+y = x'y+xy' +xy = m1+m2+m3
Figure 3.2 Two-variable Map
(a) xy
(b) x+y
y x |  |  | y
 |  | 0 | 1
 | 0 |  | 
x | 1 |  | 1
y x |  |  | y
 |  | 0 | 1
 | 0 |  | 1
x | 1 | 1 | 1

## Slide 10: THE MAP METHOD
Three-variable map:
  For 3 binary variables.
  2n = 8 minterms.
  Map consists of 8 squares.
  Minterms are not arranged in a binary sequence.
  Only one bit changes in value from one adjacent column to the next.
y X |  |  | y |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
x | 1 | m4 | m5 | m7 | m6
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | x’y’z’ | x’y’z | x’yz | x’yz’
x | 1 | xy’z’ | xy’z | xyz | xyz’
 |  |  | z |  | 

## Slide 11: THE MAP METHOD
Any two adjacent squares in the map differ by only one variable
  Primed in one square and unprimed in the other
  e.g., m5 and m7 can be simplified
  m5+ m7 = xy'z + xyz = xz (y'+y) = xz
y X |  |  | y |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
x | 1 | m4 | m5 | m7 | m6
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | x’y’z’ | x’y’z | x’yz | x’yz’
x | 1 | xy’z’ | xy’z | xyz | xyz’
 |  |  | z |  | 

## Slide 12: THE MAP METHOD
  m0 and m2 (m4 and m6) are adjacent
  m0+ m2 = x'y'z' + x'yz' = x'z' (y'+y) = x'z'
  m4+ m6 = xy'z' + xyz' = xz' (y'+y) = xz'
y X |  |  | y |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
x | 1 | m4 | m5 | m7 | m6
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | x’y’z’ | x’y’z | x’yz | x’yz’
x | 1 | xy’z’ | xy’z | xyz | xyz’
 |  |  | z |  | 

## Slide 13: THE MAP METHOD
Example 3.1: Simplify the Boolean function F(x, y, z) = S(2, 3, 4, 5)
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  |  | 1 | 1
x | 1 | m4 | m5 | m7 | m6
 |  | 1 | 1 |  | 
 |  |  | z |  | 
F = x’y
+ xy’

## Slide 14: THE MAP METHOD
Example 3.2: Simplify the Boolean function F(x, y, z) = S(3, 4, 6, 7)
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  |  | 1 | 
x | 1 | m4 | m5 | m7 | m6
 |  | 1 |  | 1 | 1
 |  |  | z |  | 
F = yz
+ xz’

## Slide 15: THE MAP METHOD
Consider four adjacent squares in the three-variable map.
Any such combination represents the logical sum of four minterms and results in an expression of only one literal.
The number of adjacent squares that may be combined
  power of two
  1,2,4 and 8.
Larger number of adjacent squares
  Product term with fewer literal

## Slide 16: THE MAP METHOD
m0+m2+m4+m6 = x‘ y‘ z‘ + x‘ y z‘ + x y‘ z‘ + x y z'
= x'z'(y'+y) +xz'(y'+y) = x‘ z' + x z‘ = z'
m1+m3+m5+m7 = x‘ y‘ z + x‘ y z + x y‘ z + x y z
=x‘ z (y‘ + y) + x z (y‘ + y) = x‘ z + x z = z
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | x’y’z’ | x’y’z | x’yz | x’yz’
x | 1 | m4 | m5 | m7 | m6
 |  | xy’z’ | xy’z | xyz | xyz’
 |  |  | z |  | 

## Slide 17: THE MAP METHOD
1 square represents 1 minterm
  A Term of 3 literals.
2 adjacent squares
  A term of 2 literals.
4 adjacent squares
  A term of 1 literal.
8 adjacent squares
  Entire map
  Function F = 1

## Slide 18: THE MAP METHOD
Example 3.2: Simplify the Boolean function F(x, y, z) = S(0, 2, 4, 5, 6)
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 1 |  |  | 1
x | 1 | m4 | m5 | m7 | m6
 |  | 1 | 1 |  | 1
 |  |  | z |  | 
F = z’
+ xy’

## Slide 19: THE MAP METHOD
If a funtion is not expressed in sum of minterms
  Use the map to obtain the minterms
  Simplify the function and find the minimum number of terms.
  Make sure that the algebraic expression is in sum of products form.

## Slide 20: THE MAP METHOD
Example 3.2: Simplify the Boolean function F = A’ C + A’ B + A B’ C + B C.
  Express it in sum of minterms
  And find the minimal sum of products expression.
BC A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  | 1 | 1 | 1
A | 1 | m4 | m5 | m7 | m6
 |  |  | 1 | 1 | 
 |  |  | C |  | 
F = C
+ A’B

## Slide 21: 3.2 Four – Variable K-Map

## Slide 22: FOUR-VARIABLE MAP
16 minterms
Combinations of 2, 4, 8, and 16 adjacent squares
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
00 |  | m0 | m1 | m3 | m2 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | x
 | 11 | m12 | m13 | m15 | m14 |  | 
w |  |  |  |  |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  |  | z |  |  |  | 
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | w’x’y’z’ | w’x’y’z | w’x’yz | w’x’yz’ |  | 
 | 01 | m4 | m5 | m7 | m6 |  | x
 |  | w’xy’z’ | w’xy’z | w’xyz | w’xyz’ |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
w |  | wxy’z’ | wxy’z | wxyz | wxyz’ |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | wx’y’z’ | wx’y’z | wx’yz | wxyz’ |  | 
 |  |  | z |  |  |  | 

## Slide 23: FOUR-VARIABLE MAP
Minimization of four-variable Boolean function is similar to three-variable functions.
Adjacent squares are defined to be squares next to each other.
  Ex: m0 and m2, m3 and m11.
1 square represents 1 minterm
  A Term of 4 literals.
2 adjacent squares
  A term of 3 literals.
4 adjacent squares
  A term of 2 literal.
8 adjacent squares
  A term of 1 literal.
16 adjacent squares
  Entire map
  Function F = 1

## Slide 24: FOUR-VARIABLE MAP
Example 3.5: simplify F(w, x, y, z) = S(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | 1 | 1 |  | 1 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | x
 |  | 1 | 1 |  | 1 |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
w |  | 1 | 1 |  |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 1 | 1 |  |  |  | 
 |  |  | z |  |  |  | 
F = y’
+ w’z’
+ xz’

## Slide 25: FOUR-VARIABLE MAP
Example 3-6: simplify F = A B C + B C D + A B C D + A B C
CD AB |  |  |  | C |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 1 | m1 1 | m3 | m2 1 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | B
 |  |  |  |  | 1 |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
A |  |  |  |  |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 1 | 1 |  | 1 |  | 
 |  |  | D |  |  |  | 
F = B’ C’
+ A’CD’
+ B’D’

## Slide 26: FOUR-VARIABLE MAP
Prime implicant is a product term obtained by combining the maximum possible number of adjacent squares in the map.
If a minterm in a square is covered by only one prime implicant, that prime implicant is said to be essential.

## Slide 27: FOUR-VARIABLE MAP
Simplify F (A, B, C, D) =
CD AB |  |  |  | C |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | 1 |  | 1 | 1 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | B
 |  |  | 1 | 1 |  |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
A |  |  | 1 | 1 |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 1 | 1 | 1 | 1 |  | 
 |  |  | D |  |  |  | 
Essential prime implicants BD
and B’D’
CD AB |  |  |  | D |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | 1 |  | 1 | 1 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | B
 |  |  | 1 | 1 |  |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
A |  |  | 1 | 1 |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 1 | 1 | 1 | 1 |  | 
 |  |  | D |  |  |  | 
Prime implicants CD,
B’C,
AD
and AB’

## Slide 28: FOUR-VARIABLE MAP
Essential prime implicants BD and B’D’.
Prime implicants CD, B’C, AD and AB’.
Logical sum of two essential prime implicants and any two prime implicants. There are four possible ways that the function can be expressed with four product terms of two literals each:
  F = BD + B’D’ + CD + AD
  = BD + B’D’ + CD + AB’
  = BD + B’D’ + B’C + AD
  = BD + B’D’ + B’C + AB’

## Slide 29: 3.3 Five – Variable K-Map

## Slide 30: FIVE-VARIABLE MAP
Maps for more than four variables becomes complicated.
A five-variable map needs 32 squares and a six-variable map needs 64 squares.
When the number of variables becomes large,
The number of squares becomes excessively large,
The geometry for combining adjacent squares becomes more involved.
  Five-variable map: two four-variable map (one on the top of the other).

## Slide 31: FIVE-VARIABLE MAP
 |  | A = 0 |  |  |  |  | 
DE BC |  |  |  | D |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | C
 | 11 | m12 | m13 | m15 | m14 |  | 
B |  |  |  |  |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  |  | E |  |  |  | 
 |  | A = 1 |  |  |  |  | 
DE BC |  |  |  | D |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m16 | m17 | m19 | m18 |  | 
 | 01 | m20 | m21 | m23 | M22 |  | C
 | 11 | m28 | m29 | m31 | m30 |  | 
B |  |  |  |  |  |  | 
 | 10 | m24 | m25 | m27 | m26 |  | 
 |  |  | E |  |  |  | 

## Slide 32: FIVE-VARIABLE MAP
Each four-variable map retains the previously defined adjacency when taken separately.
Each square in the A = 0 map is a adjacent to the corresponding square in the A = 1.
  Ex: m4 is adjacent to m20 and m15 to m31.
For six-variable map 4 x four-variable maps needed to obtain the required 64 squares.
Variables > 6 need to many squares and are impractical to use.

## Slide 33: FIVE-VARIABLE MAP
 | Number of Adjacent Squares | Number of Literals in a Term in an n-variable Map |  |  | 
K | 2k | n = 2 | n = 3 | n = 4 | n = 5
0 | 1 | 2 | 3 | 4 | 5
1 | 2 | 1 | 2 | 3 | 4
2 | 4 | 0 | 1 | 2 | 3
3 | 8 |  | 0 | 1 | 2
4 | 16 |  |  | 0 | 1
5 | 32 |  |  |  | 0
Table 3.1 shows the relationship between the number of adjacent squares and the number of literals in the term.

## Slide 34: FIVE-VARIABLE MAP
Example 3.7: simplify F = S(0, 2, 4, 6, 9, 13, 21, 23, 25, 29, 31)
 |  | A = 0 |  |  |  |  | 
DE BC |  |  |  | D |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | 1 |  |  | 1 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | C
 |  | 1 |  |  | 1 |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
B |  |  | 1 |  |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  |  | 1 |  |  |  | 
 |  |  | E |  |  |  | 
 |  | A = 1 |  |  |  |  | 
DE BC |  |  |  | D |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m16 | m17 | m19 | m18 |  | 
 | 01 | m20 | m21 | m23 | M22 |  | C
 |  |  | 1 | 1 |  |  | 
 | 11 | m28 | m29 | m31 | m30 |  | 
B |  |  | 1 | 1 |  |  | 
 | 10 | m24 | m25 | m27 | m26 |  | 
 |  |  | 1 |  |  |  | 
 |  |  | E |  |  |  | 
F = A’B’E’
+ BD’E
+ ACE

## Slide 35: FIVE-VARIABLE MAP

## Slide 36: 3.4 Product of Sums Simplification

## Slide 37: PRODUCT OF SUMS SIMPLIFICATION
The 1’s placed in the squares of the map represent the minterms of the function.
The minterms not included in the function denote the complement of the function.
Mark the empty squares by 0’s
Combine them into valid adjacent squares
Obtain simplified expression of the complement function F’.

## Slide 38: PRODUCT OF SUMS SIMPLIFICATION
Simplify the following function in (a) sum of product and (b) product of sums:F (A, B, C, D) =
CD AB |  |  |  | C |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | 1 | 1 | 0 | 1 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | B
 |  | 0 | 1 | 0 | 0 |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
A |  | 0 | 0 | 0 | 0 |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 1 | 1 | 0 | 1 |  | 
 |  |  | D |  |  |  | 
F = B’D’
+ B’C’
+ A’C’D
F’ = AB
+ CD
+ BD’
Apply DeMorgan’s theorem
(F’ = (AB + CD + BD’))’
F = (A’ + B’) (C’ + D’) (B’ + D)

## Slide 39: PRODUCT OF SUMS SIMPLIFICATION
F = B’D’ + B’C’ + A’C’D
Sum of Products
F = (A’ + B’) (C’ + D’) (B’ + D)
Products of Sum

## Slide 40: PRODUCT OF SUMS SIMPLIFICATION
Consider the function defined in Table 3.2.
Sum of minterms:
  F (x, y, z) =
Product of maxterms:
  F (x, y, z) =
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
BC A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 0 | 1 | 1 | 0
A | 1 | m4 | m5 | m7 | m6
 |  | 1 | 0 | 0 | 1
 |  |  | C |  | 

## Slide 41: PRODUCT OF SUMS SIMPLIFICATION
Sum of minterms:
  F (x, y, z) =
  Sum of products: x’z + xz’
Product of maxterms:
  F (x, y, z) =
  Product of sums: (x’+z’) (x+z)
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 0 | 1 | 1 | 0
x | 1 | m4 | m5 | m7 | m6
 |  | 1 | 0 | 0 | 1
 |  |  | z |  | 

## Slide 42: 3.5 Don’t Care Conditions

## Slide 43: DON’T CARE CONDITIONS
The value of a function is not specified for certain combinations of variables
  BCD; 1010-1111: don't care
These don’t care conditions can be used on a map to provide further simplification of the Boolean expression.
Don’t care minterm is a combination of variables whole logical value is not specified.

## Slide 44: DON’T CARE CONDITIONS
It cannot be marked with a 1 in the map
  It would require that the function always be a 1 for such combination.
It cannot be marked with a 0 in the map
  It would require that the function always be a 0 for such combination.
For don’t care conditions an X is used.
For adjacent squares in the map to simplify the function
  The don’t care minterms may be assumed to be either 0 or 1.

## Slide 45: DON’T CARE CONDITIONS
  Simplify the Boolean function F (w, x, y, z) =
  Don’t care conditions d(w, x, y, z) = .
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | X | 1 | 1 | X |  | 
 | 01 | m4 | m5 | m7 | m6 |  | x
 |  | 0 | X | 1 | 0 |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
w |  | 0 | 0 | 1 | 0 |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 0 | 0 | 1 | 0 |  | 
 |  |  | z |  |  |  | 
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | X | 1 | 1 | X |  | 
 | 01 | m4 | m5 | m7 | m6 |  | x
 |  | 0 | X | 1 | 0 |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
w |  | 0 | 0 | 1 | 0 |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 0 | 0 | 1 | 0 |  | 
 |  |  | z |  |  |  | 
F = yz
+ w’x’
F = yz
+ w’z

## Slide 46: DON’T CARE CONDITIONS
Don’t care minterms in the map are initially marked with X’s.
The choice between 0 and 1 is made depending on the way the incompletely specified function is simplified.
Once the choice is made,
  the simplified function obtained will consist of a sum of minterms
  including those minterms that were initially marked with X’s and
  have been chosen to be included with 1’s.
F(w, x, y, z) = yz + w’x’ =
F(w, x, y, z) = yz + w’z =

## Slide 47: 3.6 NAND and NOR Implementations

## Slide 48: NAND AND NOR IMPLEMENTATIONS
NAND Circuits:
The NAND gate is a universal gate.
  Can implement any digital system.
  Complement operation is obtained from one-input NAND gate.
  AND operation requires two NAND gates
  OR operation is achieved through NAND gate with additional inverters in each input

## Slide 49: NAND AND NOR IMPLEMENTATIONS
NAND Circuits:
Two graphic symbols for NAND gate

## Slide 50: NAND AND NOR IMPLEMENTATIONS
The implementation of Boolean functions with NAND gates
  Require that the function be in sum of products form.
  F = A.B + C.D
  F = A.B +C.D (b) F = ((A.B)’)’ + ((C.D)’)’ (c) F = ((A.B)’ (C.D)’)’
  = (A+B)’ + (C+D)’ = ((A+B) (C + D))’
  = A.B + C.D = A.B + C.D

## Slide 51: NAND AND NOR IMPLEMENTATIONS
Implement the following Boolean function F = (x ,y, z) = (1, 2, 3, 4, 5, 7).
  Simplify the function in sum of products using K-map.
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  | 1 | 1 | 1
x | 1 | m4 | m5 | m7 | m6
 |  | 1 | 1 | 1 | 
 |  |  | z |  | 
F = z
+ xy’
+ x’y

## Slide 52: NAND AND NOR IMPLEMENTATIONS
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  | 1 | 1 | 1
x | 1 | m4 | m5 | m7 | m6
 |  | 1 | 1 | 1 | 
 |  |  | z |  | 
F = z
+ xy’
+ x’y

## Slide 53: NAND AND NOR IMPLEMENTATIONS
The procedure
  Simplify in the form of sum of products;
  Draw a NAND gate for each product term;
    The inputs to each NAND gate are the literals of the term (the first level);
  A single NAND gate for the second sum term (the second level);
  A term with a single literal requires an inverter in the first level if the single literal is not complemented. Otherwise it can be connected directly.

## Slide 54: NAND AND NOR IMPLEMENTATIONS
General procedure for converting multilevel AND-OR diagram into all NAND diagram:
  Convert all AND gates to NAND gates with AND-invert graphic symbol.
  Convert all OR gates to NAND gates with invert-OR graphic symbol.
  Check all the bubbles in the diagram.
    For every bubble that is not compensated by another small circle along the same line,
    insert an inverter (one-input NAND gate) or
    complement the input literal

## Slide 55: NAND AND NOR IMPLEMENTATIONS
F = A (CD + B) + BC’

## Slide 56: NAND AND NOR IMPLEMENTATIONS
F = (AB’ + A’B) (C + D’)

## Slide 57: NAND AND NOR IMPLEMENTATIONS
NOR function is the dual of NAND function.
The NOR gate is also universal.

## Slide 58: NAND AND NOR IMPLEMENTATIONS
NAND Circuits:
Two graphic symbols for NAND gate

## Slide 59: NAND AND NOR IMPLEMENTATIONS
Example: Implementing F = (A + B) (C + D) E
Example: Implementing F = (A B’ + A’ B) (C + D’)

## Slide 60: 3.7 Other Two Level Implementations

## Slide 61: OTHER TWO LEVEL IMPLEMENTATIONS
NAND and NOR gates most often found in integrated circuits.
NAND and NOR are the most important gates from a practical point of view.
Some NAND or NOR gates allow the possibility of a wire connection between the outputs of two gates to provide a specific logic function.
This type of logic is called wired logic.
Example:
  Open-collector TTL NAND gates when tied together performs wired-AND logic.

## Slide 62: OTHER TWO LEVEL IMPLEMENTATIONS
Example:
  Open-collector TTL NAND gates when tied together performs wired-AND logic.
  The wired – AND gate is not a physical gate, but only a symbol to designated the function obtained from the indicated wired connection.
  F = (AB)’ (CD)’ = (AB + CD)’

## Slide 63: OTHER TWO LEVEL IMPLEMENTATIONS
Nondegenerate Forms
Consider four types of gate: AND, OR, NAND and NOR.
Assign one type of gate for the first level and one type of gate for the second level.
There are 16 possible combination of two-level forms.
  Eight of them: degenerate forms = a single operation
    AND-AND, AND-NAND, OR-OR, OR-NOR, NAND-OR, NAND-NOR, NOR-AND, NOR-NAND.

## Slide 64: OTHER TWO LEVEL IMPLEMENTATIONS
degenerate forms = a single operation
Logic Operation | Circuit Diagram
AND-AND | 
AND-NAND | 

## Slide 65: OTHER TWO LEVEL IMPLEMENTATIONS
degenerate forms = a single operation
Logic Operation | Circuit Diagram
OR-OR | 
OR-NOR | 

## Slide 66: OTHER TWO LEVEL IMPLEMENTATIONS
degenerate forms = a single operation
Logic Operation | Circuit Diagram
NAND-OR | 
NAND-NOR | 

## Slide 67: OTHER TWO LEVEL IMPLEMENTATIONS
degenerate forms = a single operation
Logic Operation | Circuit Diagram
NOR-AND | 
NOR-NAND | 

## Slide 68: OTHER TWO LEVEL IMPLEMENTATIONS
  The eight non-degenerate forms
    AND-OR, OR-AND, NAND-NAND, NOR-NOR, NOR-OR, NAND-AND, OR-NAND, AND-NOR.
    AND-OR and NAND-NAND = sum of products.
    OR-AND and NOR-NOR = product of sums.
    NOR-OR, NAND-AND, OR-NAND, AND-NOR = ?

## Slide 69: OTHER TWO LEVEL IMPLEMENTATIONS
AND – OR – INVERT Implementation
The two forms NAND – AND = AND – NOR
Both perform the AND – OR – INVERT function.
F = (AB + CD + E)’
F’ = AB + CD + E (sum of product)

## Slide 70: OTHER TWO LEVEL IMPLEMENTATIONS
OR – AND – INVERT Implementation
The two forms OR – NAND = NOR – OR
Both perform the OR – AND – INVERT function.
F = [(A+B) (C+D) E]’
F’ = (A+B) (C+D) E (product of sum)

## Slide 71: OTHER TWO LEVEL IMPLEMENTATIONS
Equivalent Nondegenerate Form |  | Implements the Function | Simplify F’ in | To get an output of
(a) | (b)* |  |  | 
AND-NOR | NAND-AND | AND-OR-INVERT | Sum of products by combining 0’s in the map | F
OR-NAND | NOR-OR | OR-AND-INVERT | Product of sums by combining 1’s in the map and then complementing | F
*Form (b) requires and inverter for a single literal term.

## Slide 72: OTHER TWO LEVEL IMPLEMENTATIONS
Example 3-11: F' = x'y+xy'+z (F': sum of products)
  Step1: x’y (z + z’) = x’yz + x’yz’
  Step2: xy’(z + z’) = xy’z + xy’z’
  Step3: z (x + x’) = xz + x’z
  Step4: xz+x’z (y+y’) = xyz + x’yz + xy’z + x’y’z
  Step5: x’yz + x’yz’ + xy’z + xy’z’+ xyz + x’y’z
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 1 | 0 | 0 | 0
x | 1 | m4 | m5 | m7 | m6
 |  | 0 | 0 | 0 | 1
 |  |  | z |  | 
F’ = z
+ xy’
+ x’y

## Slide 73: OTHER TWO LEVEL IMPLEMENTATIONS
Example 3-11: F' = x'y+xy'+z (F': sum of products)
AND-OR-INVERT

## Slide 74: OTHER TWO LEVEL IMPLEMENTATIONS
AND-OR-INVERT form require a simplified expression of the complement of the function in product of sums.
  Combine the 1’s in the map
    F = x’y’z’ + xyz’
  Take the complement
    F’ = (x+y+z) (x’+y’+z)
    F = [(x+y+z) (x’+y’+z)]’
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 1 | 0 | 0 | 0
x | 1 | m4 | m5 | m7 | m6
 |  | 0 | 0 | 0 | 1
 |  |  | z |  | 

## Slide 75: OTHER TWO LEVEL IMPLEMENTATIONS
Summary
  F' = x'y+xy'+z (F': sum of products)
  F = (x'y+xy'+z)' (F: AOI implementation)
  F = x'y'z' + xyz' (F: sum of products)
  F' = (x+y+z)(x'+y'+z) (F': product of sums)
  F = ((x+y+z)(x'+y'+z))' (F: OAI)

## Slide 76: 3.8 Exclusive-OR Function

## Slide 77: EXCLUSIVE-OR FUNCTION
Exclusive-OR (XOR)
  x Å y = x y‘ + x‘ y
  F = 1, if only x = 1 or y = 1, but not when x and y = 1.
Exclusive-NOR (XNOR) (equivalence)
  (x Å y)' = x y + x‘ y‘
  F = 1, if both x and y = 1 or both = 0.
  (x Å y)’ = (x y’ + x’ y)’ = (x’ + y) (x + y’) = x’x + x’y’ + xy = xy + x’y’

## Slide 78: EXCLUSIVE-OR FUNCTION
Some identities
  x Å 0 = x
  x Å 1 = x'
  x Å x = 0
  x Å x' = 1
  x Å y' = (x Å y)'
  x‘ Å y = x’ Å y = (x Å y)'
Commutative and associative
  A Å B = B Å A
  (A Å B) Å C = A Å (B Å C)
  = A Å B Å C

## Slide 79: EXCLUSIVE-OR FUNCTION
Implementations
  (x‘ + y') x + (x‘ + y') y
  = x y‘ + x‘ y = x Å y

## Slide 80: EXCLUSIVE-OR FUNCTION
The XOR operation with three or more variables can be converted into an ordinary Boolean function by replacing Å symbol with its equivalent Boolean expression.
  AÅBÅC = (AB'+A'B)C' + (AB+A'B')C
  = AB'C'+A'BC'+ABC+A'B'C
  = S(1, 2, 4, 7)
  XOR is a odd function → an odd number of 1's, then F = 1.
  XNOR is a even function → an even number of 1's, then F = 1.

## Slide 81: EXCLUSIVE-OR FUNCTION
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  | 1 |  | 1
x | 1 | m4 | m5 | m7 | m6
 |  | 1 |  | 1 | 
 |  |  | z |  | 
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 1 |  | 1 | 
x | 1 | m4 | m5 | m7 | m6
 |  |  | 1 |  | 1
 |  |  | z |  | 
Odd Function
F = A Å B Å C
(b) Even Function
F = (A Å B Å C)’

## Slide 82: EXCLUSIVE-OR FUNCTION
Four-variable Exclusive-OR function
  AÅBÅCÅD = (AB'+A'B)Å(CD'+C'D) = (AB'+A'B)(CD+C'D')+(AB+A'B')(CD'+C'D)
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  |  | 1 |  | 1 |  | 
 | 01 | m4 | m5 | m7 | m6 |  | x
 |  | 1 |  | 1 |  |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
w |  |  | 1 |  | 1 |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  | 1 |  | 1 |  |  | 
 |  |  | z |  |  |  | 
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 | m0 | m1 | m3 | m2 |  | 
 |  | 1 |  | 1 |  |  | 
 | 01 | m4 | m5 | m7 | m6 |  | x
 |  |  | 1 |  |  |  | 
 | 11 | m12 | m13 | m15 | m14 |  | 
w |  | 1 |  | 1 |  |  | 
 | 10 | m8 | m9 | m11 | m10 |  | 
 |  |  | 1 |  | 1 |  | 
 |  |  | z |  |  |  | 
F = AÅBÅCÅD
F = (AÅBÅCÅD)’

## Slide 83: EXCLUSIVE-OR FUNCTION
Parity Generation and Checking
  A parity bit: P = x Å y Å z
  Parity check: C = x Å y Å z Å P
    C=1: one bit error or an odd number of data bit error
    C=0: correct or an even # of data bit error

## Slide 84: EXCLUSIVE-OR FUNCTION
Three-Bit Message |  |  | Parity Bit
x | y | Z | P
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 85: EXCLUSIVE-OR FUNCTION
Three-Bit Message |  |  |  | Parity Error Check
x | y | Z | P | C
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 86: 3.9 Hardware Description Language

## Slide 87: HARDWARE DESCRIPTION LANGUAGE
Describe the design of digital systems in a textual form
  Hardware structure
  Function/behavior
  Timing
VHDL and Verilog HDL

## Slide 88: HARDWARE DESCRIPTION LANGUAGE
Specification
RTL design and Simulation
Gate Level Simulation
ASIC Layout
FPGA Implementation
Logic Synthesis

## Slide 89: HARDWARE DESCRIPTION LANGUAGE
Documentation language
HDL is used to represent and document digital systems in a form that can be read by both humans and computers
Examples of keywords:
  module, end-module, input, output, wire, and, or, and not

## Slide 90: HARDWARE DESCRIPTION LANGUAGE
//Description of Simple circuit | 
module smpl_circuit (A, B, C, x, y); | 
 | input A, B, C;
 | output x, y;
 | wire w1;
 | and g1 (e, A, B);
 | not g2 (y, C);
 | or g3 (x, e, y);
endmodule | 

## Slide 91: HARDWARE DESCRIPTION LANGUAGE
Boolean expressions are specified in Verilog HDL with a
  continuous assignment statement consisting of the keyword assign followed by a Boolean expression.
To distinguish the arithmetic plus from logical OR, Verilog HDL uses the symbols
  (&) for AND,
  (|) for OR,
  (~) for NOT

## Slide 92: HARDWARE DESCRIPTION LANGUAGE
Boolean expression:
  x = A.B + C’
  y = C’
//Description of Simple circuit | 
module smpl_circuit (A, B, C, x, y); | 
 | input A, B, C;
 | output x, y;
 | assign x = (A & B) ¦ ~C
 | assing y = ~C
endmodule |