## Slide 1: INTRODUCTION TO LOGIC DESIGN Chapter 4 Combinational Logic
gürtaçyemişçioğlu

## Slide 2: OUTLINE OF CHAPTER 4
Combinational
Circuits
Analysis
Procedure
Binary Adder
Subtractor
Decimal
Adder
Binary
Multiplier
Magnitude
Comparator
Decoders
Encoders
Multiplexers
Design
Procedure

## Slide 3: 4.1 Combinational circuits

## Slide 4: COMBINATIONAL CIRCUITS
Logic circuits for digital systems
  Combinational
  Sequential
A combinational circuit
  outputs at any time are determined from the present combination of inputs.
  Performs operation specified by a set of Boolean functions.

## Slide 5: COMBINATIONAL CIRCUITS
Sequential circuits
  Employ storage elements in addition to logic gates.
  Their outputs are a function of inputs and state of the storage elements.
  Not only present values of inputs, but also on past inputs.
  Circuit behaviour must be specified by a time sequence of inputs and internal states.

## Slide 6: COMBINATIONAL CIRCUITS
Combinational circuit consist of
  Input variables
  Logic gates
    Accept signals from the inputs
    Generate signals to the output
  Output variables

## Slide 7: COMBINATIONAL CIRCUITS
For n input variable, there are 2n possible binary input combinations.
For each possible input combination there is one possible input output value.
Combinational
Circuit
n inputs
m outputs

## Slide 8: COMBINATIONAL CIRCUITS
Analysis
  Given a circuit, find out its function
  Function may be expressed as:
    Boolean function
    Truth table
Design
  Given a desired function, determine its circuit
  Function may be expressed as:
    Boolean function
    Truth table
?
?
?

## Slide 9: 4.2 Analysis procedure

## Slide 10: ANALYSIS PROCEDURE
To obtain the output Boolean functions from a logic diagram:
  Label all gate outputs that are function of input variables
    Determine the Boolean functions for each gate output
  Label the gates that are a function of input variables and previously labelled gates.
    Find the Boolean function for these gates.
  Repeat the process outlined in step2 until the outputs are obtained.
  Obtain the output Boolean functions in terms of input variables.

## Slide 11: ANALYSIS PROCEDURE
Boolean expression approach
A.B.C
A+B+C
A.B
B.C
A.C
A.B+A.C+B.C
(A.B+A.C+B.C)'
(A.B+A.C+B.C)‘.A+B+C
(A.B+A.C+B.C)‘.A+B+C+A.B.C

## Slide 12: ANALYSIS PROCEDURE
Boolean expression approach
T1 = A+B+C
T2 = A.B.C
F2 = A.B+A.C+B.C
F2’ = (A’+B’)(A’+C’)(B’+C’) = (A’ + B’C’).(B’+C’) post4b
T3 = F2’ . T1
T3 = (A’+B’C’).(B’+C’).(A+B+C)
T3 = (A’+B’C’).(AB’+B’C+AC’+BC’)
T3 = (A’.A.B’+A’.B’.C+A’.A.C’+A’.B.C’+
A.B’.B’.C’+B’.B’.C’.C+A.B’.C’.C’+B’.B.C’.C’)
T3 =A’.B’.C + A’.B.C’ + A.B’.C’ + A.B’.C’
T3 = A’.B’.C + A’.B.C’ + A.B’C’
F1= T3+T2
F1 = A’.B’.C + A’.B.C’ + A.B’C’ + A.B.C
T2
T1
F2
F2’
T3

## Slide 13: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
A = 0
B = 0
C = 0
A = 0
B = 0
C = 0
A = 0
B = 0
A = 0
C = 0
B = 0
C = 0
0
0
0
0
0
0
1
0
0
0 0

## Slide 14: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
A = 0
B = 0
C = 1
A = 0
B = 0
C = 1
A = 0
B = 0
A = 0
C = 1
B = 0
C = 1
0
1
0
0
0
0
1
1
1
0 0
1 0

## Slide 15: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
A = 0
B = 1
C = 0
A = 0
B = 1
C = 0
A = 0
B = 1
A = 0
C = 0
B = 1
C = 0
0
1
0
0
0
0
1
1
1
0 0
1 0
1 0

## Slide 16: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
0 1 0 |  | 
A = 0
B = 1
C = 1
A = 0
B = 1
C = 1
A = 0
B = 1
A = 0
C = 1
B = 1
C = 1
0
1
0
0
1
1
0
0
0
0 0
1 0
1 0
0 1

## Slide 17: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
0 1 1 |  | 
1 0 0 |  | 
A = 1
B = 0
C = 0
A = 1
B = 0
C = 0
A = 1
B = 0
A = 1
C = 0
B = 0
C = 0
0
1
0
0
0
0
1
1
1
0 0
1 0
1 0
0 1
1 0

## Slide 18: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
0 1 1 |  | 
1 0 0 |  | 
1 0 1 |  | 
A = 1
B = 0
C = 1
A = 1
B = 0
C = 1
A = 1
B = 0
A = 1
C = 1
B = 0
C = 1
0
1
0
1
0
1
0
0
0
0 0
1 0
1 0
0 1
1 0
0 1

## Slide 19: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
0 1 1 |  | 
1 0 0 |  | 
1 0 1 |  | 
1 1 0 |  | 
A = 1
B = 1
C = 0
A = 1
B = 1
C = 0
A = 1
B = 1
A = 1
C = 0
B = 1
C = 0
0
1
1
0
0
1
0
0
0
0 0
1 0
1 0
0 1
1 0
0 1
0 1

## Slide 20: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
0 1 1 |  | 
1 0 0 |  | 
1 0 1 |  | 
1 1 0 |  | 
1 1 1 |  | 
A = 1
B = 1
C = 1
A = 1
B = 1
C = 1
A = 1
B = 1
A = 1
C = 1
B = 1
C = 1
1
1
1
1
1
1
0
0
1
0 0
1 0
1 0
0 1
1 0
0 1
0 1
1 1

## Slide 21: ANALYSIS PROCEDURE
Truth table approach
A B C | F1 | F2
0 0 0 |  | 
0 0 1 |  | 
0 1 0 |  | 
0 1 1 |  | 
1 0 0 |  | 
1 0 1 |  | 
1 1 0 |  | 
1 1 1 |  | 
0 0
1 0
1 0
0 1
1 0
0 1
0 1
1 1
BC A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 0 | 1 | 0 | 1
A | 1 | m4 | m5 | m7 | m6
 |  | 1 | 0 | 1 | 0
 |  |  | C |  | 
BC A |  |  |  | B | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 0 | 0 | 1 | 0
A | 1 | m4 | m5 | m7 | m6
 |  | 0 | 1 | 1 | 1
 |  |  | C |  | 
F1 = A’B’C
+ A’BC’
+ AB’C’
+ ABC
F2 = BC
+ AC
+ AB

## Slide 22: 4.3 design Procedure

## Slide 23: DESIGN PROCEDURE
For a given a problem statement:
  Determine the number of inputs and outputs
  Derive the truth table
  Simplify the Boolean expression for each output
  Produce the required circuit

## Slide 24: DESIGN PROCEDURE
A truth table for a combinational circuit consist of:
  Input columns
    Obtained from 2n binary numbers for the n input variables.
  Output columns
    Determined from the stated specifications.
    Output functions specified in the truth table give exact definition of the combinational circuit.

## Slide 25: DESIGN PROCEDURE
The output binary functions listed in the truth table are simplified by any method:
  Algebraic manipulation
  The map method
  Computer – based simplification program
There is a variety of simplified expressions from which to choose.

## Slide 26: DESIGN PROCEDURE
Practical design must consider such constraints:
  The number of gates
  Number of inputs to a gate
  Propagation time of the signal through the gates
  Number of interconnections
  Limitations of the driving capability of each gate
  Etc.

## Slide 27: DESIGN PROCEDURE
Code conversion example
Code converter is a circuit that makes the two systems compatible even though each uses a different binary code.
To convert from binary code A to binary code B;
Combinational
Circuit
Input:
supply the bit combination of elements specified by code A
Output: generate the corresponding bit combination of code B.

## Slide 28: DESIGN PROCEDURE
Example:
Design a circuit to convert a “BCD” code to “Excess 3” code.
Combinational
Circuit
BCD:
4 – bits
0 – 9 values
Excess 3:
4 – bits
Value +3

## Slide 29: DESIGN PROCEDURE
Each code uses 4-bits to represent a decimal digit.
  4 input variables
    A, B, C, D
  4 output variables
    w, x, y, z
  24 = 16 bit combinations but only 10 have meaning in BCD.
  Rest 6 bit combinations are don’t-care combinations.
Input BCD | Output Excess-3
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x

## Slide 30: DESIGN PROCEDURE
Input BCD | Output Excess-3
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
CD AB |  |  |  | C |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | B
 | 11 |  |  |  |  |  | 
A |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | D |  |  |  | 
1
X
1
1
1
1
X
X
X
X
X
w = A
+ BC
+ BD
w’s karnaugh map

## Slide 31: DESIGN PROCEDURE
Input BCD | Output Excess-3
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
CD AB |  |  |  | C |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | B
 | 11 |  |  |  |  |  | 
A |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | D |  |  |  | 
1
X
1
1
1
1
X
X
X
X
X
x = B’C
+ B’D
+ BC’D’
x’s karnaugh map

## Slide 32: DESIGN PROCEDURE
Input BCD | Output Excess-3
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
CD AB |  |  |  | C |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | B
 | 11 |  |  |  |  |  | 
A |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | D |  |  |  | 
1
X
1
1
1
1
X
X
X
X
X
y = CD
+ C’D’
y’s karnaugh map

## Slide 33: DESIGN PROCEDURE
Input BCD | Output Excess-3
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
CD AB |  |  |  | C |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | B
 | 11 |  |  |  |  |  | 
A |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | D |  |  |  | 
1
X
1
1
1
1
X
X
X
X
X
z = D’
z’s karnaugh map

## Slide 34: DESIGN PROCEDURE
w = A + BC + BD = A + B (C + D)
x = B’C + B’D + BC’D’ = B’ (C+D) + BC’D’
x = B’ (C + D) + B (C+D)’
y = CD + C’D’ = CD + (C + D)’
z = D’

## Slide 35: DESIGN PROCEDURE
7 segment decoder
a, b, c, d, e, f, g are the outputs.
Outputs are in segments.
Each segment is turned on based on the input number.
Ex:
If BCD 5 is entered, then segments (outputs) a, f, g, c, d should be turned on.
a
b
c
g
e
d
f

## Slide 36: DESIGN PROCEDURE
a
b
c
g
e
d
f
7 segment decoder
w
x
y
z
a
b
c
d
e
f
g

## Slide 37: DESIGN PROCEDURE
a
b
c
g
e
d
f
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
0
1
2
3
4
5
6
7
8
9

## Slide 38: DESIGN PROCEDURE
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | x
 | 11 |  |  |  |  |  | 
w |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | z |  |  |  | 
1
X
1
1
1
1
X
X
X
X
X
a = w
+ y
+ x z
a’s karnaugh map
1
1
1
+ x’ z’

## Slide 39: DESIGN PROCEDURE
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | x
 | 11 |  |  |  |  |  | 
w |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | z |  |  |  | 
1
X
1
1
1
1
X
X
X
X
X
b = w
+ w’x’
+ y z
b’s karnaugh map
1
1
1
+ y’ z’

## Slide 40: DESIGN PROCEDURE
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | x
 | 11 |  |  |  |  |  | 
w |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | z |  |  |  | 
1
X
1
1
1
1
X
X
X
X
X
c = w
+ xy
+ x’ z
c’s karnaugh map
1
1
1
+ x’ y’
1

## Slide 41: DESIGN PROCEDURE
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | x
 | 11 |  |  |  |  |  | 
w |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | z |  |  |  | 
1
X
1
1
1
X
X
X
X
X
d = w
+ yz’
+ w’x’ y
d’s karnaugh map
1
1
+ x y’z
1
+ x’z’

## Slide 42: DESIGN PROCEDURE
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | x
 | 11 |  |  |  |  |  | 
w |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | z |  |  |  | 
1
X
1
X
X
X
X
X
e = yz’
e’s karnaugh map
1
1
+ x’z’

## Slide 43: DESIGN PROCEDURE
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | x
 | 11 |  |  |  |  |  | 
w |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | z |  |  |  | 
1
X
1
1
X
X
X
X
X
f = w
+ xy’
+ x z’
f’s karnaugh map
1
1
+ y’z’
1

## Slide 44: DESIGN PROCEDURE
Input BCD | 7 - segment |  |  |  |  |  | 
w x y z | a | b | c | d | e | f | g
0 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 0 0 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 0 1 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 0 1 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 1 0 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 1 0 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 1 1 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 1 1 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 0 0 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 0 0 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 0 1 0 | X | X | X | X | X | X | X
1 0 1 1 | X | X | X | X | X | X | X
1 1 0 0 | X | X | X | X | X | X | X
1 1 0 1 | X | X | X | X | X | X | X
1 1 1 0 | X | X | X | X | X | X | X
1 1 1 1 | X | X | X | X | X | X | X
yz wx |  |  |  | y |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | x
 | 11 |  |  |  |  |  | 
w |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | z |  |  |  | 
1
X
1
1
X
X
X
X
X
g = w
+ xy’
+ x z’
g’s karnaugh map
1
1
+ x’y
1
1

## Slide 45: 4.4 binary adder - Subtractor

## Slide 46: BINARY ADDER - SUBTRACTOR
The most basic arithmetic operation is the addition of two binary digits.
Simple addition consists of 4 possible elementary operations:
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = 10
First 3 operations produce a sum of one digit.
In the 4th operation, the binary sum consists of two digits.

## Slide 47: BINARY ADDER - SUBTRACTOR
The higher significant bit is called a carry.
A combinational circuit that performs the addition of two bits is called a half adder.
One that performs the addition of three bits (two significant bits and a previous carry) is a full adder.
Two half adders can be employed to implement a full adder.

## Slide 48: BINARY ADDER - SUBTRACTOR
Half Adder
Adds 2 bits
  2 inputs
  2 outputs
Produces SUM and CARRY.
x | y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
HA
x
y
SUM (S)
CARRY (C)
S = x’y
+ xy’
C = xy

## Slide 49: BINARY ADDER - SUBTRACTOR
Half Adder
S = x’y + xy’
C = xy

## Slide 50: BINARY ADDER - SUBTRACTOR
Full Adder
Adds 3 bits
  3 inputs
  2 outputs
Produces SUM and CARRY.
x | y | z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
FA
x
y
SUM (S)
CARRY (C)
S = x’y’z
+ x’yz
C = x’yz
z
+ xy’z’
+ xyz
+ xy’z
+ xyz’
+ xyz

## Slide 51: BINARY ADDER - SUBTRACTOR
S = x’y’z + x’yz + xy’z’ + xyz
C = x’yz + xy’z + xyz’ + xyz
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  | 1 |  | 1
x | 1 | m4 | m5 | M7 | m6
 |  | 1 |  | 1 | 
 |  |  | z |  | 
yz x |  |  |  | y | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  |  |  | 1 | 
x | 1 | m4 | m5 | M7 | m6
 |  |  | 1 | 1 | 1
 |  |  | z |  | 
C = xy
+ xz
+ yz
S = x ⊕y ⊕ z

## Slide 52: BINARY ADDER - SUBTRACTOR
Full adder implementation:
S = x’y’z + x’yz + xy’z’ + xyz
S = x ⊕y ⊕ z
C = x’yz + xy’z + xyz’ + xyz
C = xy + xz + yz

## Slide 53: BINARY ADDER - SUBTRACTOR
Implementation of Full Adder with Two Half Adders and an OR gate

## Slide 54: BINARY ADDER - SUBTRACTOR
Binary Adder:
Digital circuit that produces the arithmetic sum of two binary numbers.
It can be constructed with full adders connected in cascade.
The output carry from each full adder connected to the input carry of the next full adder in the chain.
Binary Adder
x3x2x1x0 y3y2y1y0
S3S2S1S0
C0
Cy
c3 c2 c1 .
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0

## Slide 55: BINARY ADDER - SUBTRACTOR
Binary Adder: 4-bit Ripple Carry Adder
FA
x0
FA
FA
FA
y0
S0
C1
0
x1
x2
x3
y1
y2
y3
S1
S2
S3
C2
C3
C4
LSB
MSB

## Slide 56: BINARY ADDER - SUBTRACTOR
The S outputs generate the required sum bits.
An n-bit adder requires n full adders with each output carry connected to the input carry of the next higher-order full adder.
Example: A = 1011 and B = 0011.
Subscript i: | 3 | 2 | 1 | 0 | 
Input carry |  |  |  |  | Ci
Augend |  |  |  |  | Ai
Addend |  |  |  |  | Bi
Sum |  |  |  |  | Si
Output Carry |  |  |  |  | Ci+1
1
1
1
1
0
0
1
0
0
1
1
1
1
1
0
0
0
1
1
0

## Slide 57: BINARY ADDER - SUBTRACTOR
Binary Adder: 4-bit Ripple Carry Adder
FA
1
FA
FA
FA
1
0
1
0
1
0
1
1
0
0
1
1
1
1
0
0
LSB
MSB

## Slide 58: BINARY ADDER - SUBTRACTOR
Carry propagation
The addition of two binary numbers in parallel implies that all the bits of the augend and addend are available at the same time.
Signals must propagate through the gates before the correct output sum is available in the output terminals.
The total propagation time
  = propagation delay of a typical gate x the number of gate levels in the circuit.
Longest propagation delay time in an adder is the time it takes the carry to propagate through the full adders.

## Slide 59: BINARY ADDER - SUBTRACTOR
Carry propagation
Since each bit of the sum output depends on the value of the input carry, the value of Si in any given stage in the adder will in its steady state final value only after the input carry to that stage has been propagated.

## Slide 60: BINARY ADDER - SUBTRACTOR
Carry propagation
The number of gate levels for the carry propagation can be found from the circuit of the full adder.

## Slide 61: BINARY ADDER - SUBTRACTOR
Carry propagation
The signal from the input carry Ci to the output carry Ci+1, propagates through
  an AND gate and an OR gate,
  which constitute two gate levels.
If there are 4 full adders in the adder, the output carry C4 would have
  2 x 4 = 8 gate levels from C0 to C4.
For an n-bit adder, there are 2n gate levels for the carry to propagate from input to output.

## Slide 62: BINARY ADDER - SUBTRACTOR
The carry propagation time is a limiting factor on the speed with which two numbers are added.
Since all other arithmetic operations are implemented by successive additions, the time consumed during the addition process is very critical.
Reduce the carry propagation delay
  Employ faster gates
  Look-ahead carry (more complex mechanism, yet faster)

## Slide 63: BINARY ADDER - SUBTRACTOR
Consider
Two new variables:
  Pi = Ai ⊕ Bi
  Gi = Ai . Bi
Sum = Pi ⊕ Ci
Carry = Gi + Pi . Ci

## Slide 64: BINARY ADDER - SUBTRACTOR
Gi is called carry generate
  Produces a carry of 1 when both Ai and Bi are 1, regardless of the input carry.
Pi . Ci is called a carry propagate
  It is the term associated with the propagation of the carry from Ci to Ci + 1.

## Slide 65: BINARY ADDER - SUBTRACTOR
Boolean functions for the carry outputs of each stage:
  C0 = input carry
  C1 = G0 + P0 . C0
  C2 = G1 + P1. C1 = G1 + P1 (G0 + P0 . C0)
  = G1 + P1 . G0 + P1 . P0 . C0
  C3 = G2 + P2 . C2 = G2 + P2 (G1 + P1 . G0 + P1 . P0 . CO)
  = G2 + P2 . G1 + P2 . P1 . G0 + P2 . P1 . P0 . C0

## Slide 66: BINARY ADDER - SUBTRACTOR
Carry Lookahead Generator
C3 does not have to wait for C2 and C1 to propagate.
C3 is propagated at the same time as C1 and C2.

## Slide 67: BINARY ADDER - SUBTRACTOR
4-Bit Adder with Carry Lookahead Generator
Each sum output requires two XOR gates.
  First XOR gate generates the Pi
  AND gate generates the Gi variable.
  Carries are propagated through CLA and applied as an input to the second XOR gate.
  All output carries are generated after a delay though two levels of gates. S1 through S3 have equal propagating delay times.

## Slide 68: BINARY ADDER - SUBTRACTOR
Binary Subtactor
The subtraction of unsigned binary numbers can be done most conveniently by means of complements.
A – B can be performed by taking 2’s complement of B and adding it to A.
2’s complement can be done by taking 1’s complement and adding 1.
1’s complement can be implemented with inverters.

## Slide 69: BINARY ADDER - SUBTRACTOR
Binary Subtactor
Circuit of subtractor consist of:
  An adder
  Inverters
The input carry C0 = 1 when performing subtraction
The operation performed becomes:
  A + 1’s complement of B + 1 = A + 2’s complement of B.
  A – B = A + (-B) = A +B’ + 1.
For unsigned numbers,
  A – B if A ≥ B or 2’s complement of (B – A) if A < B.

## Slide 70: BINARY ADDER - SUBTRACTOR
XOR gate combines addition and subtraction into one circuit with common binary adder.
Mode input M controls the operation.
  M = 0 = Addition.
  M = 1 = Subtraction.

## Slide 71: BINARY ADDER - SUBTRACTOR
When M = 0 (Addition).
  B ⊕ 0 = B.
  Full adders receive the value of B
  C0 = 0.
  Circuit performs A + B.
When M = 1 (Subtraction).
  B ⊕ 1 = B’.
  C0 = 1.
  Circuit performs A + B’ + 1
XOR with output V is for detecting an overflow.

## Slide 72: BINARY ADDER - SUBTRACTOR
Overflow
There is a need for an overflow detection.
The detection of an overflow after addition of two binary numbers depends on whether the number is to be:
  Signed
  Unsigned
 | 1 | n=1 | 1-bit register
+ | 1 | n=1 | 1-bit register
1 | 0 | n=2 | 2-bit register

## Slide 73: BINARY ADDER - SUBTRACTOR
Overflow
Signed
  Left most bit represents the sign bit.
  Negative numbers are in 2’s complement format.
  Sign bit treated as part of the number and the end carry does not indicate an overflow.

## Slide 74: BINARY ADDER - SUBTRACTOR
Overflow
Unsigned
  When added, overflow is detected from the end carry out of the most significant position.
Overflow cannot occur if positive and negative numbers are added.
Overflow occurs if both numbers are positive or negative.

## Slide 75: BINARY ADDER - SUBTRACTOR
Overflow
Ex: +70 , +80 in 8-bit registers.
8-bit register = 27 = 256.
  (-128) to (+127)
 |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 
 | +70 |  | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
+ | +80 |  | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
 | +150 |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0

## Slide 76: BINARY ADDER - SUBTRACTOR
Overflow
8-bit result that should have been positive has a negative sign bit and vice versa.
If carry out of sign bit is taken as the sign bit of the result then the 8-bit answer will be correct.
Since it can not be accommodated within 8-bit register, then there is a overflow.
 |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 
 | +70 |  | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
+ | +80 |  | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
 | +150 |  | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0

## Slide 77: BINARY ADDER - SUBTRACTOR
Overflow can be detected by:
  Observing the carry into the sign bit.
  Observing the carry out of the sign bit.
    If they are not equal, an overflow has occurred.
If two carries are applied to an XOR gate overflow is detected.
    When the output is 1.
  2’s complement must be computed for this method to work correctly.
    This take care of the condition when the maximum negative numbers is complemented.

## Slide 78: BINARY ADDER - SUBTRACTOR
If two binary numbers are unsigned
  the C bit detects
    a carry after addition or
    a borrow after subtraction.
If the numbers are signed, then the V bit detects an overflow.
  If V = 0, then no overflow.
    The n-bit result is correct.
  If V = 1, then result contains n+1 bits only the right most n-bits of the number.
  Overflow has occurred. The (n+1)th bit is the actual sign and has been shifted out of position.

## Slide 79: 4.5 decimal Adder

## Slide 80: DECIMAL ADDER
BCD Adder
Consider the arithmetic addition of two decimal digits in BCD and an input carry.
In BCD each input digit does not exceed 9
Output sum cannot be greater than 9 + 9 + 1 = 19.
  1 is an input carry.

## Slide 81: DECIMAL ADDER
Suppose:
  Two BCD digits applied to a 4-bit binary adder.
  The output produces a result that ranges from 0 through 19.
c3 c2 c1 .
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0

## Slide 82: DECIMAL ADDER
X +Y | x3 x2 x1 x0 | y3 y2 y1 y0 | Sum | Cy | S3 S2 S1 S0
0 + 0 | 0 0 0 0 | 0 0 0 0 | = 0 | 0 | 0 0 0 0
0 + 1 | 0 0 0 0 | 0 0 0 1 | = 1 | 0 | 0 0 0 1
0 + 2 | 0 0 0 0 | 0 0 1 0 | = 2 | 0 | 0 0 1 0
0 + 9 | 0 0 0 0 | 1 0 0 1 | = 9 | 0 | 1 0 0 1
1 + 0 | 0 0 0 1 | 0 0 0 0 | = 1 | 0 | 0 0 0 1
1 + 1 | 0 0 0 1 | 0 0 0 1 | = 2 | 0 | 0 0 1 0
1 + 8 | 0 0 0 1 | 1 0 0 0 | = 9 | 0 | 1 0 0 1
1 + 9 | 0 0 0 1 | 1 0 0 1 | = A | 0 | 1 0 1 0
2 + 0 | 0 0 1 0 | 0 0 0 0 | = 2 | 0 | 0 0 1 0
9 + 9 | 1 0 0 1 | 1 0 0 1 | = 12 | 1 | 0 0 1 0
Invalid Code
Wrong BCD Value
0001 1000

## Slide 83: DECIMAL ADDER
X +Y | x3 x2 x1 x0 | y3 y2 y1 y0 | Sum | Cy | S3 S2 S1 S0 | Required BCD Output | Value
9 + 0 | 1 0 0 1 | 0 0 0 0 | = 9 | 0 | 1 0 0 1 | 0 0 0 0 1 0 0 1 | = 9
9 + 1 | 1 0 0 1 | 0 0 0 1 | = 10 | 0 | 1 0 1 0 | 0 0 0 1 0 0 0 0 | = 16
9 + 2 | 1 0 0 1 | 0 0 1 0 | = 11 | 0 | 1 0 1 1 | 0 0 0 1 0 0 0 1 | = 17
9 + 3 | 1 0 0 1 | 0 0 1 1 | = 12 | 0 | 1 1 0 0 | 0 0 0 1 0 0 1 0 | = 18
9 + 4 | 1 0 0 1 | 0 1 0 0 | = 13 | 0 | 1 1 0 1 | 0 0 0 1 0 0 1 1 | = 19
9 + 5 | 1 0 0 1 | 0 1 0 1 | = 14 | 0 | 1 1 1 0 | 0 0 0 1 0 1 0 0 | = 20
9 + 6 | 1 0 0 1 | 0 1 1 0 | = 15 | 0 | 1 1 1 1 | 0 0 0 1 0 1 0 1 | = 21
9 + 7 | 1 0 0 1 | 0 1 1 1 | = 16 | 1 | 0 0 0 0 | 0 0 0 1 0 1 1 0 | = 22
9 + 8 | 1 0 0 1 | 1 0 0 0 | = 17 | 1 | 0 0 0 1 | 0 0 0 1 0 1 1 1 | = 23
9 + 9 | 1 0 0 1 | 1 0 0 1 | = 18 | 1 | 0 0 1 0 | 0 0 0 1 1 0 0 0 | = 24
+ 6










## Slide 84: DECIMAL ADDER
The problem is to find a rule by which the binary sum is to be converted to the correct BCD digit representation of the number in the BCD sum.

## Slide 85: DECIMAL ADDER
Binary Sum |  |  |  |  | BCD Sum |  |  |  |  | Decimal
K | Z3 | Z2 | Z1 | Z0 | C | S3 | S2 | S1 | S0 | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 2
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 3
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 4
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 5
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 6
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 7
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 8
0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 9

## Slide 86: DECIMAL ADDER
Binary Sum |  |  |  |  | BCD Sum |  |  |  |  | Decimal
K | Z3 | Z2 | Z1 | Z0 | C | S3 | S2 | S1 | S0 | 
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 10
0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 11
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 12
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 13
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 14
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 15
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 16
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 17
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 18
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 19

## Slide 87: DECIMAL ADDER
In examining the contents of the table;
  When the binary SUM = 1001, the corresponding BCD number is identical.
  When the binary SUM >1001, the BCD number is invalid.
  The addition of 6 (0110) is required.
  Correction is needed when K = 1.
  Correction is needed from 1010 – 1111.
    Z3 = 1,
    Z2 and Z1 must = 1 to distinguish from 1000 and 1001

## Slide 88: DECIMAL ADDER
Z3 Z2 Z1 Z0 | Err
0 0 0 0 | 0
. | .
. | .
. | .
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 1
1 0 1 1 | 1
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
Z1Z0 Z3Z2 |  |  |  | Z1 |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | Z2
 | 11 |  |  |  |  |  | 
Z3 |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | Z0 |  |  |  | 
1
1
1
1
1
1
Err = Z3Z2
+ Z3Z1
Output Carry = K + Z3Z2+ Z3Z1

## Slide 89: DECIMAL ADDER
When Output carry = 0,
  Nothing is added.
When Output carry = 1,
  add 0110 to the binary sum.
  provide an output carry for the next stage.

## Slide 90: 4.6 binary multiplier

## Slide 91: BINARY MULTIPLIER
Consider; 2-bit number
B1
B0
A1
A0
A0B1
C0
C1
C2
C3
x
A0B0
A1B1
A1B0
+
Multiplicand
bits
Multiplier
bits
First partial product
(AND gate)
Second partial product
(AND gate)
Product

## Slide 92: BINARY MULTIPLIER
For more bits;
  A bit of multiplier is ANDed with each bit of multiplicand in as many levels as there are bits.
  The binary output of AND gate in each level is added with the partial product of previous level.
  For J multiplier bits and K multiplicand bits we need
    J x K AND gates.

## Slide 93: 4.7 magnitude Comparator

## Slide 94: MAGNITUDE COMPARATOR
Compare two numbers (A and B)
3 outputs <, =, >
  A > B, A = B, A<B
Consider compare 4-bit number to 4-bit number
  A = A3 A2 A1 A0
  B = B3 B2 B1 B0
Magnitude Comparator
A3A2A1A0 B3B2B1B0
A > B A = B A < B

## Slide 95: MAGNITUDE COMPARATOR
A = B if:
  A3 = B3 AND A2 = B2 AND A1 = B1 AND A0 = B0
Ai | Bi | xi (A = B)
1
1
1
1
0
0
0
0
1
1
0
0
xi = Ai’ . Bi’
+ Ai . Bi
x = x3 . x2 . x1 . x0 = (A = B)
x3 = A3’ . B3’ + A3 . B3
x2 = A2’ . B2’ + A2 . B2
x1 = A1’ . B1’ + A1 . B1
x0 = A0’ . B0’ + A0 . B0

## Slide 96: MAGNITUDE COMPARATOR
A > B if
  Ai = 1 and Bi = 0
Ai | Bi | yi (A > B)
1
1
1
1
0
0
0
0
0
0
0
1
yi = Ai . Bi’
y3 = A3 . B3’
y2 = x3 . A2 . B2’
y1 = x3 . x2 . A1 . B1’
y0 = x3 . x2 . x1 . A0 . B0’
y = y3 + y2 + y1 + x0 = (A > B)

## Slide 97: MAGNITUDE COMPARATOR
A < B if
  Ai = 0 and Bi = 1
Ai | Bi | zi (A < B)
1
1
1
1
0
0
0
0
0
0
1
0
zi = Ai’ . Bi
z3 = A3’ . B3
z2 = x3 . A2’ . B2
z1 = x3 . x2 . A1’ . B1
z0 = x3 . x2 . x1 . A0’ . B0
z = z3 + z2 + z1 + z0 = (A < B)

## Slide 98: MAGNITUDE COMPARATOR

## Slide 99: 4.8 decoders

## Slide 100: DECODERS
Discrete quantities of information are represented in digital systems by binary codes.
A binary code of n bits is capable of representing up to 2n distinct elements of coded information.
A decoder is a combinational circuit that converts binary information from n input lines to a maximum of 2n unique output lines.

## Slide 101: DECODERS
Example: 2-bit binary number
Binary Decoder
x1
x0
Only one lamp will turn on!
0
0
1
0
0
0
1
0
2
3
1
0
0
1
0
0
0
1
0
0
1
0
1
1
0
0
0
1

## Slide 102: DECODERS
2-to-4 Line Decoder
Binary Decoder
A
B
D3
D2
D1
D0
A | B | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
D3= A’B’
D2= A’B
D1= AB’
D0= AB

## Slide 103: DECODERS
3-to-8 Line Decoder (Binary to Octal Conversion)
x | y | z | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
y3= I1’I0’
y2= I1’I0
y1= I1I0’
y0= I1I0
Binary Decoder
x
y
z
D7
D6 D5
D4 D3
D2
D1
D0

## Slide 104: DECODERS
3-to-8 Line Decoder (Binary to Octal Conversion)
x | y | z | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
D0= x’ y’ z’
D1= x’ y’ z
D2= x’ y z’
D3= x’ y z
D4= x y’ z’
D5= x y’ z
D6= x y z’
D7= x y z

## Slide 105: DECODERS
3-to-8 Line Decoder (Binary to Octal Conversion)
D0= x’ y’ z’
D1= x’ y’ z
D2= x’ y z’
D3= x’ y z
D4= x y’ z’
D5= x y’ z
D6= x y z’
D7= x y z

## Slide 106: DECODERS
Some decoders are with NAND gates.
NAND becomes more economical to generate the decoder minterms in their complemented form.
Decoders include one or more ENABLE inputs to control the circuit operation.

## Slide 107: DECODERS
2-to-4 Line Decoder with ENABLE input
Binary Decoder
A
B
E
D3
D2
D1
D0
E | A | B | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 108: DECODERS
2-to-4 line decoder with ENABLE input can function as a demultiplexer.
A demultiplexer is a circuit that receives information from single line and directs it to one of 2n possible output lines.
The selection of a specific output is controlled by the bit combination of n selected lines.

## Slide 109: DECODERS
The decoder can function as 1-to-4 line demultiplexer.
  E is taken as a data input line.
  A and B are taken as the selection inputs.
E | A | B | D0 | D1 | D2 | D3
1/0 | 0 | 0 | E | 0 | 0 | 0
1/0 | 0 | 1 | 0 | E | 0 | 0
1/0 | 1 | 0 | 0 | 0 | E | 0
1/0 | 1 | 1 | 0 | 0 | 0 | E

## Slide 110: DECODERS
Decoders with enable inputs can be connected together to form a larger decoder circuit.
3-to-8 line decoders with enable inputs can be connected to form a 4-to-16 line decoder.

## Slide 111: DECODERS
When w = 0, top decoder enabled and other disabled.
The bottom decoder outputs all 0’s.
The top eight outputs generate minterms 0000 to 0111.
When w = 1, bottom decoder enabled and other disabled.

## Slide 112: DECODERS
Active – High / Active – Low
Binary Decoder
A
B
D3
D2
D1
D0
Binary Decoder
A
B
D3
D2
D1
D0
A | B | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
A | B | D0 | D1 | D2 | D3
0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0

## Slide 113: DECODERS
A decoder provides the 2n minterm of n input variables.
Since any Boolean function can be expressed in sum of minterms
  Use decoder to generate the mintersm
  An external OR gate to form the logical sum.
Any combinational circuit with n inputs and m outputs can be implemented with an n-to-2n- line decoder and m OR gates.

## Slide 114: DECODERS
Example: Full Adder
S(x, y, z) = ∑(1, 2, 4, 7)
C(x, y, z) = ∑(3, 5, 6, 7)
Binary Decoder
x
y
z
D7D6
D5D4D3D2 D1
D0
x
y
z
S C

## Slide 115: 4.9 encoders

## Slide 116: ENCODERS
An encoder is a digital circuit that performs the inverse operation of a decoder.
An encoder has 2n (or fewer) input lines and n output lines.
The output lines generate the binary code corresponding to the input value.

## Slide 117: ENCODERS
Example: 4-to-2 Binary Encoder
x4 x3 x2 x1 | y1 y0
0 0 0 1 | 0 0
0 0 1 0 | 0 1
0 1 0 0 | 1 0
1 0 0 0 | 1 1
1
2
3
Binary Encoder
Only one switch should be activated at a time
4
x1
x2
x3
x4
y1
y0

## Slide 118: ENCODERS
Example: Octal-to-Binary Encoder
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | Y2 Y1 Y0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 0 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 0 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 1 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 1 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 0 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 0 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 1 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 1 1
Y2= D7
+D6
+D5
+D4
Y1= D7
+D6
+D3
+D2
Y0= D7
+D5
+D3
+D1

## Slide 119: ENCODERS
Example: Octal-to-Binary Encoder
Y2= D7
+D6
+D5
+D4
Y1= D7
+D6
+D3
+D2
Y0= D7
+D5
+D3
+D1
Binary Encoder
Y2
Y1
Y0
D7
D6
D5
D4 D3
D2
D1
D0

## Slide 120: ENCODERS
4-Input Priority Encoder
Encoder circuit that includes the priority function.
If two or more inputs are equal 1 at the same time,
  The input having the highest priority will take precedence.
Priority Encoder
V
X
Y
D3
D2
D1
D0
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | X | Y | V
0 | 0 | 0 | 0 | x | x | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1

## Slide 121: ENCODERS
4-Input Priority Encoder
X’s in the output represent don’t care conditions.
X’s in the input are useful fir representing a truth table in condensed form.
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | X | Y | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1
Valid ouput = 1, when one or more inputs =1

## Slide 122: ENCODERS
4-Input Priority Encoder
X’s in the input are useful for representing a truth table in condensed form.
Truth table uses an X to represent either 1 or 0.
Example: X100 represents two minterms 0100 and 1100.
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | X | Y | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1

## Slide 123: ENCODERS
4-Input Priority Encoder
According to the table:
  Higher the subscript number,
  The higher the priority of the input.
  Input D3 has the highest priority.
  When D3 = 1, the xy is 111, regardless of the values of the other inputs.
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | X | Y | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1

## Slide 124: ENCODERS
4-Input Priority Encoder
When each X in a row is replaced first by 0 and then by 1
  We obtain all 16 possible input combinations.
001X = 0010 and 0011
01XX = 0100 and 0101 and 0110 and 0111
1XXXX = 1000 and 1001 and 1010 and 1011 and 1100 and 1101 and 1110 and 1111

## Slide 125: ENCODERS
4-Input Priority Encoder
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | X | Y | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1
D1D0 D3D2 |  |  |  | D1 |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | D2
 | 11 |  |  |  |  |  | 
D3 |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | D0 |  |  |  | 
X
X’s K-MAP
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
X = D2
+ D3

## Slide 126: ENCODERS
4-Input Priority Encoder
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | X | Y | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1
D1D0 D3D2 |  |  |  | D1 |  |  | 
 |  | 0 0 | 0 1 | 1 1 | 1 0 |  | 
 | 00 |  |  |  |  |  | 
 | 01 |  |  |  |  |  | D2
 | 11 |  |  |  |  |  | 
D3 |  |  |  |  |  |  | 
 | 10 |  |  |  |  |  | 
 |  |  | D0 |  |  |  | 
X
Y’s K-MAP
0
1
1
0
0
0
0
1
1
1
1
1
1
1
1
Y = D3
+ D1D2’

## Slide 127: ENCODERS
4-Input Priority Encoder
Inputs |  |  |  | Outputs |  | 
D3 | D2 | D1 | D0 | X | Y | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1
V = D0
+ D1
+ D2
+ D3

## Slide 128: ENCODERS
4-Input Priority Encoder
X = D2+ D3
Y = D3+ D1D2’
V = D0+ D1+ D2+ D3

## Slide 129: ENCODERS
X
Y
Z
D7
D6
D5
D4 D3
D2
D1
D0
X
Y
Z
D7
D6
D5
D4 D3
D2
D1
D0
Binary Encoder
Binary Decoder
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 130: 4.10 multiplexers

## Slide 131: MULTIPLEXERS
A multiplexer (MUX) is a combinational circuit that selects binary information from one of many input lines and directs it to a single output line.
The selection of a particular input line is controlled by a set of selection lines.
There are 2n input lines and n selected lines.
MUX
A
Q
B
C
D
S0
S1
0
0
0
1
1
0
1
1
Q = A
Q = B
Q = C
Q = D

## Slide 132: MULTIPLEXERS
Consider 2-to-1 MUX
MUX
A
Q
B
S0
0
1
Q = A
Q = B
S0 | A | B | Q
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
1
0
AB S0 |  |  |  | A | 
 |  | 0 0 | 0 1 | 1 1 | 1 0
 | 0 | m0 | m1 | m3 | m2
 |  | 0 | 0 | 1 | 1
S0 | 1 | m4 | m5 | m7 | m6
 |  | 0 | 1 | 1 | 0
 |  |  | B |  | 
Q = S0’ A
+ S0 B

## Slide 133: MULTIPLEXERS
Consider 2-to-1 MUX
MUX
A
Q
B
S0
0
1
0
Q = S0’ A
+ S0 B

## Slide 134: MULTIPLEXERS
4-to-1 Multiplexer
MUX
A
Q
B
C
D
S0
S1
0
0
0
1
1
0
1
1
Q = A
Q = B
Q = C
Q = D
S0 | S1 | Q
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 135: MULTIPLEXERS
4-to-1 Multiplexer
x3
x2
x1
x0
y3
y2
y1
y0
D0
I0
I1
S
MUX
D1
I0
I1
S
MUX
D2
I0
I1
S
MUX
D3
I0
I1
S
MUX
E
E
E
E

## Slide 136: MULTIPLEXERS
Example: F(x, y) = ∑ (0, 1, 3)
D
I0
I1
I2
I3
S1
x y | F
0 0 | 1
0 1 | 1
1 0 | 0
1 1 | 1
x y
F
1
1
0
1
MUX
S0

## Slide 137: MULTIPLEXERS
Boolean function implementation
  Decoder can be used to implement Boolean functions by employing external OR gates. (see slide 114- DECODERS).
  Multiplexer is essentially a decoder that includes the OR gate within the unit.
  The minterms of a function are generated in multiplexer by the circuit associated with the selection inputs.

## Slide 138: MULTIPLEXERS
Boolean function implementation
  This provides a method of implementing a Boolean function of n variables with a multiplexer that has n – 1 selection inputs.
  The first n – 1 variables of the function are connected to the selection inputs of the multiplexer.
  The remaining single variable of the function is used for the data inputs.

## Slide 139: MULTIPLEXERS
Example:F(x, y, z) = ∑(1, 2, 6, 7)
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
MUX
Y
I0
I1
I2
I3 I4
I5
I6
I7
S2 S1 S0
x y z
0
1
1
0
0
0
1
1
F
MUX
Y
I0
I1
I2
I3
S1 S0
x y z | F
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 0
1 0 1 | 0
1 1 0 | 1
1 1 1 | 1
x y
F
F = z
z
F = z
z
F = 0
0
F = 1
1

## Slide 140: MULTIPLEXERS
Example:F(x, y, z) = ∑(1, 2, 6, 7)
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
MUX
Y
I0
I1
I2
I3
S1 S0
x y
F
F = z
z
F = z’
z’
F = 0
0
F = 1
1

## Slide 141: MULTIPLEXERS
Example:F(A, B, C, D) = ∑(1,3,4,11,12,13,14,15)
F
MUX
Y
I0
I1
I2
I3 I4
I5
I6
I7
S2 S1 S0
A B C D | F
0 0 0 0 | 0
0 0 0 1 | 1
0 0 1 0 | 0
0 0 1 1 | 1
0 1 0 0 | 1
0 1 0 1 | 0
0 1 1 0 | 0
0 1 1 1 | 0
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 0
1 0 1 1 | 1
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
A B C
F
F = D
D
F = D
D
F = D’
D’
F = 0
0
F = 0
F = D
F = 1
F = 1
0
D
1
1

## Slide 142: MULTIPLEXERS
8-to-1 MUX using Dual 4-to-1 MUX
Y
S2 S1 S0
MUX
Y
I0
I1
I2
I3
S1 S0
0 0
1
MUX
Y
I0
I1
I2
I3
S1 S0
MUX
Y
I0
I1
S
I0
I1
I2
I3
I4
I5
I6
I7

## Slide 143: DEMULTIPLEXERS
DeMUX
I
Y3
Y2
Y1
Y0
S1 S0
S1 S0 | Y3 | Y2 | Y1 | Y0
0 0 | 0 | 0 | 0 | I
0 1 | 0 | 0 | I | 0
1 0 | 0 | I | 0 | 0
1 1 | I | 0 | 0 | 0

## Slide 144: DEMULTIPLEXER
DeMUX
I
Y3
Y2
Y1
Y0
S1 S0
S1 S0 | Y3 | Y2 | Y1 | Y0
0 0 | 0 | 0 | 0 | I
0 1 | 0 | 0 | I | 0
1 0 | 0 | I | 0 | 0
1 1 | I | 0 | 0 | 0
Binary Decoder
A
B
E
D3
D2
D1
D0
E | A | B | Y3 | Y2 | Y1 | Y0
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 145: MULTIPLEXERS
A multiplexer can be constructed with three – state gates.
A three – state gate is a digital circuit that exhibits three states.
Two of the states are signals equivalent to logic 1 and 0.
The third state is high – impedance state.
Hight – impedance state behaves like an open circuit.
  The output appears to be disconnected.
  The circuit has no logic significance.

## Slide 146: MULTIPLEXERS
Three – state gates may perform any conventional logic such as AND or NAND.
The most commonly used is the buffer gate.
The high – impedance state of a three – state gate provides a special feature not available in other gates.
Large number of three – state gate outputs can be connected with wires to form a common line without endangering loading effects.

## Slide 147: MULTIPLEXERS
Three state gates
  Tri-state buffer
  Tri-state inverter
A
Y
C
C A | Y
0 x | Hi-Z
1 0 | 0
1 1 | 1
A
Y
C

## Slide 148: MULTIPLEXERS
Three state gates
A
Y
C
B
D
C D | Y
0 0 | Hi-Z
0 1 | B
1 0 | A
1 1 | ?
Not Allowed
Y=
A
C
B
A if C = 1
B if C = 0
2-to-1 MUX

## Slide 149: MULTIPLEXERS
I0
Y
E
S1
I1
I2
I3
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
S0
4-to-1 MUX